Applying Non-stable Time Series Model to Forecast the Groundwater Dynamic Variation in the Well-Irrigated Rice Area in Sanjiang Plain

# Qiang Fu*, Zu Wei**

*School of Water Conservancy & Civil Engineering, Northeast Agriculture University, Harbin, Heilongjiang 150030, China, fuqiang100@371.net

**School of Agriculture, Northeast Agriculture University, Harbin, Heilongjiang 150030, China

Abstract: Recently, the situation of groundwater shortage is rather serious in Sanjiang Plain. More and more so called “funnels” and “hanging pump” phenomenon appears. The groundwater level descends continually. Therefore, the Chuang Ye Farm in Jian San Jiang Department has been taken as an example in this article, to build up the non-stable time series random model by means of applying the random analysis method. Through using this model, the article simulates the dynamic variation and forecast the varied trend in the future. This article refers to provide some references for the continually develop of agriculture and groundwater resources.

Key words: non-stable time series model; well irrigation rice; groundwater; Sanjiang Plain

1. Introduction

San Jiang Plain is an important base of food production in our country. In recent decades, the great progress has been made through developing well rice and adopting rice to control flood. The area of rice has achieved about 10 million acres by the end of 1998, and 80% of which is well-irrigated rice. Most farmers have been getting rich gradually. But the blindly abuse of enlarging rice area has led to the groundwater crisis. Because farmers have exploited the ground water largely and immoderately and the measurements of saving water were out of date, it leads to water resources waste for no reason and the groundwater crisis and appears the phenomenon of “hanging pump” and funnel. In the spring of 1996, the fact that more than 600 “hanging pump” can’t work normally has appeared only in Jian San Jiang administration bureau. The ground water resources crisis has constrained the future development in Sanjiang Plain. Therefore, researching the groundwater dynamic variety law is imperative under the situation in order to provide scientific reference for ascertaining the development scale of well rice in Sanjiang Plain reasonably. It is significant in theory and in practice (Fu, 2000).

2. Establishing the Random Model

The dynamic varies of the groundwater table resulted from the precipitation, man-made exploitation and random factors. Because of seasonal precipitation, the groundwater table varies periodically. Variation of the groundwater table has the trend of periodical descent because man-made exploitation is increasing year after year. The mathematics expression of the groundwater level dynamic change in the area of well irrigated rice is as follows (Li, 1999).

（1）

（2）

Where  is the groundwater level (),  is the varied trend item () arose by groundwater exploitation,  is periodical change item () arose by seasonal precipitation,  is the random item and  is surplus value of the groundwater level.

Thus, long-term observation sequences belong to non-stable time series. It is necessary to analyze the series’ components one by one.

2.1 The Varied Trend Item (Ding, 1988; Yang, 1996; Ding, 1998)

The varied trend of the groundwater level annual time series can be ascertained by the stepwise regression analysis method. Firstly, give a common polynomial function:

Then ascertain the mathematics expression of trend item through adopting stepwise regression method and selecting in computer, or append the trend line to original data directly in the software of Excel2000. If water level fits the one of the followed formulae, it just is the required trend variety item.

（1）

（2）

（3）

Where  and  are indefinite coefficients and  is time serial number.

In practice, the moving average method, orthogonal polynomial method and spline function may be also adopted to select trend item and gain the trend item equation. To analyze periodical item of the trend item is deducted from the original data.

2.2 Periodical Variation Item

The common methods of selecting periodical item  include variance analysis, correlation analysis, harmonic analysis and periodical figure analysis (Fu, 2000; Li, 1999; Ding, 1988; Ding, 1998).

Since the groundwater dynamic variation takes place yearly or monthly as period obviously, this paper adopts harmonic analysis method. The aim of harmonic analysis is to separate some simple harmonic waves with different amplitude and phase from the irregular curve of groundwater dynamic variation for researching its statistical law and character. Because Fourier series may fit the physical phenomena with periodicity and separate the periodical variation item and random item in the surplus value of groundwater level, the periodical variation item of groundwater level can be ascertained by Fourier series harmonic analysis. The formula of Fourier series is:

The frequency multiplication limit is  and the number of largest wave  equals to . Where take  when  is even number and  when  is odd number. Same as the regression analysis, regression variance of original series  can be proved. It is:

Thus, the total variance  of series  may be expressed by the summation of each harmonic variance and surplus variance. Therefore, the statistical measurement  can be carried out to inspect the significance of the th harmonic, that  and

followsdistribution with of freedom degree of . We may do significant test each harmonic one by one through using  inspection with the mentioned data. The periodical item of the series can express as the superposition of each significant harmonic. Consequently, ascertain the model of periodical item function is as following.

Where:  = number of significant harmonic.

Thus, there is only random item  when trend item  and periodical item  are deducted from the original series of groundwater .

2.3 Random Item (Ding, 1988; 1998; Du, 1991; Zheng, 1999)

If random component  is stable,  consists of stable dependent component  and stable independent random component  (pure random component), that is: .

For the stable random component , we may use linear stable random model to express its statistic character. Establish  model and its expression is:

where  is the average of the random series, and  is the independent random variable. The average of  is zero. The variance is .  are weight coefficients of auto regression, which is called auto regression coefficient commonly.  Because of the existing of some relations between the variance  of independent random variable and the variance  in the series , there are parameters (, and ) in common auto regression model. Where,  means the level of the series ,  means the variation degree of  around the mean value, and  depend degree of the series on time.

The  model is established as followed:

Step 1: to select the model’s type.

Through analyzing and treating the random series, the auto correlation figure can be drawn according to the followed formula. The formula is:

Where time delay k equals to 0,1,2,…m. When n is larger than 50 ()， m may be less than n/4 and m equals to n/10 usually. Draw the allowable range that confidence level of auto-correlation coefficient is 95% in the auto-correlation figure. If α equals to 0.05, allowable range of auto-correlation coefficient  is as:

If -step correlation coefficient is prominent to the independent sequence, the original random sequence is a mean square contingency sequence and the  model can be adopted.

Step 2: normal conversion (Ding, 1988; Zheng, 1999).

Do normal test for the random series . The mean value  and variance  of original random series are  and . The variation coefficient is  and skewness coefficient is . If the series is skewness distribution, it is necessary to doing normal conversion.

Step 3: identification of the model form (Ding, 1988; Ding, 1998; Du, 1991).

The identification of the model form is to ascertain the steps . The main method is to do statistical analysis for partial correlation coefficient. The coefficient  can be calculated by Yule-Walker equation estimation method through solving the followed matrix. It is as the following:

The allowable range of partial correlation coefficient is . When the value of  is in the allowable range, the value of  acts as the steps ().

Step 4: parameter estimation

Where  is gained during solving the partial correlation coefficient. Therefore, the  model can be ascertained.

Step 5: Farther identification of the model.

When the selected steps are , we may identify the random series by adopting AIC criterion in order to ensure the model has the fewest parameters. The criterion of AIC is .  should be calculated respectively. If  is the smallest of them, the  model is the best. Otherwise, select the smallest AIC value and compare them further.

Step 6: model inspection.

The main inspection is whether the residual error item  is independent or not.

`

Calculate  and auto correlation coefficients (). The calculation formula of statistical measurement is: . Therefore,  gradually follows  distribution with the freedom degree . If  is less than  （0.05）,  is independent each other. The normal test of the residual error  is the same as the former step.

The former steps are basic steps for establishing  model.

2.4 Establish Non-stable Time Series Model

Through surplus the former trend item , periodical item  and random item , the non-stable time series random model of the groundwater can be obtained as:

3. Modeling Example

3.1 Introduce Basic Conditions

Chuang Ye farm occupies the area of 533.3  in Jian San Jiang Administration Bureau, Sanjiang Plain. The main crop is rice and the areas of the farm had increased largely from 2000 acres in 1985 to 365000 acres in 2000. Annual groundwater exploitation had increased from 1.2 million  in 1985 to 164.25 million  in 2000. The investigation data in 1996 indicated that the exploitable groundwater was 49.26 million  in the farm and exploitation of the groundwater had reached to 75 million . The groundwater is exploited excessively. If it is necessary to satisfy the well rice areas increasing year after year, this need exploit the groundwater more extensively in the condition that irrigation norm varies very little. The groundwater exploitation in 2000 has reached to 164.25 million  and the phenomena of funnel and “hanging pump” have appeared largely. This has treated to the agriculture production and domestic water. Therefore, it is necessary to simulate the groundwater dynamic variation law and forecast developable trend according to the observation data of groundwater level from 1985 to 2000 in Chuang Ye farm in order to provide significant reference for the decision-makers.

Table 1. The Data Table of the Groundwater Depth in Sanjiang Plain (1985～2000)

|  | Jan. | Feb. | Mar. | Apr. | May. | Jun. | Jul. | Aug. | Sept. | Oct. | Nov. | Dec. | Mean |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1985 | 2.97 | 3.02 | 3.29 | 3.35 | 5.60 | 5.41 | 4.82 | 3.61 | 2.92 | 2.03 | 1.95 | 1.94 | 3.41 |
| 1986 | 3.01 | 3.18 | 3.45 | 3.51 | 5.82 | 5.58 | 4.95 | 3.95 | 3.01 | 2.21 | 2.13 | 2.13 | 3.58 |
| 1987 | 3.2 | 3.31 | 3.56 | 3.72 | 6.01 | 5.73 | 5.2 | 4.11 | 3.21 | 2.33 | 2.3 | 2.3 | 3.75 |
| 1988 | 3.4 | 3.42 | 3.8 | 3.88 | 6.21 | 5.88 | 5.41 | 4.31 | 3.35 | 2.48 | 2.4 | 2.41 | 3.91 |
| 1989 | 3.45 | 3.51 | 3.62 | 3.91 | 6.31 | 6.02 | 5.52 | 4.37 | 3.39 | 2.52 | 2.48 | 2.45 | 3.96 |
| 1990 | 3.84 | 3.84 | 3.95 | 4.23 | 6.59 | 6.41 | 5.83 | 4.76 | 3.61 | 2.61 | 2.60 | 2.55 | 4.24 |
| 1991 | 4.15 | 4.17 | 4.25 | 4.41 | 7.05 | 6.93 | 6.31 | 5.20 | 3.81 | 2.95 | 2.85 | 2.84 | 4.58 |
| 1992 | 4.25 | 4.30 | 4.33 | 4.43 | 7.23 | 7.00 | 6.65 | 5.48 | 3.90 | 3.61 | 3.50 | 3.47 | 4.85 |
| 1993 | 4.5 | 4.53 | 4.7 | 4.99 | 7.68 | 7.45 | 7.30 | 5.73 | 4.55 | 3.86 | 3.65 | 3.65 | 5.22 |
| 1994 | 4.75 | 4.78 | 4.81 | 4.91 | 7.97 | 7.81 | 7.80 | 6.14 | 4.79 | 4.01 | 3.90 | 3.90 | 5.46 |
| 1995 | 4.60 | 4.63 | 4.80 | 5.00 | 8.16 | 8.01 | 7.92 | 6.37 | 5.40 | 4.76 | 4.27 | 4.25 | 5.68 |
| 1996 | 4.60 | 4.65 | 4.83 | 5.00 | 8.47 | 8.00 | 7.90 | 6.47 | 5.52 | 4.93 | 4.60 | 4.60 | 5.80 |
| 1997 | 5.01 | 5.11 | 5.1 | 5.29 | 8.67 | 8.21 | 8.06 | 6.69 | 5.73 | 5.18 | 4.95 | 4.95 | 6.08 |
| 1998 | 5.03 | 5.33 | 5.63 | 6.10 | 11.07 | 10.93 | 9.10 | 8.02 | 7.52 | 5.33 | 5.19 | 5.19 | 7.04 |
| 1999 | 5.22 | 5.22 | 5.34 | 6.17 | 11.59 | 11.85 | 13.06 | 10.58 | 8.62 | 7.50 | 6.57 | 6.57 | 8.19 |
| 2000 | 6.49 | 6.39 | 6.40 | 6.55 | 10.25 | 13.76 | 12.75 | 10.92 | 8.95 | 7.86 | 7.01 | 7.00 | 8.69 |

From Table 1, the groundwater embedded depth has taken on ascending trend since Chuang Ye farm developed the well rice planting in 1985. Annual mean embedded depth of the groundwater increased 2.39 meter among 1985 and 1996 because the well rice area is about 0.12 million acres and the groundwater exploitation is comparatively small. However, the groundwater level has descended rapidly for recent four years because the rice area increasing has broken the dynamic balance of groundwater and could not supply the lateral influent of ambient river water. Because of the effect of seasonal precipitation, the groundwater table has periodical variation during the year. Therefore, the type of data model belongs to non-stable time series random model. It can be expressed by adding the above items as:

Where, the symbolic meanings are the same as the above and under-mentioned symbols.

3.2 Establish the Model of Trend Item

Based upon, to select the appropriate trend item, the model in the specific condition which takes the significant level =0.05 by fitting has been established. The model is as:

The curve of selected trend item shows in Figure 1.

Figure 1. The Curve of Tendency Item

### Figure 2. The Curve of Period Item

3.3 Establish the Fit Model of the Periodical Item

According to the above formulae, the limit of frequency multiplication (the maximal number of wave) has been taken as , where  is the number of samples. If  equals to 192 and  equals to 96, Fourier series is showed as in Table 6.

The total variance  of series  is 2.9873. Calculate the variance of each harmonic.  equals to 3.05 in the condition of significant level . After inspecting each harmonic variance, there are some harmonics to reach the significant level. They are No.1, No.16 and No.32. Their variance is 8.56%, 63.4% and 9.31%, and their  statistical measurement equals to 8.8433, 163.6796 and 9.7032 respectively. Because the values are larger than , establish periodical model to fit periodical series through selecting No.1, No.16 and No.32 harmonic. It is:

The curve of periodical item function is shown in Figure 2.

If the trend item  and periodical trend item  are deductible from the original series , the random item  is as: =--.

3.4 Establish Random Model

3.4.1 Normal Inspection of Random Series

In calculating, the manual value  of the random series  equals to 0, whose variance  is 0.5625 and whose skewness coefficient is 0.0239. Because the skewness coefficient tends to 0, the series may be taken account as a standard distribution and do not need normal conversion.

3.4.2 Auto Correlation Analysis of the Random Series

Applying the above formulae, the auto-correlation coefficient may be obtained when . The auto correlation figure has been shown in Figure 3. From Figure 3 the step 1 and step 12 of the random series is prominent to the independent series. Therefore, annual variation of the groundwater has dependent character and is a mean square contingency series. Adopt  model according to the above reasons.

3.4.3 Partial Correlation Analysis of Random Series

The task of partial correlation analysis is to ascertain the model steps. The partial correlation figure shows in Figure 4. It shows that  drops into the allowable range of 95% when . Thus we can ascertain that steps of the  model are . Select =1，4，5，9，12 and their  is out of the allowable rang of 95%. The correlation component  model of the random series is as followed:

3.4.4 Farther Identification of  Model

Farther identification is that the steps of model are fit or not by using  criterion. The result of calculation is as followed:

The model with 12 steps is best one according to  criterion.

3.4.5  Model Inspection

The main inspection is that the residential item  is independent or not. Through calculating the statistical measurement , , gain  by investigating the table of  when the significant level  equals to 0.05. Because <, the presumption that  depend each other can be received.

The normal test of independent random series  is as followed . Thus pass the normal inspection. Because variance， and mean value is 0, ～ obeys normal distribution. The random item model is:

3.5 Model combination

After folding each trend item model, the non-stable time series random model about the dynamic variation of the groundwater embedded depth can be carried out as:

Table 2. The Data of Forecast Groundwater Depth in Chuang Ye Farm in Sanjiang Plain (2001 ～2003)

|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | Mean |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2001 | 7.7790 | 7.6623 | 7.4138 | 8.0388 | 10.7718 | 13.8892 | 14.3394 | 13.4114 | 11.7809 | 10.0815 | 8.7644 | 8.3037 | 10.19 |
| 2002 | 8.5626 | 8.4424 | 8.2990 | 9.1161 | 11.3228 | 13.9963 | 15.2516 | 15.2722 | 14.4037 | 12.9368 | 11.3916 | 10.2419 | 11.6031 |
| 2003 | 9.5539 | 8.9517 | 8.7462 | 9.6365 | 11.6317 | 14.0312 | 15.7047 | 16.5313 | 16.6389 | 16.0139 | 14.7786 | 13.1547 | 12.95 |

4. Fitness and Forecast of the Model

Applying the model to fit the monthly mean precipitation from 1985 to 2000 in Chang Ye farm, the calculation has been carried out with well fitting as shown in Figure 5. The forecast is the embedded depth of the groundwater month by month in next 3 years. The forecast curve is shown in Figure 6 and the forecast value is in Table 2.

From the previous figure, the result calculated by the non-stable random model fitted to the original groundwater embedded depth series very well. The relative error of the model is . Through calculating, the mean relative error of the model is 6.49%. It can be found from Table 2. The groundwater level will descend continually in next 3 years in the region and the mean annual draw down rang is about 1.5 meter if according to the present development trend.

###### About Groundwater Depth

Figure 3. The Auto-correlation Figure of the Random Serial

About Groundwater Depth

#### Figure 4. The Partial Correlation Figure of the Random Serial

Figure 5. The Fitted Curve of the Random Model

Figure 6. The Forecasting Curve of the Groundwater Depth Dynamic varied in Chuang Ye Farm (2001-2003)

5. Conclusion

Applying surplus and fitting the regression analysis, Fourier series harmonic analysis and auto regression model, the authors have established the groundwater embedded depth forecast model with high fitting precision and good forecast result in Chuang Ye Farm, Sanjiang Plain. Meanwhile, the authors provided the references for future sustainable utilization of the groundwater resource in the region and put forward the indexes of quantity and scientific references in theory to guide the well rice production reasonably in Chuang Ye Farm and Sanjiang Plain.

Acknowledgement: (The financial support provided by Chinese National “863” High-Technique Programme (No. 2002AA2Z4251-09).

Correspondence author:

Qiang Fu

School of Water Conservancy & Civil Engineering

Northeast Agriculture University

Harbin, Heilongjiang 150030, China

Telephone: 01186-451-55190298 (O)

Cellular phone: 01186-13936246215

E-mail: fuqiang100@371.net

## References

Ding J, Deng Y. Stochastic Hydrology. Chengdu University of Science and Technology Publisher, Chengdu, Sichuan, China. 1988:36-48.

Ding Y, Jiang Z. Signal Treatment on Time Sequence of Meteorological Data. Weather Publisher, Beijing, China. 1998:32-7.

Du J, Xiang J. Time Sequence Analysis in the Application of Modeling and Forecasting. Anhui Education Publisher, Hefei, Anhui, China. 1991:64-8.

Fu Q. Synthesis Study on Save Water Technology and Optimization in the Course of Water Irrigation Rice Filed Production in San Jiang Plain. The paper of Ph. D application, North-East Agriculture University. Harbin, Heilongjiang, China. 2000:25-36.

Li J. Random Model Forecast of Groundwater Level in Exploitation Region. The Journal of Hydrology and Water Resource. 1999(20)4:7-9.

Yang S, Wu Y. Time Series Analysis and its Application to Engineering. Central Chinese University of Technology Publisher, Wuhan, Hubei, China. 1996:125-34.

Zhen S, Li Y. Discharge Forecast Model in Huo Quang Irrigated Area. The Journal of Advances in Water Science 1999;4(10):382-7.