Dr. Ibrahim CAN
Atatürk Universitesi

Muhendislik Fakultesi

25240 Erzurum-TURKEY

February 06, 2004

The Editor
Marsland Company

P.O. Box 753

East Lansing, Michigan 48826

The United States

To whom it may concern:

Enclosed is a paper, entitled "Simplified equations calculates head losses in commercial pipes" by Ibrahim CAN. Please accept it as a candidate for publication in the Nature and Science. Should you need to contact me, please use the above address. You may also contact me by fax at +90-442-236-0957 or via email at ibcan@atauni.edu.tr or ibrahim0369@yahoo.com

Sincerely,

Ibrahim CAN (the corresponding author)

Simplified equations calculates head losses in commercial pipes

Ibrahim CAN*

Civil Engineering Department, Ataturk University, 25240 Erzurum, Turkey

ibcan@atauni.edu.tr      ibrahim0369@yahoo.com

Abstract

Direct solutions of pipe flow problems are not possible because of the implicit form of Colebrook-White equation which is most commonly used for determining the friction factor of commercial pipes. New empirical equations for head loss, , due to friction undergone by water flowing in the PVC, commercial steel, asphalted cast iron, galvanized iron, cast iron and concrete pipes which are commonly used in pipelines and water distribution systems were developed. The calculation of the parameters of the proposed models has been done through non-linear multivariable regression. Maximum relative error of each model is less than 2 %. Therefore, these simple equations can offer significant advantage in optimization studies and hydraulic analysis of pipelines and water distribution systems.

Key words: commercial pipes, head losses, pipelines, water distribution systems

Introduction

Head losses are generally the result of two mechanisms:

- Friction along the pipe walls

- Turbulence due to changes in streamlines through fittings and appurtenances

Head losses along the pipe wall are called friction losses or head losses due to friction, while losses due to turbulence within the bulk fluid are called minor losses (Walski et al., 2001; White 1994). Estimation of head losses due to friction in pipes is an important task in optimization studies and hydraulic analysis of pipelines and water distribution systems (Giles, 1962; Fox et al., 1992).

The best equation for computing the frictional head loss in a given pipe for a given discharge is the Darcy-Weisbach equation (Giles, 1962; Fox et al., 1992; Walski et al., 2001):

(1)

Where	hf is the head loss due to friction that has the unit of length (L), f is a dimensionless friction factor, L is the length of the pipe (L), D is the internal diameter (L), V is the average velocity (LT-1), and g is the acceleration due to gravity (LT-2). For turbulent flow (RE>4000), the friction factor f is a function of the Reynolds number RE, and the relative roughness, which is the internal pipe roughness  divided by the pipe diameter. The Reynolds number for full flowing circular pipes can be found using the following equation:

(2)

Where	RE is the Reynolds number,  is the kinematic viscosity (L2T-1). The kinematic viscosity is a function of temperature, but optimization studies and hydraulic analysis of pipelines and water distribution systems treats kinematic viscosity as a constant assuming a temperature of 20 oC (Walski et al., 2001). The kinematic viscosity of water for  20 oC is 10-6 m2/s (Giles, 1962). Numerous formulas exist that relate the friction factor to the Reynolds number and relative roughness. One of the earliest and most popular of these formulas is the Colebrook-White equation (Giles, 1962; Fox et al., 1992; Shames, 1989; White 1994):

(3)

The difficulty with using the Colebrook-White equation is that it is an implicit function of the friction factor (f is found on both sides of the equation). Typically, the equation is solved by iterating through assumed values of f until both sides are equal. The optimization studies and hydraulic analysis of pipelines and water distribution systems often involves the implementation of a tedious and time-consuming iterative procedure that requires extensive use of computers. Empirical head loss equations have a long and honorable history of use in pipeline problems. Their initial use preceded by decades the development of the Moody diagram, and they are still commonly used today in professional practice. Some prefer to continue to use such an equation owing simply to force of habit, while others prefer it to avoid some of the difficulties of determining the friction factor in the Darcy-Weisbach equation (Larock et al., 2000). In this work, empirical equations for estimation of head losses in PVC, commercial steel, asphalted cast iron, galvanized iron, cast iron and concrete pipes which is commonly used in pipelines and water distribution systems were improved. The calculation of the parameters of the new improved empirical equations has been done through non-linear multivariable regression.

Methods

The development of the models which is proposed for six commercial pipes involves three basic steps. These include the generation of data required for calculation of the parameters of the models, calculation of the parameters of the proposed models, and the evaluation of the models.

Data generation

The data set for each model consists of a two dimensional grid of 625 data points, created from twenty-five pipe diameter (D) values selected in equal increments on the interval of    0.1 m to 1.2 m and twenty-five average velocity (V) values selected in equal increments on the interval of 0.5 m/s to 3.1 m/s. The target friction values for the 625 points are values obtained using the values Colebook–White formula (Eq. 3). The friction values, calculated iteratively using (Eq. 3), were considered to have converged when the ratio of the difference in values obtained between two iterations and the the value obtained from the most recent iteration was less than 10-8. Later, the head loss values obtained using the Darcy-Weisbach equation (Eq. 1).

Proposed Model

The model which is proposed for calculation of head loss is:

(4)

Where, a, b and c are model parameter.

The calculation of the parameters of the proposed model has been done through non-linear multivariable regression. The optimization toolbox of the MATLAB was used to perform this steps. Obtained formulas have been given in Table (1).

Table 1. Pipe types and proposed head loss formulas

| Pipe Type | Head Loss (m) |
| --- | --- |
| PVC (0.0015 mm) |  |
| Commercial Steel (0.05 mm) |  |
| Asphalted Cast Iron (0.12 mm) |  |
| Galvanized Iron (0.15 mm) |  |
| Cast Iron (0.26 mm) |  |
| Concrete (0.5 mm) |  |

Performance Evaluation of the models

Several statistical measures are available for evaluating the performance of a model. These include correlation coefficient, relative error, standard error (Dowdy et al., 1982), among others. Correlation coefficient and relative error are the most frequently used criteria and were employed in this study.  Using the obtained formulas (Table 1) and Eq. (3) and Eq. (2), for diameter of 0.1 m -1.2 m, mean velocity 0.5 m/s – 3.1 m/s and pipeline length 1000 m, head losses for each pipe type were calculated respectively. The desired head loss versus calculated head loss plotted for each pipe type separately (Fig. 1 through Fig. 6). Each model’s correlation coefficient is R. Maximum relative error of each model is less than 2 %. It can be seen from the figures that the fitness of desired and calculated head loss of each pipe type is perfect.

Conclusions

In this work, non-linear multivariable regression method was used to obtain simple and explicit formulas for head loss, , due to friction in the PVC, commercial steel, asphalted cast iron, galvanized iron, cast iron and concrete pipes which are commonly used in pipelines and water distribution systems. Correlation coefficient of each model is and maximum relative error of each model is less than 2 %. Therefore, these simple equations can offer significant advantage in optimization studies and hydraulic analysis of pipelines and water distribution systems.

References

- DOWDY S and STANLEY W, Statistics For Research, New York, John Wiley & Sons, 1982,

- FOX RW and McDONALD AT, Introduction to Fluid Mechanics, New York Wiley, 1992,

- GILES RV, Theory and Problems of Fluid Mechanics and Hydraulics, New York, Schaum Publishing Co, 1962, 274 pp

- LAROCK BE, JEPPSON RW and WATTERS GZ Hydraulics of Pipeline Systems, New York, CRC Press, 2000,

- Optimization Toolbox Release Notes For Use With MATLAB©, The MathWorks, Inc. Natick, MA

- SHAMES IH, Mechanics of  Fluids, Singapore, McGraw-Hill Book Co, 1989, 692 pp

- WALSKI TM, CHASE DV and SAVIC DA Water Distribution Modeling, Waterbury, CT, USA, Haestad Pres., 2001,

- WHITE FM,  Fluid Mechanics, Singapore, McGraw-Hill Book Co., 1994, 736 pp

# Text boxes

Figure 1. Predicted versus desired values of the head loss for PVC pipes

Figure 2. Predicted versus desired values of the head loss for commercial

steel  pipes

Figure 4. Predicted versus desired values of the head loss for galvanized iron

pipes

Figure 3. Predicted versus desired values of the head loss for asphalted cast

iron  pipes

Figure 5. Predicted versus desired values of the head loss for cast iron pipes

Figure 6. Predicted versus desired values of the head loss for concrete pipes