Influence of furfural on the recombinant Zymomonas mobilis strain CP4 (pZB5) for ethanol production

ABSTRACT: The toxicity of furfural as an inhibitor of growth and ethanol production by recombinant Zymomonas mobilis strain CP4 (pZB5) was investigated by adding furfural 0.475 g/l and 1.9 g/l in the fermentation media. The inhibitory effects of furfural were observed with a decrease of 30% and 60% (w/v) in biomass production and 19% and 76% (v/v) in ethanol production, respectively.

Keywords: ethanol, furfural, glucose, inhibitor, Zymomonas mobilis, xylose

INTRODUCTION:

Traditionally, ethanol is been produced in batch fermentations with yeast strains that cannot tolerate high concentrations of ethanol. Strain improvement is necessary to obtain alcohol-tolerant strains for fermentation. Z. mobilis, a gram-negative bacterium, is considered an alternative organism for large-scale fuel ethanol production (Mohagheghi et al, 2004).

The complex of lignocellulosic components in plant fiber presents difficulties for conversion of wood to ethanol. It is important to study the effects on fermentation parameters of all the components that result from hydrolysis and separation and know how to deal with toxic compounds.

Three major pretreatment alternatives exist: milling, steam explosion, and dilute acid hydrolysis. The latter option maximizes use of the hemicellulose fraction of the wood (Boussaid, 2000). Typically, wood residues are treated at temperatures ranging from 200°C to 220°C, with cooking times of 3 to 5 minutes and 2% to 3% of SO2 (v/v).  Another condition is 170°C, 15-60 minutes cooking and 0.01-0.1% (v/v) of H2SO4 (Um et al., 2001).

The components of hemicellulose are converted to pentoses and degradation products, according to the following reactions:

Pentosan -----(H2O)----(         pentose (xylose)---(- 3 H2O)--(                    furfural

Figure 1. Conversion reactions.

Hydroxymethylfurfural (HMF) is also produced from hexose sugars under high temperature acidic conditions.

Morphological changes are observed by light microscopy during growth of Z. mobilis at partially inhibitory concentrations of aldehydes. Cells either appear as elongated or forming short chains after 6 hours compared with normal cells. After 24 h, cells are swollen and rounded (Zaldivar et al, 1999).

Shahab and Hadi (1995) demonstrate that furfural reacted primarily with AT base-pair sequences in double-stranded DNA causing strand breaks via spontaneous depurination and depyrimidination.

# MATERIALS AND METHODS

Recombinant Z. mobilis strain CP4 (pZB5), which contains the Escherichia coli genes for xylose assimilation and pentose metabolism (transketolase, transdolase) on the plasmid pZB5 together with the gene for tetracycline resistance (Zhang et al., 1995), was used in these experiments.

Growth media for the recombinant Z. mobilis strain was as follows: glucose and xylose concentrations as specified, (NH4)2SO4 (1 g/l in media containing 10 g/l glucose and 10 g/l xylose); KH2PO4 (2 g/l); MgSO4.7H2O (1 g/l); yeast extract (10 g/l). Media were sterilized by autoclaving at 121°C for 15 minutes. Tetracycline was added aseptically to the sterile media at room temperature at a concentration of 10 mg/l as selection pressure for plasmid (pZB5) maintenance.

All inocula were prepared in stationary shake flasks incubated at 30°C at an inoculation density of 0.004 g/l.

Experiments were conducted in 500 ml shake flasks with a working volume of 200 ml. Control fermentations without furfural were carried out simultaneously, under exactly the same conditions, using the same inoculum preparation to compare with those fermentations containing furfural. Environmental conditions were controlled at a temperature of 30°C and an agitation rate of 200 rpm.

Furfural at (0.475 g/l) and at (1.9 g/l) were added 10 hours after inoculation, between lag and exponential phases. Samples were withdrawn at regular intervals for OD measurements and were filtered (Whatman Syringe filters, Fisher Scientific, pore size 0.2 (m, Nylon) for xylose, glucose, ethanol and furfural analysis. The filtered solutions were stored at –20°C prior to analysis. Each of the fermentations was run in duplicate.

Biomass concentrations were determined by OD measurements (at 600 nm) using a spectrophotometer (Perkin Elmer Lambda 3B UV/VIS) and converted to DCW by use of a calibration curve.

Sugars and ethanol concentrations were determined in the filtered supernatants using a Waters HPLC with an Aminex HPX-87H column (BioRad, Hercules, CA) with 5 mM H2SO4 (at 65° C, 0.6 ml/min) as the mobile phase.

UV spectra were used as a rapid and convenient method to estimate total furans (HMF and furfural).  Many of the lignin and sugar degradation products absorb in the UV region, all of which contain a single prominent peak at approximately 278 nm, shoulders at 320 and 220 nm, and end absorbance continuing off-scale at around 220 nm. The following equation was used to estimate furfural content: A284-A320=0.127*Total furfural (mg/l) + 0.05   (Martinez et al., 2000).

RESULTS:

Figure 2. Biomass production.

Furfural concentrations of 0.475 g/l and 1.9 g/l cause considerable, but not complete inhibition of biomass production. This toxic compound affects growth in the exponential phase. The specific growth rate (() decrease by 29% (w/v) in the experiment containing 0.475 g furfural /l and 73% (w/v) at the higher treatment level.

Figure 3. Consumption of sugars and ethanol production in control fermentation.

Figure 4.  Consumption of sugars and ethanol production using 0.475 g/l of furfural.

Figure 5. Consumption of sugars and production of ethanol using 1.9 g/l of furfural.

Glucose is completely consumed in control and 0.475 g/l furfural fermentations. However, due to the toxicity of the furfural in the mixture of 1.9 g/l furfural and 5 g/l glucose, xylose as well as glucose is utilized at lower rate thus resulting in a lower production of ethanol. (Figure 5)

Figure 6.     Ypsmax=f (furfural)

Table 1.  Fermentation parameters

| Fermentation furfural g/l | Qs substrate g/time | Qetoh product g/time | Yxs cell mass/substrate g/g | Yps product/substrate g/g | ( hr-1 |
| --- | --- | --- | --- | --- | --- |
| Control 0.475 1.9 | 0.45 0.40 0.17 | 0.22 0.18 0.05 | 0.00271 0.00261 0.00226 | 0.5 0.45 0.3 | 0.089 0.063 0.024 |

The volumetric sugar consumption rates, Qs, are shown in Table 1. Ethanol is produced after 15 hours. However, the final concentration is reduced by 19.04% and 76.19% compared to control by using 0.475 g/l and 1.9 g/l furfural, respectively. Overall volumetric ethanol productivity, Qetoh, values are calculated using samples acquired at 38 hours.

The required nutrients for the microorganism in the culture media are modified by furfural, so that the production of biomass (Yxs) is affected as shown in Table 1. Inhibition of the fermentation by furfural has been reported to decrease with increasing cell mass concentration (Boyer et al., 1992; Navarro, 1994). With the increase of furfural, the consumption of sugars Qs and the relation with ethanol production Yps are reduced due to the morphological changes in the cell.

DISCUSSIONS:

Ranatunga et al (1997) conducted a similar study in which inhibition of ethanol production was reported to be 4% using the same strain of Z. mobilis as in this study. The substrate in their work consisted of the pretreated liquid hydrolyzate prepared from the mixture of red oak, white oak, and yellow-poplar. The hydrolyzated mixture contained the following components: glucose (2.40+0.48 mg/ml), xylose (44.75+2.02 mg/ml), acetic acid (9.22+0.43 g/l), and furfural (0.91+0.051 g/l). Such substrate composition was different from the one used in present work [50% (w/v) of glucose, 50% (w/v) of xylose, no acetic acid and 1.9 g/l of furfural].

Previous work indicated that 1.3 g/l furfural might be found in hydrolysate liquor from yellow poplar sawdust (Hayward et al., 1999). In our research Qetoh decreased compared with the reference fermentation when the furfural concentration increased above 1.9 g/l, indicating that when the concentration of furfural was increased beyond 1.9 g/l the energy reserves of the cell were depleted, because the toxicity of the furfural did not allow Z. mobilis to metabolize sugars to ethanol. (Campbell, 1996).

Data from this study and others have been incorporated into Table 2, that presents a comparison of furfural inhibition studies using several fermentative microorganisms.

Table 2.  Inhibition of ethanol production by furfural (Zaldivar and Ingram, 2000).

| CONCENTRATION (g/l) | INHIBITION (%) | MICROORGANISM | REFERENCE |
| --- | --- | --- | --- |
| 1.3 4.51 0.95 1.9 2.8 4.0 3.5 | 9 96 40 76 -1 79 -38 | Pichia stipitis E. coli pL01297b Zymomonas mobilis Zymomonas mobilis S. cerevisiae S.cerevisiae (anaerobic) E. coli LY01 | Tran et al, 1986 Beall et al., 1991 Ranatunga et al., 1997 This work Palmqvist et al., 1999 Palmqvist et al., 1999 Zaldivar J et al., 1999 |

Despite differences in experimental protocols and metabolic pathways, Z. mobilis is one the least tolerant microorganisms. These studies suggest that the complete removal of furfural in the hydrolysate liquor may be necessary for a biomass-to-fuel process.

ACKNOWLEDGEMENTS:

REFERENCE:

- Beall DS, Ohta K, Ingram LO. Parametric studies of ethanol production from xylose and other sugars by recombinant Escherichia coli. Biotechnol Bioeng 1991; 38:296-303.

- Boussaid A. Fermentability of the hemicellulose-derived sugars from steam exploded softwood (Douglas fir). Appl Biotechnol Bioeng 2000; 64(3):284-9.

- Boyer LJ, Vega K, Klasson KT, Clausen EC, Gaddy JL. The effects of furfural on ethanol production by Saccharomyces cerevisiae. Biomass Bioenergy 1992; 3(1): 41-48.

- Campbell N. Biology. In: Benjamin Cummings. California USA. 1996; 89-107

- Hayward TM, Hamilton J, Templeton D, Jennings E, Ruth M, Tholudur A, McMillan J, Tucker M,  Mohagheghi A. Enzyme production, Growth, and adaptation of T.reseei Strains QM9414, L-27, RL-P37, and rut C-30 to Conditioned Yellow Poplar sawdust Hydrolisate.  Appl Biochem Biotech. 1999; 77(79): 293-309.

- Martinez A, Rodriguez M, York S, Preston J, Ingram L. Use of the UV Absorbance to Monitor Furans in Dilute Acid Hydrolysis of Biomass. Biotechnology 2000; 16:637-641

- Mohagheghi A, Dowe N, Schell D, Chou Y, Eddy C, Zhang M. Performance of a newly developed integrant of Zymomonas mobilis for ethanol production on corn stover hydrolysate. Biotechnology Letters 2004; 26:321-325

- Navarro AR. Effects of furfural on ethanol fermentation by Saccharomyces cerevisiae: Mathematical models. Curr Microbiol 1994; 29:87-90.

- Palmqvist E, Almeida JS, Hahn-Hagerdal B. Influence of furfural on anaerobic glycolytic kinetics of Saccharomyces cerevisiae in batch culture. Biotechnol Bioeng 1999; 62:447-454.

- Ranatunga TD, Jervis J, Helm RF, McMillan JD, Hatzis C. Identification of inhibitory components toxic toward Zymomonas mobilis CP4 (pZB5) xylose fermentation.  Appl Biochem Biotechnol 1997; 67:185-198.

- Shahab U, Hadi SM. Reactions of furfural and Methyl furfural with DNA. Biochemistry and Molecular Biology International. 1995; 35(1): 185-195.

- Tran AV, Chambers R. Ethanol fermentation of read oak acid prehydrolysate by the yeast Pichia stipitis CBS S776. Enzyme Microb Technol 1986; 8:439-444.

- Um B, Sung B, Soon C. Effect of Pretreatment Reagent and Hydrogen Peroxide on Enzymatic Hydrolysis of Oak in Percolation Process. Applied Biochem Biotechnol 2001; 91(93): 81-94.

- Zaldivar J, Martinez A, Ingram L. Effect of selected aldehydes in the growth and fermentation of ethanologenic Escherichia coli. Appl Biotechnol Bioeng. 1999; 65(1): 24-33.

- Zhang M, Eddy C, Deanda K, Finkelstein M, Picataggio S. Metabolic engineering of a Pentose Metabolism Pathway in Ethanologenic Zymomonas mobilis. Science. 1995; 267:240-243