The Cellular Response of the Reaction to the Electromagnetic Field Frequency at 2.4 G Hertz

Shen Cherng *, Chia-Ching Chu *, Hsien-Chiao Teng **

* Department of Electrical Engineering, Chengshiu University, Niaosong, Kaohsiung, Taiwan 833 cherngs@csu.edu.tw

** Department of Electrical Engineering, Chinese Military Academy, Fengshan, Kaohsiung, Taiwan 830, scteng@cc.cma.edu.tw

Abstract: Electromagnetic field (EMF) initiates the cellular response of being stimulated frequency at 2.4 GHz. By using signal-to-noise ratio spectrum analysis of the fluctuating process and measuring the magnetic fluctuation at the distance 10-1 mm perpendicular to the cells layer, the rat liver epithelial cellular responding extremely low frequency (ELF) 14 Hz was observed when the cells layer cultured into the substrate with patch radiator resonated at 2.4 GHz. Twenty percent inhabitation of the gap junction intracellular communication (GJIC) from the analysis of Lucifer yellow fluorescence microscopic image confirmed the biological effect while comparing with the control [The Journal of American Science. 2005;1(2):xx-xx].

Key words: ELF, EMF, radiator, power gain, gap junctional intracellular communication

Introduction

There have been of considerable discussions about the biological response to the exposure of electromagnetic field (EMF). Public hazard and health effect is one of the major concerns. We go further to answer if biological system reacts to cellular phone operated at 2.4 GHz. In this article, we investigated if any intrinsic signal can be initiated from the rat liver epithelial cells monolayer. The cells layer can function as a thin film substrate for patch resonator operated at 2.4 GHz. Near magnetic field fluctuation can be measured and transformed to the oscilloscope voltage

V={V1,V2,…..VN-1, VN}, Computing the autocorrelation of sequence V, we get

Sk is the Fourier exponent expansion of Rq and also is the power density component of the system at frequency ωk =k (fundamental frequencies).

The unit of Sk is watt per frequency for each Vp and . Relying on cells layer surface electrical current distribution, gap junctional intracellular communication (GJIC) modulation can be used to express the cell’s response under the exposure of EMF. Since GJIC is affiliated with many endpoints [1], GJIC modulation is a good scale factor to evaluate if the ELF signal being existed for the cell system. Scrape loading dye transfer of Lucifer yellow is the technique used to measure GJIC modulation [2].

Materials and Methods

By using IE3D simulator, we simulated the design to confirm the operation frequency at 2.4 GHz before fabrication [3]. Figure 1 depicted a patch radiator design with a single rat liver epithelial cells layer cover on substrate. Radiation pattern was measured at 2.4 GHz frequency. The glass substrate was etched concavely at 0.15 mm in depth where the cells would be cultured into it. The aluminum metal layer was deposited 0.05 mm thick by evaporation before etching the substrate. The thickness of the cell layer was about 1 μm Therefore, the depth between the metal and cell was about 0.2 mm. The thickness of the substrate was 0.4 mm.

Figure 1a. Biological cell patch antenna (cell layer is deposited on the substrate).

In addition, Figure 1b showed the magnetic fluctuation very near the cell layer on the patch substrate.

Figure 1b. The near geo-magnetic field fluctuation (10–4 m to the rat liver epithelial cell layer) of the patch resonated at 2.4 GHz.

Cell Culture

The rat liver epithelial cell line was obtained from the Fisher Scientific (WB344). It was derived from normal liver and maintained in D-medium (Formula 78-5470EF, GIBCO, Grand Island, NY), supplemented with 10% fetal bovine serum (GIBCO) and 50 µg/ml gentamicin (Quality Biological, Inc.). The cells were incubated at 37˚C in a humidified atmosphere containing 5% CO2 and 95% air and were fed or trypsinized every two to three days.

Power spectrum

Matlab and Fortran computer languages were used for power density spectrum analysis of sequence V. The sample rate was taken 2000 times in a second. Trial signal, Asin(ωt), was created by Matlab. We took the maximum peak of sequence V and add trial signal with amplitude A =Vmax to V and refer the result to be Vtest at frequency ω. We performed Power density spectrum (PDS) calculation by taking autocorrelation and Fourier transform of Vtest. Then, using with different amplitudes, for instance A=0.7Vmax, A=0.4Vmax, and A=0.03Vmax for a given test signal at frequency ω, we refer results to be S0.7(ω), S0.4(ω) and S0.03(ω) respectively. The spectrum curve is then defined as  and shown in Figure 2. By using square curve fitting, we can solve the equations to get p, q and r-values respectively. Intrinsic ELF would have its own specific power depicted as a small signal buried in background. The threshold value of r is the condition of recognizing the cellular response frequency and highly related to thermal motion. Accordingly, intrinsic ELF have to be reconfirmed by bioassay of GJIC .

Figure 2. In comparison with the trial signal at 14Hz SNR spectrums of the magnetic field fluctuation at the distance 10 –4 m to the rat liver epithelial cell layer and the controls.

## Bioassay of GJIC

The scrape load/dye transfer (SL/DT) technique was used to measure the GJIC within cells. After exposure to ELF at intrinsic frequency, the cells were rinsed with phosphate buffered saline (PBS), and a PBS solution containing 4% concentration lucifer yellow fluorescence dye is injected into the cells by a scrape using a scalpel blade. Afterwards the cells were incubated for 3 min and extra cellular dye was rinsed off and fixed with 5% formalin. We then measured the area of the dye migrated from the scrape line using digital images taken by an epifluorescent microscope and quantitated with Nucleotech image analysis software [3] for the GJIC images.

# Results

Figure 2 illustrated the fitting curves of trial signal at 14 Hz in different conditions. Analysis allows us to validate the observation that ELF at 14 Hz modulates GJIC. GJIC modulation can then be an index to find the buried ELF biological signal. Figure 3a and Figure 3b depicted the images of the GJIC under different conditions.

Figure 3a. The fluorescent image of the gap junctional intracellular communication before exposure of 2.4 GHz EMF.

Figure 3b. Rat liver epithelial cells GJIC image at 2.4 GHz (20% inhibitation fluorescent than control).

Figure 5. Radiation pattern with cells’ thin layer on substrate (rat liver epithelial cells mono-layer cultured on glass plate).

Figure 6. Radiation pattern with no cells layer on the substrate (only substrate glass, medium and patch radiator)

# Discussion

The cell monolayer, which may function as part of a patch substrate, affects the induced geo-magnetic field, which fluctuates from 20 m Gauss to 200 m Gauss. The calculated electrical current with confluent cells is about 10 –9 Amp [4] under the magnetic fluctuation.

# Conclusion

We conclude that the cell monolayer induced responding extremely low frequency (ELF) in 2.4GHz EMF under the influence of radiation is buried in near field V(t). The intrinsic ELF modulated the GJIC within cells. In addition, this report demonstrated the calculated intracellular signal power curves for cell system. The major concern for this report, not only was the 2.4GHz reaction on cell line system, but also challenged whether cellular phone that we are using induced magnetic field fluctuation may cause the health effect though environment. Our study shows that we can recognize the biological effects of the cells with path radiator to the reaction of EMF and investigate the possible damage of the health of 2.4 GHz in low power EMF environment.

Correspondence to:

Hsien-Chiao Teng

Department of Electrical Engineering

Chinese Military Academy

Fengshan, Kaohsiung, Taiwan 830

Email: scteng@cc.cma.edu.tw

Telephone: 011-886-77479510 ext 134

References

[1]	Trosko JE, Chang CC. Role of stem cells and gap junctional intercellular communication in human carcinogensis. Radiation Research 2001;155:175-80.

[2]	Wong KL. Planar antennas for wireless communication, Wiley, New York, 2003, p216, p259.

[3]	Upham BL, Deocampo ND, Wurl B, Trosko JE. Inhibition of Gap Junctional Intracellular Communication by perfluorinated fatty acids is dependent on the chain length of the fluorinated tail. Int J Cancer 1998;78:491-5.

[4]	Hart F. Cell culture dosimetry for low frequency magnetic fields. Bioelectromagnetics 1996;17:48.

.

# Text boxes

- sample with cells

- sample only buffer

○   sample with nothing