Timed Colored Petri Nets Based

Modelling and Scheduling of Aero-engine maintenance
Xinmin Tang， Shisheng Zhong

School of Mechatronics Engineering, Harbin Institute of Technology, Harbin, Heilongjiang 150001, China

txmofhit@hit.edu.cn; zss@hit.edu.cn

Abstract: Aero-engines maintenance procedure can be treated as a typical discrete event dynamic system. A theory that synthesized timed colored Petri net is proposed. The theory adopts a bottom-up approach by merging all sub modules, and each one characterizes the critical resource contention among processes. Nevertheless Petri net seems inapplicable to dynamic scheduling modelling because of its structural rigidity. Shared composition method of Petri net is introduced, which makes its structure adjustable dynamically. Given a set of preemptive dispatching rules, the makespan can be analyzed using linear state equation in the sense of max-plus algebra. To minimize makespan of each aero-engine, genetic algorithm is adopted to arrange the firing sequence of transitions. Dynamic scheduling strategy uses rolling horizon composed by colors is presented. According to the simulation result, the module is verified to be effective and robust.

Keywords: timed colored Petri nets; shared composition; static scheduling; dynamic scheduling

1 Introduction

Aero-engine maintenance procedure can be treated as a typical discrete dynamic system (DES). It involves planning, scheduling and controlling of resources, aerial materials, activities, etc. Woxvold proposed a solution to planning and scheduling of aircraft maintenance by combining of MRP (Materials Requirements Planning), PAC (Production Activity Control) and CPM (Critical Path Method) into a unitary structuring technique, which was applied to maintenance of Boeing 737 commercial aircraft[1]. Goldratt used project management technology based on TOC (theory of constraints) to solve maintenance scheduling problem in Israeli air force, which shorten aircraft maintenance duration dramatically by some case studies[2].

In the maintenance work shop, maintenance tasks with different work level may be carried out concurrently, as a result machines resource conflicts are unavoidable. Additionally, maintenance procedures are always interrupted by stochastic events unexpected. Scheduling methods mentioned above do not provide strict mathematical model and are usually applied to static other than dynamic environment. Petri nets as a tool to characterize a concurrent, asynchronous, conflicting, stochastic system is widely used in discrete dynamic system modelling, simulating and scheduling[3]. Timed colored Petri nets is one of high level model which has advantages over basic Petri nets in making the model of  a DES much more compact and concise.  In this paper, this is gained by introducing “colors” to distinguish among tokens presenting different aero-engines.

The organization of this paper is described as follows. In Sections 2, sub modules based on timed colored Petri nets describe interactions between components of aero-engine and machine resources are built, and then shared composition method of Petri nets is adopted to realize bottom-up modelling . In Section 3, the makespan of each aero-engine is analyzed using max-plus algebra, then Genetic algorithm is adopted to optimize the firing sequence of transitions during static scheduling. In Section 4, to deal with discrete events emerge in workshop, a dynamic scheduling strategy uses rolling horizon is presented, which made the model more adaptive and robust. In Section 5, an example is demonstrated and the performance is analyzed. Finally, conclusions are provided.

2  Bottom-up Modelling  of Aero-engine Maintenance Procedure

# 2.1  Construction of Sub Modules

Suppose that the directional chart  represents the maintenance workflow of an aero-engine component. Each node of the chart is multivocal, firstly it specifies the maintenance process , where represents all processes of the component, secondly it specifies the machine to process , where  represents all machines. It is assumed that one process only uses one machine and the mapping between andis . For , if there exists a directional edge, then the component must be transferred to machine  after accomplished processing in machine .

Definition 1 (Work Processing Module).  is a state machine and satisfies the following conditions: (1) There exists but only one place  is called idle place and . (2)   is called operation place and .

The rules to construct from  are described as follows: (1) Build up one by one mapping from nodes  to transitions , . (2) For , if there exists a directional edge, then add place  to , let   and . (3) If in-degree  of is zero, then add idle place  to , let  and .

Definition 2 (Resource Sharing Module).  is extended from and satisfies the following conditions: (1)  is called resource place and  represents the quantity of the resource. (2) , , such that , where  , which means resources are not exhaustive and should be released after the process is accomplished.

The rules to extendfrom are described as follows: (1) , Build up one by one mapping from  to ,  . (2) , , if , then let , else let .

According to definition 2, the resource place looks like “resource dispatching and recycling center”. Its initial marking specifies that the resource is available and processes related must compete for the resource[4].

# 2.2  Extension to Sub Modules

It is obvious that  reveals the interactions between processes of a single component instance. In order to characterize the resources contention among multiple instances of the component, the original Petri nets should be expanded for more meaningful. An effective resolution is to set up relationship between color set and nodes of Petri nets including places and transitions. Additionally, the deterministic time delay should be related with the transitions of .

Definitions 3 (Timed colored resource sharing module).  extended by is defined as follows:  is timed colored Petri nets, where  are maintenance operation state places,  are machine resource places;  are maintenance processes;  is color function defined from places and transitions into color set, , , , , , ; , ;    is input function that specifies input place of transition ;   is output function that specifies output place of transition ; initial marking  is defined from  into vector and represents the token number with a binding color  in the place ; is time delay function specify the firing time duration of transitions.

Transition  with a binding color  is said to be firing enable at marking a  if   and , where . When enabled transition  begins to fire, the new marking is calculated from:

(1)

Once transition  begins firing, it will finish after duration . The new marking is calculated from:

(2)

The flowing of colored token from place to place represents the components of aero-engine transferring from one machine to another, which reveals’ the busy and idle state of machine resources in the discrete time duration.  based on timed colored Petri nets has properties as follows:

Property 1 (Conservation). Note that the  is a state machine, then , such that  and , so , such that  , where  represents the projection of  from  to subset . For , : , in other words, resource tokens are not exhaustive and can be reusable after released, so . Synthetically, there exists vector  , such that , where ,  is the quantity of token with a binding color . So  is conservative.

Property 2 (Boundedness). Note that  is conservative, then there exist , where  , that is , satisfies , then :  , so  is bounded.

Property 3 (Deadlock-free). For , ,  , such that , that is , which means  contains siphons and traps, call them . If for every resource place of , there exists at least one token, that is , each siphon contains a marked trap (MST), so  is deadlock-free[4].

# 2.3  Shared Composition of Sub Modules

To characterize the resources contention among inhomogeneous components have different processing routines, shared composition of sub modules is introduced. Jiang Changjun discussed the state constancy and behavior constancy on shared composition Petri nets[5].

Definition 4 (Shared composition). For timed colored Petri nets , where , , . If  satisfies that: (1) , ; (2) , ; (3) , ; (4) if  , let  , else if , let , ; (5) if   , let , where  , else if , let ,,  is the shared composition Petri nets of  and , for short,  .

Property 4 (State constancy).  Suppose that   is timed colored Petri nets, , and . If , , such that   , then  is state constant, where , .

Proof: Let ,  be sub nets of  and satisfy the following conditions: (1) ; (2) ; (3)  ; (4) if , then . Obviously, , such that  , then ,   is satisfied. Since , according to definition,  satisfies state constancy.

State constancy reveals that sub modules keep mark of all places except shared ones unaltered after merged, which means in the merged module, new arrival component does not change the state of processing components. This property provides theoretic support for dynamic scheduling driven by events.

3 GA Based Multiple Aero-engine Static Scheduling

Static scheduling can be described as follows: all components are ready for processing at the beginning and there are no new arrivals, after scheduling the processing orders of all components are assume to be unaltered and machines never break down.

# 3.1  Static Scheduling Makespan Calculating

There are three ways to dealing with scheduling problem in Petri nets. One is by using reachability graph to determine a firing sequence of transitions to get the optimal schedule. The second way is by heuristic search of reachability graph. The last is using decision rules to solve conflicts[6]. In this paper, genetic algorithm is adopted to determine the firing sequence of transitions Petri nets.

Suppose that the processing order is given, which means the firing sequence of transitions with binding color instances is , then the deterministic state transmission equation can be describe as: , where  is weight function defined from colored arcs,  is the firing vector from  to  step. According to the firing rules of timed Petri nets, if transition  with a binding color  is fire enable, the firing procedure is summarized as follows:

1) Before  step, suppose that arrival timestamp of the token with color  in input operation place of transition  is , arrival timestamp of the token with color  in input resource place of  is , then the firing timestamp  of transitions  with a binding color  is calculated from:

(3)

2) After  step, transition accomplishes firing after a duration , the timestamp is , which is calculated from:

(4)

In formulas (4) above, max-plus algebra symbols “” and “” are introduced. The two symbols are defined respectively as follows:  and . Suppose that initial timestamp is  and the iterations ends after  steps when there are no enable transitions, then the makespan is calculated from  , where .

Obviously, given the firing sequence of transitions, makespan can be calculated within linear time complexity. In the next section, genetic algorithm is adopted to determine the firing sequence of transitions Petri nets.

# 3.2  Genetic Algorithm Based Static Scheduling

Genetic algorithm behaves excellently when dealing with configuration optimization problems. In this paper, Genetic operator encodes the transition firing sequence of Petri nets into chromosome and the scheduling algorithm decodes the chromosome into schedule. In the later genetic algorithm search procedure, population evolves generation by generation to converge to an optimal or near optimal solution.

1) Encoding Cheng analyzed the advantages and disadvantages of nine encoding schemas for classical job shop scheduling[7]. In this paper, each gene represents a transition and chromosome represents the transitions firing sequence. Encoding of transitions firing sequence can be carried out by using natural numbers. To be specific, all transitions in the sub module are encoded by the same number which is different from other sub modules, and every transition can be distinguished from each other by order of number in chromosome.

# Table 1. Encoding Schema of Chromosme

| Process | 1-1 | 2-1 | 1-2 | 2-2 | 2-3 | … |
| --- | --- | --- | --- | --- | --- | --- |
| Transition |  |  |  |  |  | … |
| Chromosome | 1 | 2 | 1 | 2 | 2 | … |

Suppose that two instances of aero-engine module  and  are operated in work shop concurrently, then genes must be either “1” or “2”. For example, as shown in table 1. if transitions in sub module of  are described as , , …, then the first “2” must represents , and the later must represents , the rest may be deduced by analogy.

2) Selection Single aero-engine maintenance scheduling aims for minimal makespan, therefore those chromosomes with minor scheduling makespan owned more fitness. Suppose that there are  individuals in the generation , for each chromosome , its fitness is calculated from:

(5)

where  is a compensate value to prevent the fitness from being zero,  and  are the maximal and minimal makspan values of individuals from  respectively. If the individuals of next generation are chosen by roulette, then those fitter ones will survive at higher possibility.

If multiple aero-engines are operated in work shop concurrently, the fitness is multi-objective function. According to weighted sum approach proposed by Tasahiko, the weighted fitness function  is defined as follows:

(6)

where  is the number of aero-engines,  is the fitness function of  chromosome,  is the weighted factor of  chromosome.

3) Crossover Illegal chromosomes maybe results from ordinary crossover operation, to avoid which a new crossover operation strategy is proposed. To be specific, first dividing the components’ numbers into two subsets named  and ,  and making sure that the intersection of the two subsets is empty, then scan the two father chromosomes and let son chromosome be:

(7)

where  represents the projection of  from  to subset , finally exchanging with, a new son chromosome is produced after repeating the operation above.

4) Mutation Mutation is fairly straightforward. The procedure is to exchange two genes in chosen chromosome randomly.

4 Rolling Horizon Based Dynamic Schduling

Aero-engine maintenance is a dynamic procedure and may be interrupted by stochastic events unexpected, therefore seeking for dynamic scheduling strategies adaptive to the alteration seems to be necessary considerably. Obviously, it is robust and sensitive to unexpected events, which differs from static scheduling.

# 4.1  Rolling Horizon and Scheduling Sub Module

Inspired by the rolling horizon optimization for the predictive control technology, Fang Jian proposed a period and event-driven rolling horizon scheduling strategy, which means scheduling objects are those components included in rolling horizon[8]. In this paper, corresponding definitions about rolling horizon in timed colored Petri nets are defined as follows:

Definition  5 (Rolling horizon). Rolling horizon  is defined as the subset of colors of the merged timed colored resource sharing module , that is . The color set number of rolling horizon  is called capacity.

Definition 6 (Dynamic scheduling sub module). For sub nets  of ,  which satisfies: (1) ; (2) ; (3) if , and , let; (4) if , and , let ,  is defined as the dynamic scheduling sub module of  corresponding to Rolling horizon  .

There are two ways to construct scheduling sub module: one is to reconstruct the module by “bottom-up modelling” and keep the marking of operation places and resource places unaltered in , the other is to decomposed the merged  into two sub ones and one of whose color set is rolling horizon. The scheduling sub module is the reduction of merged system and used to dynamic scheduling.

# 4.2  Rescheduling Driven by Events and Period

There are two strategies for rescheduling: continuous scheduling and periodical scheduling. The former executes rescheduling once events emerges, which can cope with unexpected events, while the latter executes rescheduling periodically. In this paper, a hybrid strategy is adopted. Some key events including new project arriving, due date changing and machine breaking down are defined as following. If any key event takes place, then executes rescheduling, else executes rescheduling periodically.

1) New components Arriving New instances should be added to module, which means new colors should be added to color set of  merged , that is , , and keep the sate of processed and processing components unchanged, that is , :  .

2) Changing of due date  Suppose that is the makespan of  chromosome,  is the weighted factor of  chromosome, if the variation value of  is , then  should be adjusted, let   and the weighted fitness function  should be adjusted accordingly.

3) Machine  breaking down   If a machine breaks down while machining, then remove the corresponding colored token kept by transition and keep the colored tokens’ number  in resource places unchanged, else if the machine is idle and becomes unusable, then let  . If the broken down machine is recovered and becomes usable, the let , where ,  is the mapping function from machines to resource places.

5 Case Studying

Assembly workflow of aero-engine is shown in Figure 1, eight modules of aero-engine at the most left denote branches in the assembly procedure where each branch means one part of engine. Each part of an aero-engine is machined, balanced and assembled. In addition, blocks with the same name denote the same type of machine. The number above a block means the operation time of the operation on this machine. Arrows means sequence of operations.

# Figure 1. Aero-engine assembly workflow

Aero-engine assembly module represents by Petri nets is shown Figure 2. The mapping procedures from workflow can be described as follows: firstly the Resource Shared Modules of HPC, T2N, HPTR, HPCR, LPT, CRF, AGB, FAN are constructed respectively according to the workflow of each module, then merge all eight Resource Shared Modules by shared composition.

Figure 2. Petri nets module of aero-engine assembly

As shown in Figure 3. we choose 3 aero-engines situation with starting simultaneously. The rationality of Petri nets is verified by three aspects: (1) All processes follow the sequence of workflow strictly. (2) All processes are executed one by one without overlapping. (3) All processes are executed as closely as possible, which reduce the running time and increase the efficiency of utilization of machines.

# Figure 3. Static scheduling result for 3 aero-engines

From static scheduling result, for 1PstP aero-engine it takes 174.7 hours to accomplish the assembly procedure, while it takes only 366.4 hours for the 3 aero-engines. This is because the total time duration of aero-engines is only regarding the path which require the longest operation time. We maximize the utility of critical machines to minimize the time duration of processes operated on them. Thus, the makespan is not proportional to the number of aero-engines.

6 Cconclusion

To cope with the problem of concurrency and asynchrony of multiple aero-engines maintenance, shared composition method of Petri net is adopted to realize bottom-up modelling. The constructed model characterizes interactions between components with different processing routines and machine resources. Genetic algorithm is adopted to arrange firing sequence of transitions for static scheduling. To deal with discrete events emerge in workshop, a dynamic scheduling strategy uses rolling horizon composed by colors is presented, which made the model more adaptive and robust.

# Acknowledgments

The authors also wish to acknowledge the financial support of the National Natural Science Foundation of China(60373102, 60572174).

Correspondence to: Xinmin Tang

School of Mechatronics Engineering

Harbin Institute of Technology, Harbin

Heilongjiang 150001, China

Telephone: 01186-451-8641-3847

E-mail: txmofhit@hit.edu.cn

References

- P. Samaranayake, Development of engineering structures for scheduling and control of aircraft maintenance, International Journal of Operations & Production Management 2002;22(8): 843-867.

- Junyu Chen, The Study of Maintenance Scheduling in Aviation Engines, National Chiao Tung University, Taiwan, 2003: 9-12.

- Mu Der Jeng, Frank DiCesare, Synthesis Using Resource Control Nets for Modelling  Shared-Resource Systems, IEEE Transactions on Robotics and Automation 1995; 11( 3):317-327.

- Claude Girault, Rüdiger Valk, Petri Nets for Systems Engineering A Guide to Modelling , Verification, and Application, Springer-Verlag Berlin Heidelberg, 2003:214-215.

- Jiang Changjun, Dynamic constancy of Petri nets, Science in China( Series E) 1997; 27(6):567-573.

- Zhonghua Huang, Zhiming Wu, Deadlock-Free Scheduling Method for Automated Manufacturing Systems Using Genetic Algorithm and Petri Nets, Proceedings of the 2004 IEEE International Conference on Robotics & Automation 2004;566-571.

- Pan Quanke, Multi-Objective Scheduling Optimization of Job-shop in Intelligent Manufacturing System, Nanjing University of Aeronautics and Astronautics, Nanjing, 2003:20-25.

- Fang Jian, Xi Yugeng, “The Genetic Algorithms-Based Rolling Horizon Scheduling Strategy,” Control Theory and Appliciations 1997;14(4):589-594.