Daily groundwater level fluctuation forecasting using soft computing technique

Azhar K. Affandia＊and Kunio Watanabe a

aGeosphere Research Institute of Saitama University, Shimo Okubo 255, Sakura-ku, Saitama 338-8570, Japan

*Corresponding author:

Mr. Azhar K. Affandi

Geosphere Research Institute

Saitama University

255 Shimo-okubo, Sakura-ku, Saitama-shi, Saitama-ken

338-8570, JAPAN

E-mail address:　azhar_affandi@yahoo.com

Phone:	+81-48-858-3568

Received: 5/14/2007

Daily groundwater level fluctuation forecasting using soft computing technique

Azhar K. Affandia and Kunio Watanabe a

aGeosphere Research Institute of Saitama University, Shimo Okubo 255, Sakura-ku, Saitama 338-8570, Japan

ABSTRACT: The study presented here deals with forecasting daily groundwater level fluctuation (GLF) for monitoring of GLF pattern. The calculation model is based on adaptive neuro-fuzzy inference system (ANFIS) and two algorithms of artificial neural network model (ANN) models namely Levenberg-Marquardt (LM) and radial basis function (RBF). The objective in this study is to predict daily GLF for monitoring purpose. The first step was to investigate the effect of input time lag for one day ahead prediction using ANFIS algorithm. It was founded that three input variables including three time-lag gave a good prediction results. The second experiment was to predict the GLF one to seven step ahead using the three input variables. In this experiment the three algorithms were applied. The results indicate that the performances were decreasing by increasing the time step ahead and in general there was no significant different between that three algorithms used. The best accuracy was for one day ahead prediction. The results obtained in this study suggest that GLF monitoring can be conducted by forecasting model with some time-lag as inputs.

Key words: groundwater level fluctuation, forecasting, soft computing, artificial neural network, Levenberg-Marquardt, radial basis function, adaptive neuro-fuzzy inference system.

INTRODUCTION

Groundwater is a highly valuable resource.  Groundwater is used for many purposes such as agriculture, domestic and industrial use by constructing and operating extraction wells. Measurement and analysis of groundwater level is needed for sustainability and maintaining the groundwater availability. Groundwater level modeling is important for environmental protection: maintaining the groundwater equilibrium system, controlling groundwater level fluctuation and against severe land subsidence. Groundwater management approaches based on a variety of simulation and prediction techniques and control measures have been proposed and adopted by researchers and relevant authorities to address the problem of providing long-term countermeasures against land subsidence and protection of groundwater resources. Recently, groundwater level fluctuation (GLF) analysis by means of forecasting or prediction has increased.

A common nonlinear method usually used is artificial neural networks (ANN). Many kinds of algorithms for training the network have been performed for GLF forecasting. A significant advantage of the ANN approach in system modeling is that one need not have a well-defined physical relationship for systematically converting an input to an output (Nayak et al., 2004). There have been various papers considering the application of the ANN technique in water resource problems. In surface hydrology, ANN applications have been used for runoff analysis (Gautam et al., 2000; Zhang & Govindaraju, 2003; Parida et al., 2006), rainfall forecasting (Luk et al., 2000; Toth et al., 2000; Trafalis et al., 2002; Ramirez et al., 2005), rainfall-runoff model (Sajikumar and Thandaveswar, 1999; Chiang et al., 2004; Lin & Chen, 2004; Rajurkar et al., 2004; Chen & Adam, 2006) and stream flow forecasting (Wang et al., 2006). In a groundwater domain, ANN was used for groundwater reclamation (Ranjithan et al., 1993), a groundwater management (Coppola et al., 2003; Rao et al., 2003; Zaheer & Bai, 2003). Several papers have reported the use of ANN for groundwater level forecasting (Coulibaly et al., 2001; Daliakopoulos et al., 2005; Lallahem et al., 2005; Nayak et al., 2006). Gautam et al. (2004) reported that the groundwater table change between before and after a bridge pier construction could be well analyzed by ANN and pointed that the ANN will be used for the monitoring of groundwater. ANN model is a non-linear model and as many previous researchers have pointed out, this model is a powerful tool to estimate a fluctuation of groundwater level from other input data.　A detail concept and application of ANN in hydrology can be found in Govindaraju (2000a, b) and in Maier & Dandy (2000).

The application of a more promising soft computing technique, fuzzy inference system (FIS) recently is increasing in hydrological problem. There were several applications of a fuzzy rule-based theory in hydrology. Lu and Lo (2002) used self-organizing maps (SOM) and the fuzzy theory for diagnosing reservoir water quality. Tayfur et al. (2003) developed fuzzy logic algorithms for estimating sediment loads from bare soil surface. Wong et al. (2003) predicted volume of rainfall using SOM, BPNN and fuzzy rule systems. Alvisi et al. (2006) forecasted water level using fuzzy logic and ANN.

The combination of ANN and FIS, namely adaptive neuro-fuzzy inference system (ANFIS), has advantages in computational framework. The learning capability of ANN can be used effectively for automatic fuzzy if-then rule generation and parameter optimization (Nayak et al., 2004). Several researchers have used the ANFIS hydrology. Ponnambalam et al. (2003) used ANFIS for minimizing variance of reservoir systems operation. Nayak et al. (2004) applied ANFIS to hydrologic time series modeling. Kisi (2005) investigated the ability of ANFIS and ANN to model the streamflow-suspended sediment relationship. Chang and Chang (2006) used ANFIS to construct a water level forecasting system during flood period. Tutmez et al. (2006) developed ANFIS model for groundwater electrical conductivity based on the concentration of positively charged ions in water.

Most of the previous researches analyzed monthly GLF. However, in this paper we propose to predict daily GLF. The daily GLF time series from two observation wells in Saitama city, Japan were used as a case study. The groundwater in the study is abstracted from multi layer aquifer and the aquifer layer system cannot be clearly defined. The main objective of this paper is to develop a reliable groundwater level fluctuation forecasting system to generate trend forecasts for the forthcoming monitoring and management period based on observed data using ANFIS and ANN technique. The ANN model using backpropagation with Levenberg- Marquardt (BP-LM) and radial basis function (RBF) algorithms were developed.  The daily GLF of the past two years and two months was used as dataset.

MATERIAL AND METHODS

- Artificial neural network

An artificial neural network (ANN) is different from a conventional system such as an analytical or statistical model. ANN is a network consisting of an arbitrary number of very simple elements called nodes. Each node is a simple processing element that responds to the weighted inputs it receives from other nodes (Lee et al., 2004). The arrangement of the nodes is referred to as the network architecture. There are several types of ANN architecture and algorithms have been successfully used for solving groundwater level forecasting (Coulibaly, 2001; Daliakopoulos, 2005). The feed-forward neural network with Levenberg-Marquardt algorithm (LM) and radial basis function (RBF) will be presented.

Feed-forward neural network

A common type of feed-forward neural network (FFNN) consists of three layers: an input layer is connected to a hidden layer, which is connected to an output layer (Figure 1).

Input GLF X1		d

X2

X3                                                                                             	 Target

X4                                                                                          	   GLF

X5

Input Layer	     Hidden Layer               Output Layer

Bias node

Figure 1. Topology three-layer feed forward Artificial Neural Network

During this operation each node j receives incoming signals from every node i in the previous layer. Each incoming signal (yi) associates with a weight (wji). The net input, xj, to node j is a sum of the incoming signal times the weight as described in equation 1.

(1)

Note that this includes an extra node it calls the bias node, which is assumed to have a value of 1 at all times. The weight on this extra node is called the bias as a threshold value.

The output signal yj, which is a non-linear function, is produced by a transfer function of its input. The most commonly used transfer or activation function is the logistic sigmoid and hyperbolic tangent functions. In this study, the logistic sigmoid (eq. 2) transfer function is used as activation function between input layer and hidden layer, while linear function is used between hidden layer and an output layer.

(2)

The nonlinear nature of this tangent transfer function plays an important role in the performance of the ANN. Other functions can be used as long as they are continuous and possess a derivative at all points.

The backward pass is concerned with error computation and weight update. The algorithm that is usually used in this operation is a backpropagation algorithm. Backpropagation neural networks (BPNN) were introduced by Rumelhart et al. (1986), and a good description of the BPNN in groundwater problems can be found in Ranjithan et al. (1993) and Govindaraju (2000a, 2000b), among others. In back a propagation algorithm, the difference between the actual output of the output layer and the desired output is backpropagated to the previous layer and the weights are adjusted. In this study, the weight and bias values update according to Levenberg-Marquardt (LM) algorithm. This process proceeds for the previous layer until the input layer is reached. The LM algorithm is widely applied to many different domains. This method work extremely well in practice, and is considered the most efficient algorithm. Like Quasi-Newton methods, the LM algorithm was designed to approach second order training speed without having to compute Hessian matrix. To update weights and biases, the LM algorithm uses an approximation of the Hessian matrix.

(3)

The W is weight and J is the Jacobian matrix that contains first derivatives of the network errors with respect to the weights and biases, the e is a vector of network errors, µ a scalar that controls the learning.

The Radial basis function network

The radial basis function (RBF) network consists of three layers same as BP namely input layer, a hidden layer or radial basis layer and an output layer or linear layer. The input layer collects the input information. The hidden layer consists of set a basis function, which apply nonlinear transformation to the input source. The most common transformation is Gauss function as the nonlinearity of the hidden nodes. The response of the j-th hidden node to xi is given by

(4)

where  is Euclidean norm, is the center of the basis function and ( is a positive constant that determines the width of the symmetric response of the hidden node.

The output values of the network are computed as linear combination of these basis functions (hidden nodes),

(5)

where wj  is the network connection weights and K is the number of hidden nodes

Assume that N samples of the signal are available for training. The center, cj, 1 ≤ j ≤ K, can be selected from the network training input xi, 1 ≤ i ≤ N. the weights can then be solved using the least square method.

The RBF networks have been widely used for nonlinear system identification because of its simple topological structure and its ability to reveal how　learning proceeds in an explicit manner (Lin & Chen, 2004). They have increasingly attracted interest for engineering applications due to their advantages over traditional multilayer perceptrons, namely faster convergence, smaller extrapolation errors, and higher reliability (Moradkhani et al., 2004). The architecture and training algorithms for radial basis function networks (RBF) are simple and clear.

- ANFIS

Fuzzy logic that is first introduced by Zadeh (1965) is about mapping an input space to an output space, and the primary mechanism for doing this is a list of if-then statements called rules. Fuzzy rule based modeling is qualitative modeling scheme where the system behavior is described using a natural language (Nayak et al., 2004). All rules are evaluated in parallel, and the order of the rules is unimportant. The rules refer to variables and the adjectives that describe those variables. The fuzzy components or steps, in general, are inputs fuzzification, fuzzy operator, implication method, aggregate all output, and defuzzification.

FIS is based on the concept of fuzzy set theory and fuzzy reasoning. It is a method that interprets the values in the input vector and, based on some set of rules, assigns values to the output vector. There are two types of fuzzy rule system that are widely used and those are proposed by Namdani (1974) and Takagi-Sugeno (1985). Takagi-Sugeno has been adopted for ANFIS used in this paper.  The Takagi-Sugeno method uses a composite procedure for fuzzy inference and output defuzzification (Alvisi et al., 2006).

ANFIS was proposed by Jang (1993). ANFIS is fuzzy system that is trained by a training algorithm derived from neural network theory. The training algorithm is a hybrid training algorithm based on backpropagation and the least squares approach. In this algorithm, the parameters defining the shape of the membership functions are identified by backpropagation algorithm while the consequent parameters are identified by the least squares method. An ANFIS can be viewed as a special 3 layer feedforward neural network. The first layer represents input variables, the hidden layer represents fuzzy rules, and the third layer is an output.

RESULT AND DISCUSSION

This paper is dealing with the problem investigating two schemes of ANFIS and ANN models for GLF forecasting. Records of daily GLFs were compiled from observation wells in case study area for last two years and two month (2003 to 2005). Two observation wells were analyzed. The daily GLFs were missing for several days, which were interpolated using cubic spline method. In order to ensure that all variable get equal attention during calculating process, they should be standardized (Maier and Dandy, 2000). By this consideration, the inputs and output were scale in the range of 0 to 1 by normalizing with respect to minimum and maximum data before feeding into the calculation model. The training dataset of 730 daily records was used to train the data to obtain parameters. Other dataset consisting of 60 daily records was used as testing dataset. The first set of analyses examined the impact of adding time lag by applying seven models input (Model 1 to Model 7) on the ANFIS model for Urawa1 and Urawa2 data records. The performances of simulated outputs were evaluated based on the goodness of fit statistic such as root mean square error (RMSE), mean absolute error (MAE), mean relative error (MRE) and deterministic coefficient (R2). The RMSE statistic measures the residual variance that show global goodness of fit between calculated and observed GLF. The mean absolute error is the average of the absolute of the residuals. The mean relative error measures the accuracy that less sensitive for the outlying values than the RMSE. The coefficient determination (r-square) is the ratio of the explained variation to the total variation. It represents the percent of data (observed-predicted) that is the closest to the line of the best fit.

Table 1 shows the performance result obtained in training and testing period of the ANFIS model. The experiment showed that the R2 values became higher with additional time lag for training period. However, there were the biggest R2 values for Model 2 and Model 3 on Urawa2 and Urawa1 during testing period, respectively. The RMSE values were never achieve 0.17 meter during training and testing period for all models studied. The biggest RMSE was 0.165 m for Model 1 in training period and 0.159 for Model 7 in testing period. It can be seen from the calculating results that Model 2 and Model 3 have highest R2 in testing period for Urawa2 and Urawa1, respectively. They have not so much difference in R2 or RMSE values. For further analysis, we suggested to use Model 2 to compare the performance of ANFIS with two ANN models (LM and RBF). The GLFs predictions from one to seven ahead (daily) have been performed.

Table 1.The performance of ANFIS models during training and testing period

| Model | Training | Testing |
| --- | --- | --- |
|  | RMSE | R2 | RMSE | R2 |
| Urawa1 |
| 1 | 0.165 | 0.972 | 0.139 | 0.799 |
| 2 | 0.161 | 0.973 | 0.137 | 0.805 |
| 3 | 0.155 | 0.975 | 0.134 | 0.814 |
| 4 | 0.144 | 0.978 | 0.138 | 0.805 |
| 5 | 0.131 | 0.982 | 0.145 | 0.791 |
| 6 | 0.114 | 0.986 | 0.151 | 0.779 |
| 7 | 0.099 | 0.990 | 0.159 | 0.755 |
| Urawa2 |
| 1 | 0.115 | 0.980 | 0.077 | 0.934 |
| 2 | 0.110 | 0.982 | 0.075 | 0.941 |
| 3 | 0.105 | 0.983 | 0.077 | 0.938 |
| 4 | 0.100 | 0.985 | 0.079 | 0.936 |
| 5 | 0.094 | 0.987 | 0.078 | 0.938 |
| 6 | 0.085 | 0.989 | 0.077 | 0.938 |
| 7 | 0.074 | 0.992 | 0.079 | 0.932 |

Figure 2 shows the comparison results of three soft computing models using input Model 2 in testing period. The general tendency of predictions shows that the determination coefficient (R2) values decreases when predicting time-step increase and the prediction of one day ahead has the biggest R2 values. It can thus be suggested that the model is good to predict one step ahead. The statistics indices of one day ahead prediction are presented in Table 2. The maximum value of mean absolute error (MAE) was 0.275 meter using LM algorithm for Urawa1 in training period. The mean relative error (MRE) values were not achieving 1.75 % in testing period. The determination coefficients (R2) were good. It is clear that the soft computing approach have high predicting power.

Figure 2. Comparison results of three different algorithms for lead time prediction using input Model 2.

Figure 3 show the results of one day ahead prediction and observed GLF in testing period using Model 2.  The most striking result to emerge from the calculation is that there are no significant different results of the three algorithms used. All predicted values tend to slightly underpredict groundwater level. Underpredict defines that predicted value shallower depth than observed, overpredict is deeper than observed. The maximum positive deviation was 0.3746 meters for Urawa 1 using RBF algorithm and the maximum negative was 0.2938 meters for Urawa 1 using LM algorithm.  It is observed that the prediction errors are falling around ± 0.2 meters. It can be seen from Figure 4 that the predicted results, 85 % are satisfactory. Based on these results founded, we can predict or monitor daily groundwater fluctuation with considering some time lag feeding to the model.

Table 2. The performance of LM, RBF and ANFIS models during training and testing period

| Algorithms | Training | Testing |
| --- | --- | --- |
|  | MAE | RMSE | MRE | R2 | MAE | RMSE | MRE | R2 |
|  | Urawa1 |
| LM | 0.275 | 0.517 | 3.523 | 0.897 | 0.117 | 0.141 | 1.748 | 0.781 |
| RBF | 0.132 | 0.164 | 1.865 | 0.972 | 0.112 | 0.138 | 1.671 | 0.801 |
| ANFIS | 0.130 | 0.161 | 1.832 | 0.973 | 0.112 | 0.137 | 1.663 | 0.805 |
|  | Urawa2 |
| LM | 0.088 | 0.110 | 0.913 | 0.982 | 0.059 | 0.073 | 0.622 | 0.941 |
| RBF | 0.089 | 0.112 | 0.930 | 0.981 | 0.060 | 0.075 | 0.637 | 0.938 |
| ANFIS | 0.088 | 0.110 | 0.916 | 0.982 | 0.060 | 0.075 | 0.632 | 0.941 |

CONCLUSION

This study has demonstrated the potential applicability of soft computing technique for groundwater level estimation. The groundwater level prediction for this study was done with two scenarios. First stage was one day ahead prediction with time lag input models using ANFIS algorithm. It was found that Model 2, (t, t-1, t-2) input model, gave satisfactory prediction result. The advanced study was to predict groundwater level fluctuation for seven time step ahead using input Model 2. In this second stage, we compared three soft computing technique that were ANFIS, LM and RBF algorithms. It was found that the tree algorithms had not so significant in prediction results. In general, the results showed that the prediction accuracy was decay by increasing time step ahead with the best accuracy was for one step ahead. It was also founded that predicted values were close to the observed ones and 85 % felt in the range of ± 0.2 meters. Overall these results provide evidence of the applicability of the three soft computing algorithms for daily groundwater level prediction with high accuracy. The main contribution of this paper is to predict and to monitor a daily groundwater level using time lag as an input model. Further studies are recommended, especially using much more number of observation wells to cover regional and more comprehensive analyses. Furthermore, the number of data samples is needed to assess the influence on the long term tendency of groundwater level.

Figure 3. Comparison between observed and predicted GLF using ANFIS during testing period for input Model 2.

Figure 4. One day ahead prediction deviation from observed GLF during testing period.

Correspondence to: Azhar K. Affandi

Geosphere Research Institute Saitama University,

255 Shimo-okubo, Sakura-ku, Saitama

338-8570, JAPAN

E-mail address: azhar_affandi@yahoo.com

Phone:	+81-48-858-3568

ACKNOWLEDGEMENTS

This research is supported by Technological and Professional Skills Development Sector Project (TPSDP), Directorate General of Higher Education, Ministry of National Education, the Republic of Indonesia. The authors are grateful to Government of Saitama Prefecture, Japan for providing the valuable data and giving us permission for publication.

REFERENCE:

Alvisi, S., Mascellani, G., Franchini, M. And Bardossy, A. (2006) Water level forecasting through fuzzy logic and artificial neural network approaches. Hydrology and Earth System Sciences 10: 1-17.

Chang, F.-J. And Chang, Y.-T. (2006) Adaptive neuro-fuzzy inference system for prediction of water level in reservoir. Advances in Water Resources 29: 1-10.

Chen, J. and Adam B.J. (2006) Integration of artificial neural networks with conceptual models in rainfall-runoff modeling. Journal of Hydrology 318: 232-249.

Chiang, Y.-M., Chang, L.-C. and Chang F.-J. (2004) Comparison of static-feedforward and dynamic-feedback neural networks for rainfall-runoff modeling. Journal of Hydrology 290: 297-311.

Coppola, E., Poulton, M., Charles, E., Dustman, J. and Szidarovszky, F. (2003) Application of artificial neural networks to complex groundwater management problem. Natural Resources Research 12: 303-320.

Coulibaly, P., Anctil, F., Aravena, R. and Bobée, B. (2001) Artificial neural network modeling of water table depth fluctuations. Water Resources Research 37(4): 885-896.

Daliakopoulos, L.N., Coulibalya, P., Tsanis, I.K. (2005) Groundwater level forecasting using artificial neural networks. Journal of Hydrology 309: 229-240.

Gautam, M.R., Watanabe, K. and Saegusa, H. (2000) Runoff analysis in humid forest catchment with artificial neural network. Journal of Hydrology 235: 117-136.

Gautam, M.R., Watanabe, K. and Ohno, H. (2004) Effect of bridge construction on floodplain hydrology-assessment by using monitored data and artificial neural networks models. Journal of Hydrology 292: 182-197.

Govindaraju, R.S. (2000a) Artificial neural networks in hydrology. I: Preliminary concepts. By the ASCE task Committee on application of artificial neural networks in hydrology. Journal of Hydrologic Engineering 5: 115–123.

Govindaraju, R.S. (2000b) Artificial neural networks in hydrology. II: Hydrologic application. By the ASCE task Committee on application of artificial neural networks in hydrology, Journal of Hydrologic Engineering 5: 124-137.

Jang, J.S.R. (1993) ANFIS: Adaptive network based fuzzy inference system, IEEE Trans. On System, Man, and Cybernetics 23(3): 665-685.

Kisi, O. (2005) Suspended sediment estimation using neuro-fuzzy and neural network approaches. Hydrological Sciences Journal 50(4): 683-696.

Lallahem, S., Mania, J., Hani, A. and Najjar, Y. (2005) On the use of neural networks to evaluate groundwater levels in fractured media. Journal of Hydrology 307: 92-111.

Lee, S., Ryu, J.H., Won, J.S. & Park, H.J. (2004) Determination and application of the weights for landslide susceptibility mapping using an artificial neural network. Engineering Geology 71: 289-302.

Lin, G.-F. and Chen, L.-H. (2004) A non-linear rainfall-runoff model using radial basis function network. Journal of Hydrology 289: 1-8.

Lu, R.-S. and Lo, S.-L. (2002) Diagnosing reservoir water quality using self-organizing maps and fuzzy theory. Water Research 36: 2265-2274.

Luk, K.C., Ball, J.E. and Sharma, A. (2000) A study of optimal model lag and spatial inputs to artificial neural network for rainfall forecasting. Journal of Hydrology 227: 56-65.

Maier H.R. and Dandy G.C. (2000) Neural networks for the prediction and forecasting of water resources variables: a review of modelling issues and applications, Environmental Modelling and Software 15(1): 101-124.

Moradkhani, H., Hsu, K.-L., Gupta, H.V. and Sorroshian, S. (2004) Improved streamflow forecasting using self-organizing radial basis function artificial neural networks. Journal of hydrology 295: 246-262.

Namdani, E.H. (1974) Appplication of fuzzy algorithm for control of simple dynamic plant, Proc. IEEE 121:1585-1889.

Nayak, P.C., Sudheer, K.P., Rangan, D.M. and Ramasatri, K.S. (2004) A neuro-fuzzy computing technique for modeling hydrological time series, Journal of Hydrology 291: 52-66.

Nayak, P.C., Rao, Y.R.S., and Sudheer, K.P. (2006) Groundwater level forecasting in a shallow aquifer using artificial neural network approach. Water Resources Management 20: 77-90.

Parida, B.P, Moalafhi, D.B. and Kenabatho, P.K. (2006) Forecasting runoff coefficients using ANN for water resources management: The case of Notwane Catchment in Eastern Botswana. Physics and Chemistry of the Earth 31: 928-934.

Ponnambalam, K., Karray, F. and Mousavi, S.J. (2003) Minimizing variance of reservoir systems operations benefits using soft computing tools. Fuzzy sets and systems 139: 451-461.

Rajurkar, M.P., Kothyari, U.C. and Chaube, U.C. (2004) Modeling of the daily rainfall-runoff relationship with artificial neural network. Journal of Hydrology 285: 96-113.

Ramelhart, D.E., Hinton, G.E. & Williams, R.J. (1986) Learning representations by back-propagation error. Nature 323: 533-536.

Ramirez, M.C.V., Velho, H.F.de C. and Ferreira, N.J. (2005) Artificial neural network technique for rainfall forecasting applied to the Sao Paulo region. Journal of Hydrology 301: 146-162.

Ranjithan, S., Eheart, J.W. & Garrett, J.H. (1993) A neural network-based screening for groundwater reclamation under uncertainty, Water Resources Research 29: 563-574.

Rao, S.V.N., Thandaveswara, B.S., Bhallamudi, M.S. and Srinivasulu, V. (2003) Optimal groundwater management in deltaic regions using simulated annealing and neural networks. Water Resources Management 17: 409-428.

Sajikumar, N. and Thandaveswara, B.S. (1999) A non-linear rainfall–runoff model using an artificial neural network. Journal of Hydrology 216: 32–55.

Takagi, T. and Sugeno M. (1985) Fuzzy identification of systems its application to modeling and control, IEEE Trans. On System, Man, and Cybernetics 15(1): 116-132.

Tayfur, G., Ozdemir, S. and Singh, V.P. (2003) Fuzzy logic algorithms for ruoff-induced sediment transport from bare soil surfaces. Advances in Water Resources 26: 1249-1256.

Toth, E., Brat, A. and Montanari, A. (2000) Comparison of short-term rainfall prediction models for real-time flood forecasting. Journal of Hydrology 239: 132-147.

Trafalis, T.B., Richman, M.B., White, A. and Santosa, B. (2002) Data mining techniques for improved WSR-88D rainfall estimation. Computers & Industrial Engineering 43: 775-786.

Tutmez, B., Hatipoglu, Z. And Kaymak, U. (2006) Modelling electrical conductivity of groundwater using an adaptive neuro-fuzzy inference system. Computers & Geosciences 32: 421-433.

Wang, W., Van Gelder, P.H.A.J.M., Vrijling, J.K. and Ma, J. (2006) Forecasting daily streamflow using hybrid ANN models. Journal of Hydrology 324: 383 – 399.

Wong, K.W., Wong, P.M., Gedeon, T.D. and Fung, C.C. (2003) Rainfall prediction model using soft computing technique. Soft Computing 7: 434-438.

Zadeh, L.A., Fuzzy sets. Information and control 8(3): 338-353.

Zaheer, I. and Bai, C.-G. (2003) Application of artificial neural network for water quality management. Lowland Technology International 5(2): 10-15.

Zhang, B. and Govindaraju, R.S. (2003) Geomorphology-base artificial neural networks (GANNs) for estimation of direct runoff over watersheds. Journal of Hydrology 273: 18-34.