Physico-chemical analysis of treated distillery effluent irrigation responses on crop plants Pea (Pisum sativum)

And Wheat (Triticum aestivum)

Sandeep K.Pandey*1, Anil K. Gupta2 and M.Yunus3

environ_disaster53@rediffmail.com

Abstract

Physico-chemical properties of distillery effluent and their responses of different concentrations like 0%,25%,50%,75%&100% on crop plants i.e. pea and wheat were studied under field condition. Where waste water is ~acidic in nature with high dissolved salts and organic load, on subsequent dilution it is serving as liquid fertilizer up to 50% effluent concentration, >50% effluent concentration it is posing inhibitory effect on the tested crops, further work on marginal dilution are needed to substantiate the present study.

Key words: Distillery effluent, Physico-chemical parameters, Crop response parameters

Pisum sativum, Triticum aestivum.

1. Introduction:

Water pollution is prime cause of unavailability of the suitable water for irrigation purpose. Where agro-based industries are the most culprit. The total waste water produced per liter of alcohol production is around 40 to 50 liters (Vasanthy, et al., 2006). About 40.72 million/m3 spent wash is generated annually from distilleries in India, considerable amount of plant nutrients are available in distillery effluent like: N=1660 to 4200 mg/l, P=225 to 3038mg/l, K=9600mg/l Cl=7238 to 42096mg/l, Ca =2050 to 7000 mg/l, Mg = 1715 to 2100mg/l, SO4 = 240 to 425 mg/l. It also contains plant growth promoters like gibberellic acid

Authors:

1. Lecturer, Department of Environmental Science, P.G.College, Ghazipur,(U.P.),India.

2. Associate Prof.. National Institute of Disaster Management, IIPA campus, New Delhi. India.

3. Professor, Baba Sahib Bhim Rao Ambedkar University,Vidya Vihar,Lucknow,India.

(GA) and Indol acetic acid (IAA) nearly 3246 mg/l with good fertilizers value, it contains high BOD and COD and organic compounds like phenol, lignin, oil and grease which deteriorate the surroundings. Some compounds like endol, sketol and other sulphur compounds which not under goes effective degradation by yeast and methanogenic bacteria, are the cause of objectionable smell of distillery effluent (Murugaragavan, 2002). In water scarce situation effluent is single permanent water source for irrigation, consequently causes positive effect at lower concentrations in this relation studied has been carried out by (Rani, R., and Srivastava1990;Subramani 1995; Pandey et al., 2007) adverse effect on the plant and soil has been find on higher concentrations of the effluent . The present study is an effort to analyze the effluent’s physico-chemical parameters and their relative response on Pea and Wheat to speculate its suitability for irrigation purpose at their marginal dilutions.

2. Materials & Methods:

2.1 Study area

Ghazipur a suburban area of district headquarters, located in the eastern Gangetic plain of the Indian sub continent at 25019` and 25054` N latitude, 8304`and 83058`E longitude and 67.50 m above the sea level. The experiment was carried out between Oct 2000 to Jan 2001. This period of the year is characterized by mean monthly maximum temperatures between 18.6 and 34.1 0C and mean monthly minimum temperatures between 5.4 and 16.7 0C. Maximum relative humidity varied from 95% to 100% and minimum from 69% to 71%.

2.2 Selection of Seeds

Seeds of Wheat (Triticum aestivum) Var.K68 and Field Pea (Pisum sativum) Var. Swati (KFPD-24) were chosen for the experimental work both adoptive to the site of the study (Eastern U.P.) India, and recently developed and exceedingly espouse high yield varieties.

2.3 Experimental Design and Set up

Experiment was carried out on farmhouse near P.G.College, Ghazipur. Plot area about 24×15 feet. And individual replicates size was 3×3 feet there were five treatments and each treatment having 3 replicates in each, means whole area has been divided in to 40 plots, each plots have separated by 20 cm. deep bricks around the each plot boundary.  About 100 seeds of wheat and 50 seeds of pea with uniform size for each variety were selected for each plot, the seeds were surface sterilized in 5% sodium hypochlorite solution to remove the microbial contamination then seed were thoroughly washed with de-ionized water. The plots were prepared by proper tillage then seeds were sown in the plots and were irrigated with 5 litter of different concentrations of the distillery effluents like 0%, 25%, 50%, 75%&100% (here the distillery effluents are over diluted by the factory before discharge) at the interval of 5 days or as per its requirements, after 65 days plants were take-up and roots were very carefully wash to remove the soil particles along with constant safety of secondary roots.

2.4 Waste water analysis

The experiment was conducted at Department of Evironmental Science, P.G.College, Ghazipur where pH was measured with the help of pH meter (Model no. 101 E) of Electronic India, standardized with pH buffer 4, 7 and 9.2. T.D.S was estimated by evaporation method at 1800C, Alkalinity, B.O.D., C.O.D. Hardness, D.O., Chloride, CO2 and all parameters were analyzed by standard procedure mentioned in APHA (1995).

2.5 Estimation of Germination %, Root length, Shoot length and

No. of secondary roots, girth of plants, Leaf area and vigor index

Germination percentage was calculated by dividing the seed germinated on each day by total no. of seed taken × 100. And finally adding the total percentage. Root, and shoot length measured by normal scale of 150 mm size. Girth was measured by screw gauge; vigor index measured by Jain and Saha (1971), leaf area was measured using portable leaf area meter (Model LT 3100, LICOR).

2.6 Estimation of Chlorophylls

The chlorophyll contents of primary leaves were estimated with 80% acetone with help of spectrophotometer (Hitachi, Ltd. Tokyo). Jain and Saha (1971).

Chlorophyll a = (.0127) (OD663)-(.00269) (OD 645) gm/lit.

Chlorophyll b = (.0229) (OD 645) – (.00488) (OD 638) gm/lit.

Total chlorophyll = (.0202)(OD645)+( .00802) (OD 663) gm/lit.

2.7 Statistical analysis

The data were subjected to mean and one way ANOVA (analysis of variance) using SPSS ver. 10 software Ducan’s multiple range test performed to test the significance difference among the treatments.

3. Result:

S.No.   Parameters      Value           BIS

1         T0C                 38±.270C   400C

2         Color              Reddish      None

3         T.S.                4080±.07    2100

4         T.D.S.             3800±.08    2100

5         T.S.S.              280±.09      100

6         pH                   6.5±.08       5.5-9

7         T.Alk.             1437.5±.39    -

8         T.Hard            565±.05       300

9        Ca Hard.          455±.05         -

10        Calcium          182±.22        169

11        Chloride          875±.56        600

12         D.O.               <2                 4-6

13         B.O.D.           808±.76         30

14         C.O.D.           2020±.20      250

15          Na                1312±.50        -

16          EC                18±.9              -

(Mean±Stand.error)

Table-1:  Waste water analysis of treated distillery effluent.

Treatment  Percentage      Shoot        No. of        Girth of       Length of        No. of           Total           Chlorophyll Chlorophyll

Behavior   Germination  Length     Funcl. Leafs     Plant            Root           Seco.Roots  Chlorophyll           A                   B

(cm)                                  (mm)           (cm)                                   (mg/l)             (mg/l)            (mg/l)

Control        98±.11a      12.3±.11c        4±.57a     	    1.23±.0096c  8.85±.20b       5±.57b         .006377±037E-3c .00230±.012E-3c   .00388±.041a

25%         89±.33b      14.85±.16b   4±1.1a          1.56±.0097b  12.90±.0076a  6±1.1ab       .00833±.02E-3b    .00241±.014E-2c   .00519±.06a

50%         67±.57c       19.57±.57 a  4±.57a           2.45±.10a       9.19±.0086b  10±2a          .00986±.067E-3a  .0271±.049E-3a     .00724±.011b

75%         61±.66d       15.15±.45b  4±.57a            2.45±.005a    8.77±.0088b   9±1ab         .00608±.068E-3c   .0266±.062E-2a     .00388±.012a

100%        30±.00e       5.02±.56d    3±.57a            1.08±.006c    8.85±.125b     9±.57ab       .00550±.00d         .00835±.021E-2b  .00363±.012a

Different letters in each group shows significant difference at P<0.05 levels (Mean±Stand.error)

Table-2:  Effect of different dilution of treated distillery effluent on the growth parameters

and chlorophyll content of Wheat (Triticum aestivum).

Treatment  Percentage       Shoot    No. of           Girth of       Length of       No.of          Total             Chlorophyll   Chlorophyll

Behavior  Germination    Length    Funcl. Leaf     Plant           Root         Seco.Roots   Chlorophyll          A                    B

(cm)                               (mm)           (cm)                                    (mg/l)             (mg/l)            (mg/l)

Control   100±.00a        31.34±1.1b  27.42±.57a   1.547±.007a   7.0±.76a       13±.57bc     .00694±.03E-4c   .00134±.20E-5b .00388±.47E-5b

25%      98±1a            30.69±.26b  21.24±2.6b   1.40±.005ab   7.5±.76a       15.±.66b     .00852±.02E-4b .00281±.66E-5b .0035±.45E-4b

50%     89±.33b          36.32±1.7a  20.00±.00b    1.26±.006b    7.53±.00a     19±.00a      .0635±.07E-4a    .0945±.1E-3a     .0053±.15E-4a

75%     70±1.1c          31.60±.20b   19.28±.57b   1.47±.0056a  7.08±.39a     11±1cd        .00424±.08E-5d   .000138±.4E-5b .0027±.20E-4c

100%     65±1.5d          16.98±.13c   18.4±.3b       1.22±.0056b  6.9±.37a       10±1.1d      .00400±.00d       .000127±.8E-5b  .0022±.00c

Different letters in each group shows significant difference at P<0.05 levels (Mean±Stand.error)

Table-3:  Effect of different dilution of treated distillery effluent on the growth parameters and

chlorophyll content of Pea (Pisum sativum).

Treatment                    Vigor Index                                   Treatment                       Leaf area

Behavior                                                                               Behavior

Pea                        Wheat                                                       Pea (cm)2            Wheat (cm)2

Control          3014.40±3.3a          1306.50±2.3a                        Control           4.86±.009a                     27.5±.25d

25%               2359.60±1 b            1317.20±3.8a                       25%               4.48±.003b            38.48±.002b

50%              1861.693.5bc            1805.40±6.0a                       50%               3.96±.09c               47.30±.008a

75%              1738.00±2c              921.10±3.2ab                        75%              4.42±.007b            32.20±.41c

100%            439.00±2.6d             150.60±1.77b                       100%             2.02±.004d            24.7±.15e

Different letters in each group shows significant difference at P<0.05 levels (Mean±Stand.error)

Table-4: Reading of the vigor Index.                   Table-5: Reading of the leaf area

The waste water analysis results (Table-1) revealed that all the values of the different tested parameters are not compatible to the Bureau of Indian Standard (BIS). T.S. (Total Solid), T.D.S., T.S.S.values are nearly two times higher. The value of Total alkalinity and Total hardness are nearly one and half times higher compared to bureau of Indian standard. Value of the calcium is 182 about (7.69%) higher than BIS (169). Chloride’s value is 875 about (45.83%) more than BIS (600). BOD (Biological oxygen demand) value is 808 and COD value is 2020 extremely higher about 2593 % and 708% than BIS values respectively. D.O. level is very lower <2 than BIS value (4-6).

In plant responses tests, the treatments on wheat (Table-2), the entire maximum values of the plant response parameters achieved at 50% concentration of effluent, except germination, chlorophyll b and root length. Maximum value of root length and chlorophyll b achieved at 25% concentration and maximum germination achieved at control condition. In case of treatments on Pea (Table-3) the entire maximum values achieved at 50% concentration of effluent except germination percentage, no. of functional leaves and girth of plant. No. of functional leaf, girth of plant and germination achieved maxima at control condition.

In both plant response cases (pea and wheat) vigor achieved maxima at 50 % concentration effluent and gradually decreases on further elevation on concentration (Table-4). The leaf area of wheat achieved maxima at 50% concentration and in pea (Pisum sativum) maxima was at control condition (Table-5). Effect of growth retardation is significant (at .05 level of significance) and vigorous on elevated concentrations more than 50% concentration of the effluent as evident by the aforementioned tables, while in  number of functional leaves, root length and number of secondary roots (where the retardation is non significant at .05 level of significance).

Co-relation study revealed there is a positive correlation with increasing level of the effluent concentration up to 50% concentration of treated distillery effluent in case of Pea (Pisum sativum) and Wheat (Triticum aestivum) as shown in and Figures 1-6 and  7-12 respectively.

Figure 1. Co-relationship between varying levels of effluent concentrations and their responses on root

length of Pea.

Figure 2. Co-relationship between varying levels of effluent concentrations and their responses on shoot

length of Pea

Figure 3. Co-relationship between varying levels of effluent concentrations and their responses on

chlorophyll a of Pea   .

Figure 4. Co-relationship between varying levels of effluent concentrations and their responses on

chlorophyll b of Pea.

Figure 5. Co-relationship between varying levels of effluent concentrations and their responses on Total

chlorophyll of Pea

Figure 6. Co-relationship between varying levels of effluent concentrations and their responses on Vigor of

Pea.

Figure 7. Co-relationship between varying levels of effluent concentrations and their responses on root

length of Wheat.

Figure 8. Co-relationship between varying levels of effluent concentrations and their responses on shoot

length of Wheat.

Figure 9. Co-relationship between varying levels of effluent concentrations and their responses on

chlorophyll a of Wheat.

Figure 10. Co-relationship between varying levels of effluent concentrations and their responses on

chlorophyll b of Wheat.

Figure 11. Co-relationship between varying levels of effluent concentrations and their responses on total

chlorophyll  of Wheat.

Fig.:12. Co-relationship between varying levels of effluent concentrations and their responses on vigor

of  Wheat.

4. Discussion:

The extremely higher T.S. indicates that the effluent is very saline at the same time higher B.O.D and C.O.D indicates higher organic loads, the cause of the adverse effect on the germination is the higher salinity evident by the higher E.C value. The root growth at all levels (Non significant difference at .05 level of significance) indicates that it is not the heavy metals which has been retarding the growth parameters but the higher salinity and higher organic load, causing  a cumulative retardation effect on the growth and biochemical parameters of  the pea and wheat . The salinity in rhizosphere causes a higher osmotic pressure evident by higher electrical conductivity, it causes low wall pressure and deficit of suction pressure, causes narrowing of the water balance required. The lowering water balance lowering the respiration of the plants. While increase in the organic matter content in soil increase the biodegradation and elevates the CO2 level in rhizosphere, affecting the respiration. Three factors which governs the respiration of plants are CO2 level in soil, water supply and temperature here CO2 level in soil is higher, water is physiologically scarce and low temperature. These all coincide causing encumbrance in respiration, resultant is the adverse effect on physiological and biochemical parameters. The positive response on the growth parameters are at 25 to 50 % concentration of the effluent is probably due to effect of effluent as liquid fertilizer (Subramani et al., 1995). And as gradually the concentration raises growth retardation is vigorous. It is possibly due to excess of Nitrogen, Phosphate, Potassium, Sulphate, Calcium, and Chloride by affecting the water absorption and other metabolic process in plants

(Rani  and Srivastava ,1990; Chandra et al., 2002).Correlations study suggested that the ≤50 % concentration of distillery effluent having positive correlations with root length, shoot length, chlorophyll a, chlorophyll b, total cholorophyll, vigor, but the intra pigment dependencies are not certain for both pea and wheat plants. Still further work on marginal dilution is needed to substantiate the present study.

Acknowledgement: Author is thankful to the Head, Department of Environmental Science, P.G.College, Ghazipur for providing necessary facilities.

References:

APHA. (1995). American Public Health Association, Standered methods for examination of water and waste water, Seventeenth edition, Washington D.C.

Chandra Suresh, H. C. Joshi, H. Pathak, M. C. Jain and N. Kalra. (2002).Effect of potassium salts and distillery effluent on carbon mineralization in soil. Bioresource Technology 83, 3, pp. 255-257.

Jain, N.K. and J.R. Saha (1971) Effect of storage length on seed germination in jute (Corchorus spp.) Agro, J. 63 pp.631-636.

Murugaragavan, R. (2002) Distillery spent wash on crop production in dry land soil M.Sc. (Environmental science) Thesis, Tamil Nadu Agricultural University, Coimbatore, India.

Pandey, S.K., P.Tyagi and A.K. Gupta (2007) Physico-chemical analysis and effect of distillery effluent on seed germination of wheat (Triticum aestivum), pea (Pisum sativum) and lady’s finger (Abelmoschus esculentus). Journal of Agricultural and Biological Science.pp.35-40.

Renu Rani, R., and Srivastava (1990) Ecophysiological responses of Pisum sativum and Citrus maxima to distillery effluents. Indian Jr. of Ecology and Env.Sci. 16:pp.125-132.

Subramani,A., P.Sundermoorthy and A.S. Lakshmanachary. (1995). Effect of distillery effluent on growth, Yield and Productivity of Vigna rediata .Pollution Research 14(4) pp.477-482.

Vasanthy, M., C.Thamaraiselvi and N.Namatha (2006) Effect of untreated distillery effluent on growth characters of Brassica juncea. Pollution Research 25 (2) pp.363-365.

*Corresponding Author:

Lecturer, P.G. Department of Environmental Science, P.G.College, Ghazipur.

Telephone No.:+91-5497-252764, Mob. 09918561915.Fax No.:+91-548222087.

Email:environ_solutions@sancharnet.in.,environ_disaster53@rediffmail.com.