Coag-flocculation kinetics and functional parameters response of Periwinkle shell coagulant (PSC) to pH variation in organic rich coal effluent medium

M.C MENKITI1*, P.C NNAJI2, O.D ONUKWULI1

*CORRESPONDING AUTHOR

M.C MENKITI

M.ENG(CHEM ENGR) ,MSC (ENVIRONMENTAL MGT) LECTURER 1.

DEPARTMENT OF CHEMICAL ENGINEERING, NNAMDI AZIKIWE UNIVERSITY, AWKA, NIGERIA.

E-MAIL: cmenkiti @ yahoo.com

TELEPHONE: +234 8037441882

P.C NNAJI

M.ENG (CHEM ENGR) , EXECUTIVE ENGINEER 1,QUALITY CONTROL UNIT

ENUGU STATE WATER CORPORATION, ENUGU, NIGERIA

E-MAIL:patnnaji@yahoo.com

TELEPHONE: +234 8038679175

O.D ONUKWULI

M.ENG, PhD (CHEM ENGR) ,PROFESSOR

DEPARTMENT OF CHEMICAL ENGINEERING, NNAMDI AZIKIWE UNIVERSITY, AWKA, NIGERIA.

E-MAIL: onukwuliod@ yahoo.com

TELEPHONE: +234 80 63635864

Coag-flocculation kinetics and functional parameters response of Periwinkle shell coagulant (PSC) to pH variation in organic rich coal effluent medium

M.C Menkiti1, P.C Nnaji2, O.D Onukwuli1

1. Department of Chemical Engineering, Nnamdi Azikiwe University, Awka, Nigeria.

2. Enugu State Water Corporation, Enugu, Nigeria

ABSTRACT

The coag-flocculation performance of PSC as affected by pH variation in coal washery effluent has been investigated at room temperature using various dosages of unblended PSC. In addition, coag-flocculation parameters such as α, K, βBR, KR, εp and τ1/2 are determined. Turbidity measurement was employed using the nephelometric (turbidimetric) standard method while PSC preparation was adapted from the works of Fernandez-Kim. The maximum PSC performance is recorded at α of 2, K of 1.6667x10-3m3/ kg.s, dosage of 0.4kg/m3, pH of 6 and τ1/2 of 8.0s while the minimum performance is recorded at   α of 2, K of 8.833x10-5m3/ kg.s, dosage of 0.5kg/m3, pH of 10 and τ1/2 of 218s.The minimum value of coagulation efficiency, E (%) recorded is > 95% .In general, the computed parameters lie within range of previous works .The results obtained confirmed that the theory of fast coag-flocculation holds for coag-flocculation of the coal washery effluent using the coagulant investigated and at the conditions of the experiment.

Keywords:Coag-flocculation,Kinetics,CoalEffluent,Periwinkle shell,coagulation

INTRODUCTION

Traditionally ,coag-floculation is aimed at the removal of suspended colloidal particles when the stabilized colloids are aided to overcome their repulsive forces leading to the aggregation of the particles into flocs.(Ma et al ,2001;Di  Terrlizzi, 1994;Edzwald,1987;O’meila, 1978)

Among the factors that affect the process are raw effluent quality, temperature, pH, chemical and bacteriological parameters etc(jin,2005).

Coag-flocculation may be achieved by any of the common coagulants such as alum, lime etc. The coagulation behaviors of these common coagulants have been well investigated with little or no attention given to the coag-flocculation potential of many animal and plant derivatives. To this end, a focus is hereby given to the study on periwinkle shell as potential source of coagulant derivative. Periwinkle shell is a natural carbohydrate biopolymer derived by deacetylation of chitin, a major component of the shells of crustacean. (Fernadez-Kin, 2004).

PSC is a non-toxic, biodegradable and biocompatible polymer. Previous results obtained from the study on crustacean derived coagulants highlight promise of renewable polymeric materials with extensive application in removal of colloidal particles in wide range of effluent media (Fernandez-Kin, 2004)

However, in spite of the abundance of periwinkle in our local communities in Nigeria, little or no comprehensive work has been reported. Against this backdrop, this work endeavors to explore and generate interest in the utilization of periwinkle shell as coagulants. As a step in this direction, this work focuses on coagulation performance and kinetics of PSC under varying pH of coal washery effluent, a typical medium for this kind of study. Thus, if well developed, PSC can serve as a suitable replacement either in total or in part for the inorganic coagulants.

THEORETICAL PRINCIPLES AND MODEL DEVELOPMENT

The rate of successful collisions between particles of sizes i and j to form particle of size K is (Thomas et al, 1999; Jin, 2005):

Nij = εp β (i,j) ninj	                                                                                                                                                                                  …1	                                                                                                                            where Nij = the rate of collisions between particles of size i and j(mass concentration / time)

εp = collision efficiency

β(i,j) = collision factor between particles of size i and j

ninj = particle concentration for particles of size i and j, respectively.

Assuming monodisperse, no break up and bi particle collision , the general model for perikinetic coag-flocculation is given as (Swift and Friedlander 1964 ; Jin, 2005)

…2                      where      is the rate of change of concentration of particle of size K (concentration / time).  is a function of the coag-flocculation transport mechanism .The appropriate value of  for Brownian transport is given by Von Smoluchowski (1917):

…3

where    is  Boltzmann’s constant (J/K)

is Absolute temperature (K)

The generic aggregation rate of particles (during coagulation / flocculation) can be derived by the combination of equations 2 and 3 to yield:

…4

where  is total particle concentration at time, (mass / volume)

K is the  order  coag-floculation constant

is the order of   coag-floculation process

And                                                                                                                   …5

where   is collision factor for Brownian transport

Also,                                                                                                              …6

combining equations 4,5 and 6 produce:

….7

…8

where   is the Von smoluchowski rate constant for rapid coagulation (Van Zanten, et al 1992)

However                                                                                                        ….9

….10

where     is particle diffusion coefficient

is particle radius.

From Einstein’s equation:                                                                             …11

From Stroke’s equation   :                                                                                 ….12

where B is the friction factor

η  is the viscosity of the fluid 							                                         combining equations 9 and 11 give:

...13

combining equation 12 and 13 give:

…14

Putting equation 10 in 14 yields:

…15	                     combining equations 8 and 15 give:

…16

Comparing equations 4 and 16 show:

...17

For perikinetic aggregation,  theoretically equals 2 as would shown below (Fridrikhsberg, 1984; Hunter, 1992):

From Fick’s law,

..18

Integrating equation 18 at initial conditions,:

...19

Therefore 	                                                                                      …20

It implies,

...21

Therefore                                                                                                    …22

...23

For central particle of same size undergoing Brownian motion, the initial rate of rapid coag-flocculation is:

…24

...25

at

Hence, from equation 25,

However in real practice, empirical evidence shows that in general (WST, 2003; Menkiti, 2007).Based on this , what is required to evaluate K is to determine the line of better fit between 1 and 2 while the experimental data are fitted into linearised form of equation 4.

Hence, for ,equivalence of equation 4 yields:

...26

Integrating within the limits, produces

...27

Equation 27 yields:

...28

...29

Plot of  vs. gives a slope of K and intercept of.

For; equivalence of equation 4 yields:

…30

Hence:

…31

...32

Plot of ln Vs  produces a slope of K and intercept of.

For the evaluation of coagulation period (), from Equation 32:

....33

...34

let                                                                                                              ...35

Hence:

…36	                                          When , equation 36 becomes

…37

Therefore as

Hence                                                                                              ...38

For Brownian aggregation at early stages (t≤30 minutes), equation 2 can be solved exactly, resulting in the expression (Holthof et al, 1996):

….39

Where

Therefore                                                                                   ....40

Let

Therefore 	                                                                                 ...41

Equation 41 gives a generic expression for particle of m-th order .Hence,

For singlets (m=1)

...42

For doublets (m=2)

….43

For triplets (m=3)

….44

Conversion of Turbidity (NTU) to TSS (mg/l) yields (Metcalf and Eddy,2003):

TSS (mg/l) = (TSSf).T                                                                                       ...45

Where T = turbidity (NTU)

(TSSf) =Conversion factor to TSS

EXPERIMENTAL METHODS

The procedure for processing of the periwinkle shell to coagulant is adapted from the work of Ferdinandez-Kin (2004).The jar test were conducted based on standard Bench Scale Nephlometric  Method for the Examination of water and waste water.(WST,2003;AWWA, 1985)

RESULTS AND DISCUSSION

The values of coag-flocculation reaction parameters are presented in tables 1 to 5.For the case of α =1, it is a shift from theoretical  expectation but in line with empirical evidence (WST,2003).Generally, the value of  α affects that of  K inversely .Since K is rate per concentration and K is associated with energy barrier (KT) , it is understandable that for higher α to be obtained , a lower  K is a necessary condition for such phenomenon (Fridkisberg,1984) .The K and α values are to a large extent consistent with previous works on Brownian coagulation (Van Zanten and Elimelechi,1992). K(=0.5βBR) values appreciably is less sensitive to a given pH as the dosage of PSC changes from 0.1kg/m3 to 0.5kg/m3.Variation in KR is generally minimal as presented in the tables 1 to 5 .This is because KR is a function of viscosity and room temperature both of which did not vary considerably during the study.

The discrepancies in α, K and KR are explained by the unattainable assumption that mixing of particles and coagulant throughout the dispersion is 100 % efficient before any aggregation occurs. The effect of this limitation will be local increases in particle ratios during the mixing phase given uneven distribution of particles / coagulant complexes. The complexity of this system makes it hard to have all the values of  α =2 .(Yates et al , 2001).Another account is the interplay between the van der waal  forces and the hydrodynamic interactions which typically reduces the theoretically predicted K by a factor of 2.However, since K also depends on the type of counter ion, additional short range forces represent the most likely explanation for any other remaining discrepancies (Holthof et al ,1997;Holthof et al ,1996).

At nearly invariant values of KR ,εp directly relates to 2K= βBR. The consequence is that high  εp results in high kinetic energy to overcome the zeta potential.The implication is that the double layer is either reduced or the colloids destabilized to actualize low τ1/2 in favour of  high rate of coagulation. The results show that high values τ1/2 corresponds to low εp and K, and indication of repulsion in the system.τ1/2 values lie within the range of previous works where milliseconds had been obtained. (Hunter, 1993).

TSS (Kg/m3) VS TIME PLOTS.

The TSS Vs time plots are presented in Figs 1 to 5.As single particles flocculate into large aggregates ,the turbidity of the dispersion decreases and the transmission intensity increases. This behavior simply reflects the complex dependence of turbidity on particle number (dropping) and particle size (increasing) over time (Yates et al, 2001).The consequence of this is the highest rate of coagulation usually recorded at the early time of the coag-flocculation process. This is supported by τ1/2 that lies within seconds’ .Fig 1 to 5 indicate that the best coagulation was obtained at pH of 6.

EFFICIENCY, E (%) VS TIME

Plots of E (%) Vs time are presented in Figs 6 to 10 .The E illustrates the effectiveness of the PSC to remove turbidity from the effluent .the plots show that the least E > 95% ;supports the low values of τ1/2 .This justifies the theory of fast coagulation (Von Smoluchowski , 1917)which validates  the real life application of coagulation in which 90% of particle removal is usually achieved within the first five minutes of coag-flocculation .With the exception of Fig 8 ,the highest and lowest E were recorded for pH of 6 and pH of 10 respectively.

PLOT OF E (%) VS pH

This is presented in Fig 11.It indicates the performance of various doses of the PSC at varying pH. Interestingly, all the doses have a similar trend having their maxima at pH = 6 and minima at pH = 10.All the doses have the same E at pH of 2, indicating that the doses do not affect the efficiency at pH = 2.However, the optimum doses at pH = 6 is 0.4kg/m3 PSC.

PLOT OF E (%) VS DOSAGE (kg/m3)

This is presented in Fig 12.It confirms the observation made in Fig 11.The optimum dose is 0.4kg/m3 at pH = 6.However,it should be noted that between 0.1kg/m3 to 0.3kg/m3 PSC, pH = 2 gives a better performance .As already observed, pH  = 10 gives a poor performance for all doses.

PARTICLE DISTRIBUTION PLOTS:

These are presented in Fig 13 to 17; one for each of the tables 1 to 5 for the optimum K .The trend is similar for all the curves. The particle distributions expected in a typical coag-flocculation process are shown in these figures. It is notable that the curves Ni Vs t, beginning with twins (doublets), passes through a maximum because they are absent at the initial instant (t = 0, N2 = 0) and at the end of coag-flocculation process (t = α, N2=0). The number of primary particles (singlets) can be seen to decrease more rapidly than the total number of particles. For all consolidated particles, the curves pass through maxima whose height lowers with an increase consolidation.

The curves are expected in coag-flocculation where there is absence of excessive colloidal entrapment and high shear resistance. Mainly, the dominant mechanism in these graphs are charge neutralization combined with low bridging to ensure moderate speed of coag-flocculation as represented in Figs 13 to 17.The discrete nature of formation of N1,N2 and N3 is associated with modern energy barrier. (Sawyer and  McCarly, 1967).

CONCLUSION

The reduction of TSS recorded within the first 5 minutes and high level of E (%) presents the potential of PSC as Chitin derived coagulant that can be utilized in large scale water treatment.

The experimental results with respect to functional parameters highly agree with similar previous works(Jin;2005,Van Zanten and Elimelechi;1992,Holthof et al 1996)

NOMENCLATURE:

K :αth order coag-flocculation constant

βBR:Collision factor for Brownian Transport

εp:Collision Efficiency

τ1/2:Coagulation Period / Half life

E: Coag-floculation Efficiency

R2: Coefficient of Determination

α: Coag-flocculation reaction order

-r: Coag-flocculation reaction rate

REFERENCES

AWWA (2005); American Water Works Association, Standard Methods for the Examination of Water Effluent, New York, U.S.A.

Diterlizzi S.D (1994); Introduction to Coagulation and Flocculation of Waste water, Environmental System Project, U.S.A

Edzwald,J.K (1987);Coagulation – sedimentation filtration process for removing organic substances in drinking and waste water,Noyes Data Corporation ,Park Bridge ,New Jersey

Fernandez-Kim, S (2004); Physiochemical and functional properties of Crawfish Chitosan as Affected by Different Processing Protocols: M.Sc thesis, Dept. of Food Science; Louisiana State University, U.S.A.

Fridkhsberg, D.A (1984); A course in Colloid Chemistry; Mir Publishers Moscow, Russia.

Holthof, H., Egelhaaf, S.U, Borkovec, M., Schurtenberger P and Sticher, H, (1996); Coagulation Rate Measurement of Colloidal Particles by Simultaneous Static and Dynamic Light Scattering, Langmur Vol 12, Pp 5541

Holthof, H., Schmitt, A., Ferńandez-Barbero, Borkovec. M., Cabrerizo-Vilehez., Schurtenberger, P and Hidalgo-Alvarez, R (1997), Measurement of Absolute Coagulation Rate Constants for Colloidal Particles: Comparison of Single and Multiparticle Light Scattering Techniques; Journal of Colloid and Interface Science, 192, Pp 462-470.

Hunter, R.J (1993); Introduction to Modern Colloid Science, Oxford University Press, New York.

Jin, Y (2005); Use of high Resolution Photographic Technique for studying Coagulation/flocculation in water treatment, M.Sc thesis, University of Saskatchewan, Saskatoon, Canada.

Ma,J.J;Li G;Chen,G.R;Xu,G.O and Cai G.Q (2001);Enhanced coagulation of surface waters with high organic content by permanganate perooxidation .Water science and Technology : Water Supply,1(1):51-61;UK

Menkiti, M.C (2007); Studies on coagulation and flocculation of Coal Washery Effluent: Turbid metric approach .M.Sc thesis,Nnamdi Azikiwe University Awka,Nigeria.

Metcalf and Eddy (2003); Physical Unit Process, Waste Water Engineering Treatment and Reuse, 4th Ed, Tat-McGraw Hill, New York.

O’Meila C.R (1978) Coagulation in waste water  treatment : The scientific basis of flocculation (NATO Advanced study Inst. Series E,Appl.Sc.No 27)  in : Ives ,K.J (Ed).Sijtholf and Noordhoff,Alpenan den Rijn, Netherlands.

Sawyer, C.N and McCarly P.L (1967); Chemistry for Sanitary Engineers, McGrawHill Series, U.S.A.

Swift, DL and Friedlander S.K (1964); Journal of Colloid Science, Vol 19, Pp 621.

Thomas,D.N;Judd,S.J and Fawcett,N;(1999);Flocculation modeling:A review.Water Resources,33(7):1579-1592

Van Zanten, J.H., and Elimelechi M., (1992); Determination of Rate constants by multi angle light scattering; Journal of colloid and interface Vol 154, No 1.

Von Smoluchowski, M (1917); Versucheiner Mathematischen Theorie der Koagulations Kinetic Kolloider Lousungen. Z. Phys. Chem. 92: Pp 129-168.

Water Specialist Technology (WST); (2003); About Coagulation and Flocculation: Information Bulletins, U.S.A.

Yates,P;Yan,Y;Jamson G.J and Biggs.S;(2001);Heteroaggregation of particle system:Aggregation Mechanisms and aggregate structure determination;6th World Congress of Chemical Engineering,Melbourne,Australia,23-27 September,2001.

Table 1:Coag-flocculation Functional Parameters for varying pH and constant dosage of 0.1kg/m3 PSC

| Parameter | pH =2 | pH = 4 | pH = 6 | pH = 8 | pH = 10 |
| --- | --- | --- | --- | --- | --- |
| Α | 1 | 2 | 2 | 1 | 2 |
| R2 | 0.9607 | 0.987 | 0.9931 | 0.9856 | 0.7777 |
| K | 1.4483x10-3s-1 | 3.3333x10-4m3/kg.s | 6.6667x10-4m2/kg.s | 3.9167x10-4s-1 | 1.3333x10-4m3/kg.s |
| βBR | 2.8967x10-3s-1 | 6.6666x10-4m3/kg.s | 1.3333x10-3m3/kg.s | 7.8334x10-4s-1 | 2.6667x10-4m3/kg.s |
| KR | 1.4869x10-17m3/s | 1.4182x10-17m3/s | 1.5640x10-17m3/s | 1.4250x10-17m3/s | 1.3726x10-17m3/s |
| εp | 1.9480x1014m3 | 4.7007x1013kg-1 | 8.5249x1013kg-1 | 5.4971x1013m-3 | 1.9426x1013kg-1 |
| Τ1/2 (sec) | 4.0 sec | 39.2 sec | 20.1 sec | 49.60 sec | 136.1 sec |
| -r | 1.4483x10-3C | 3.3333x10-4C2 | 6.6667x10-4C2 | 3.9167x10-4C | 1.3333x10-4C |

Table 2:Coag-flocculation Functional Parameters for varying pH and constant dosage of 0.2kg/m3 PSC

| Parameter | pH =2 | pH = 4 | pH = 6 | pH = 8 | pH = 10 |
| --- | --- | --- | --- | --- | --- |
| Α | 1 | 1 | 1 | 2 | 2 |
| R2 | 0.9888 | 0.9896 | 0.967 | 0.9790 | 0.6623 |
| K | 1.4933x10-3s-1 | 1.0217x10-3s-1 | 3.100x10-4s-1 | 1.6667x10-4m3/kg.s | 1.3333x10-4m3/kg.s |
| βBR | 2.9866x10-3s-1 | 2.0434x10-3s-1 | 6.2x10-4s-1 | 3.3334x10-4m3/kg.s | 2.6666x10-4m3/kg.s |
| KR | 1.431x10-17m3/s | 1.4150x10-17m3/s | 1.5463x10-17m3/s | 1.3880x10-17m3/s | 1.3763x10-17m3/s |
| εp | 2.086x1014m-3 | 1.4440x1014m-3 | 4.0094x1013m-3 | 2.4001x1013kg-1 | 1.9374x1013kg-1 |
| Τ1/2 (sec) | 4.0 | 13 | 43 | 117 | 136.0 |
| -r | 1.4933x10-3 C | 1.0217x10-3 C | 3.100x10-4 C | 1.6667x10-4 C2 | 1.3333x10-4 C2 |

Table 3:Coag-flocculation Functional Parameters for varying pH and constant dosage of 0.3kg/m3 PSC

| Parameter | pH =2 | pH = 4 | pH = 6 | pH = 8 | pH = 10 |
| --- | --- | --- | --- | --- | --- |
| Α | 1 | 2 | 1 | 2 | 2 |
| R2 | 0.8977 | 0.7815 | 0.9927 | 0.9627 | 0.7198 |
| K | 1.4667x10-3s-1 | 3.3333x10-4m3/kg.s | 5.6333x10-4s-1 | 1.6667x10-4m3/kg.s | 1.3333x10-4m3/kg.s |
| βBR | 2.9334x10-3s-1 | 6.6666x10-4m3/kg.s | 1.1267x10-3s-1 | 3.3334x10-4m3/kg.s | 2.6667x10-4m3/kg.s |
| KR | 1.7659x10-17m3/s | 1.7173x10-17m3/s | 1.7357x10-17m3/s | 1.4786x10-17m3/s | 1.4148x10-17m3/s |
| εp | 1.6611x1014m-3 | 3.8819x1013kg-1 | 6.4911x1013m-3 | 2.2543x1013kg-1 | 1.8848x1013kg-1 |
| Τ1/2 (sec) | 4.0 | 39 | 24.0 | 117 | 136 |
| -r | 1.46667x10-3 C | 3.3333x10-4 C2 | 5.6334x10-4 C | 1.6667x10-4 C2 | 1.3333x10-4 C2 |

Table 4 :Coag-flocculation Functional Parameters for varying pH and constant dosage of 0.4kg/m3 PSC

| Parameter | pH =2 | pH = 4 | pH = 6 | pH = 8 | pH = 10 |
| --- | --- | --- | --- | --- | --- |
| α | 1 | 2 | 2 | 2 | 2 |
| R2 | 0.9662 | 0.947 | 0.9714 | 0.983 | 0.6616 |
| K | 8.5517x10-4s-1 | 3.3333x10-4m3/kg.s | 1.6667x10-3m3/kg.s | 1.6667x10-4m3/kg.s | 1.3333x10-4m3/kg.s |
| βBR | 1.7103x10-3s-1 | 6.6666x10-4m3/kg.s | 3.3334x10-3m3/kg.s | 3.3334x10-4m3/kg.s | 2.6666x10-4m3/kg.s |
| KR | 1.424x10-17m3/s | 1.3844x10-17m3/s | 1.3861x10-17m3/s | 1.2905x10-17m3/s | 1.1373x10-17m3/s |
| εp | 1.2058x1014m-3 | 4.8154x1013kg-1 | 2.4047x10-14kg-1 | 2.5829x1013kg-1 | 2.3445x1013kg-1 |
| Τ1/2 (sec) | 6.7 | 39.0 | 8.0 | 117.0 | 136.0 |
| -r | 8.5517x10-4 C | 3.3333x10-4 C2 | 1.6667x10-3 C2 | 1.6667x10-4 C2 | 1.3333x10+ C2 |

Table 5:Coag-flocculation Functional Parameters for varying pH and constant dosage of 0.5kg/m3 PSC

| Parameter | pH =2 | pH = 4 | pH = 6 | pH = 8 | pH = 10 |
| --- | --- | --- | --- | --- | --- |
| Α | 2 | 2 | 2 | 2 | 2 |
| R2 | 0.928 | 0.9464 | 0.9744 | 0.9697 | 0.444 |
| K | 5x10-4m3kg-1s-1 | 3.3333x10-4m3/kg.s | 6.6667x10-4m3/kg.s | 1.6667x10-4m3/kg.s | 8.3333x10-5m3/kg.s |
| βBR | 1x10-3m3/kg.s | 6.6667x10-4m3/kg.s | 1.3333x10-3m3/kg.s | 3.3333x10-4m3/kg.s | 1.6667x10-4m3/kg.s |
| KR | 1.4200x10-17m3/s | 1.6622x10-17m3/s | 1.7182x10-17m3/s | 1.4924x10-17m3/s | 1.4280x10-17m3/s |
| εp | 7.0418x1013kg-1 | 4.0107x1013kg-1 | 7.759x1013kg-1 | 2.2334x1013kg-1 | 1.1671x1013kg-1 |
| Τ1/2 (sec) | 12 | 39.2 | 20 | 117 | 218 |
| -r | 5x10-4 C2 | 3.3333x10-4 C2 | 6.6667x10-4 C2 | 1.6667x10-4 C2 | 8.3333x10-5 C2 |

4/1/2009

# Text boxes

fig4: Plot of TSS vs Coag-flocculation Time for 0.4kg/m3 PSC at varying pH

pH=10

pH=8

pH=6

pH=4

pH=2

TSS x (10-3 kg/m3)

Time x (60 sec)

40

30

20

10

0

5000

4000

3000

2000

1000

0

pH

Fig 3:plot of TSS vs Coag-flocculation Time for 0.3kg/m3 PSC at varying

pH=10

pH=8

pH=6

pH=4

pH=2

TSS x (10-3 kg/m3)

Time x (60 sec)

40

30

20

10

0

6000

5000

4000

3000

2000

1000

0

pH

Fig 2:Plot of TSS vs Coag-flocculation Time for 0.2 kg /m3 PSC at varying

pH=10

pH =8

pH =6

pH= 4

pH=2

TSS x (10-3 kg/m3)

Time x (60 sec)

40

30

20

10

0

5000

4000

3000

2000

1000

0

pH

Fig 1:Plot of TSS Vs Coag-floccualtion Time for 0.1kg/m3 PSC at varying

0

1000

2000

3000

4000

5000

0

10

20

30

40

Time x (60 sec)

TSS x (10-3 kg/m3)

pH=2

pH=4

pH=6

pH=8

pH=10

Fig5:plot of TSS vs Coag- flocculation Time for 0.5kg/m3 PSc at varying pH

0

500

1000

1500

2000

2500

3000

3500

4000

4500

5000

0

10

20

30

40

Time x (60 sec)

TSS x (10-3 kg/m3)

pH=2

pH=4

pH=6

pH=8

pH=10

fig 6:Plot of E vs time at varying pH and constant dosage of 0.1kg/m3

PSC

96.5

97

97.5

98

98.5

99

99.5

100

100.5

0

10

20

30

40

Time x (60 sec)

E( %)

pH=2

pH=4

pH=6

pH=8

pH=10

fig7:plot of E vs time at varying pH & constant dosage of 0.2kg/m3 PSC

96

96.5

97

97.5

98

98.5

99

99.5

100

100.5

0

10

20

30

40

Time x (60 sec)

E( %)

pH=2

pH=4

pH=6

pH=8

pH=10

fig8:plot of E vs time at varying pH & constant dosage of 0.3kg/m3 PSC

96

96.5

97

97.5

98

98.5

99

99.5

100

100.5

0

10

20

30

40

Time x (60 sec)

E( %)

pH = 2

pH= 4

pH = 6

pH = 8

pH =10

fig9:plot of E vs time at varying pH at constant dosage of 0.4kg/m3 PSC

95.5

96

96.5

97

97.5

98

98.5

99

99.5

100

100.5

0

10

20

30

40

Time x (60 sec)

E( %)

pH =2

pH = 4

pH=6

pH=8

pH =10

fig10:Plot of E vs time at varying pH & constant dosage of 0.5kg/m3

PSC

95

96

97

98

99

100

0

10

20

30

40

Time x (60 sec)

E ( %)

pH = 2

pH = 4

pH = 6

pH =8

pH = 10

fig11:plot of Coag-flocculation efficiency Vs pH at 30 mins for

varying dosages

97.5

98

98.5

99

99.5

100

100.5

0

2

4

6

8

10

12

pH

E( %)

0.1kg/m3 PSC

0.2kg/m3PSC

0.3kg/m3 PSC

0.4kg/m3 PSC

0.5kg/m3 PSC

Fig 12:plot of Efficiency vs Dosage at varying pH & constant time

97.5

98

98.5

99

99.5

100

100.5

0

0.2

0.4

0.6

Dosage ( kg/m3)

E(%)

pH =2 at 30 mins

pH =4 at 30 mins

pH =6 at 30 mins

pH =8 at 30 mins

pH =10 at 30 mins

Fig 13:Particle distribution plot for 0.1kg/m3 PSC at pH of 2

0

50

100

150

200

250

300

350

400

0

10

20

30

40

Time x (60 sec)

No of conc.( kg/m3)

N1(kg/m3)

N2(kg/m3)

N3(kg/m3)

ΣNi(kg/m3)

Fig 14:Particle distribution plot for 0.2kg/m3 PSC at pH

of 2

0

50

100

150

200

250

300

350

400

0

10

20

30

40

Time x (60sec)

No of conc.( kg/m3)

N1(kg/m3)

N2(kg/m3)

N3(kg/m3)

ΣNi(kg/m3)

Fig 15: particle distribution plot for 0.3kg/m3 PSC at pH of 2

0

100

200

300

400

0

10

20

30

40

Time  x  (60 sec)

No of conc (kg/m3)

N1(kg/m3)

N2(kg/m3)

N3(kg/m3)

ΣN1(kg/m3)

Fig 16: Particle plot distribution plot for 0.4kg/m3 PSC at pH of 6

0

20

40

60

80

100

120

140

160

0

10

20

30

40

Time x (60 sec)

No of conc ( kg/m3)

N1(kg/m3)

N2(kg/m3)

N3(kg/m3)

ΣN1(kg/m3)

Fig 17:Particle plot distribution plot for 0.5 kg/m3 PSC at pH of 6

0

50

100

150

200

0

10

20

30

40

Time x (60sec)

No of conc.(kg/m3)

N1(kg/m3)

N2(kg/m3)

N3(kg/m3)

ΣN1(kg/m3)