Recent Status of Arsenic Contamination in Groundwater of Northeastern India – A Review

N.Linthoingambi Devi1, yadav Ishwar Chandra2, QI Shihua1

1School of Environmental Studies, China University of Geosciences, 388, Lumo Road, Wuhan, Hubei, 430074，P.R. China.

2 Department of Environmental Science, University of Mysore, Mysore-570006, India

n.linthoi.devi@gmail.com

Abstract：High concentration of arsenic (As) in groundwater in the northeastern states of India has become a major cause of concern in recent years. Arsenic in groundwater has been detected in some parts of Assam, Tripura, Manipur, Nagaland and Arunachal Pradesh. The ground water in the past was considered to be safe for drinking purpose but now it came to be known that many shallow tube wells contain arsenic at concentrations higher than the safe limit set for drinking purpose by WHO 1993. It is becoming an emerging issue in the water supply and health sectors of Northeastern India. This paper reviews the recent status of arsenic in ground water of northeastern states of India and recommends proper research methods to be adopted in mitigating the effects of it to human health.

Keywords: Arsenic, Arsenic in ground water, contaminated tube wells, drinking water in northeastern states of India.

Introduction

Arsenic contamination of drinking water is a worldwide problem due to its detrimental effects on health. These effects range from skin ailments through to serious diseases such as Cancer and to death. Arsenic contamination of ground water has been reported from many countries including Bangladesh, Vietnam, Argentina, China and parts of USA and now in India. The provisional limit of Arsenic in drinking water as recommended by WHO is 10 microgram per liter. Arsenic is a chemical that is widely distributed in nature and principally occurs in the form of inorganic or organic compounds. Inorganic compounds consist of arsenite, the most toxic forms and arsenate the less toxic forms. Exposure to inorganic compounds may occur in a variety of ways through certain industrial effluents, chemical alloys, pesticides, wood preservative agents, combustion of fossil fuels, occupational hazards in mining and dissolution in drinking water. The most commonly found arsenic compounds in drinking water are trivalent arsenite or pentavalent arsenate. However, groundwater is notoriously prone to chemical and other types of contamination from natural sources or by anthropogenic activities. Reliable data on exposure and health effects are rarely available, but it is clear that there are many countries in the world where arsenic in drinking water has been detected at concentrations greater than the WHO Guideline Value, 0.01 mg/l or the prevailing national standards. The major issue of arsenic contaminated water is to find out the level of contamination of arsenic and it is not so easy because of no color, no odor and no taste even in the highly contaminated water. Arsenite is more toxic (about ten times) than the arsenate due to former ability to react with sulfhydryl groups there by increasing the residence time (Nagarnaik et al., 2002). Although there is no widely accepted mechanism of the release of arsenic in ground water, but it has been accepted that most of all including in northeastern states of India is of natural, geological origin. The arsenic is thought to be closely associated with oxidation-reduction process of iron oxides and pyrite.

Due to the withdrawal of excessive amounts of groundwater, problems of increased iron, fluoride and arsenic (As) contamination have been reported in different parts of India (Khan, H. R., 1994, Singh, A. K., 2004). A recent study on cancer risks from As in drinking water indicates that it could cause liver, lung and kidney/bladder cancer besides skin cancer (Smith, A. H. et al., 1992). The most important remedial measure is prevention of further exposure by providing safe drinking water. From this point of view, several ideas have been highlighted in this article to control and remove As from groundwater used for household activities as well as irrigation.

Distribution of arsenic in groundwater in northeastern states

The presence of As in groundwater in West Bengal is the most serious health hazard India has ever faced. A recent study shows many areas within the northeastern states with As concentration greater than 0.05 mg/l, implying that millions of people are at serious risk of As poisoning（Singh 2004）. According to a report, the concentration of As generally varies from 0.02 to 0.9 mg/l (exceeding the WHO standard of 0.01 mg/l and Bureau of Indian Standard (BIS) of 0.05 mg/l). While As and iron pose individual problems in the aqueous environment, their association in groundwater have the potential of providing a simple means of removing As by co-precipitation and adsorption. About 95% of the area of the northeastern region contains dissolved iron in excess of 2 mg/l, and the iron concentration is as high as 15 mg/l in many areas（Singh 2004）.The presence of As in groundwater as an environmental hazard, following analysis of more than 4000 water samples from 2000 wells and other drinking-water sources during the monsoon and non-monsoon seasons of 2003–04 in the eight states of northeast India. Some of the affected districts of Assam and Tripura （Singh 2004） are close to the affected districts of Bangladesh, where As concentration is above 300 μg/l. In this part of India, the rural population is dependent on tube-well water for drinking as well as for irrigation. Most of the tube-wells are shallow. As contamination in groundwater in the region and the occurrence of melanosis, keratosis and cancers in future are serious environmental health concerns.

As has been detected in 21 of the 24 districts of Assam and three districts in the plains of Tripura, six districts in Arunachal Pradesh, one district in Manipur and two districts in Nagaland（Singh 2004）. The existence of contamination has been well established in the old Brahmaputra Plain of Bangladesh（Chowdhury, U. K.,2001，British Geological Survey, 2001）. Field surveys found it also occurred extensively in groundwater of the Upper Brahmaputra Plain in Assam（Singh 2004， Chakraborti, D.2004）. Among groundwater samples from 137 hand-pumped tube-wells in different parts of Assam, 43% indicated As concentration above 10 mg/l and 26% above 50 mg/l. Maximum concentration of 490 mg/l was detected in the region (Chakraborti, D.2004). According to the study, maximum As content was observed in Jorhat (Titabor, Dhakgorah, Selenghat and Moriani blocks), Dhemaji (Sissiborgoan and Dhemaji blocks), Golaghat district (Podumani block) and Lakhimpur (Boginodi and Lakhimpur blocks), Assam; West Tripura (Jriania block), Dhalai (Salema block) and North Tripura (Dharmanagar block) districts, Tripura; Thuobal (Kakching block), Manipur and Dibang valley (Midland), Arunachal Pradesh（Singh 2004）. Groundwater in these blocks belonging to the five states is contaminated with As. In Manipur, As was found only in Kakching block of Thoubal district, where As concentration was as high as 798–986 mg/l. In Arunachal Pradesh, six districts were contaminated with As and maximum As concentration (618 mg/l) was found in part of the Midland block, Dibang valley district. These six districts of Arunachal Pradesh are situated near the border area of Assam. In Tripura, parts of West Tripura, North Tripura and Dhalai districts had As concentration in the range 65–444 mg/l. In Nagaland, seven areas in Mokokchung district and five areas in Mon district showed the presence of As in groundwater. These two districts are situated near Jorhat district, Assam. Traces of As were also found in the plains of Wokha and Zunheboto districts,Nagaland（Singh 2004）.Very high concentration of As was found in four districts, viz. Jorhat, Lakhimpur, Nalbari and Nagoan. In Jorhat district, 80 samples were collected and 21% of the samples were found contaminated with As in the range 228–657 μg/l. In Lakhimpur district, 76 samples were analysed and 21.2% were contaminated with a range 210–550 μ/l. In Nalbari district, 19% samples (total 72 samples) contained As in the range 234–422 μg/l. In Nagaon district, 76 samples were collected and 13% were found contaminated with As（Singh 2004） The range of As concentration in Nagaon was between 217 and 601 μg/l. A survey report of two districts in Assam, i.e. Dhemaji and Karimganj indicated As contamination in groundwater. So far 241 hand tube-wells have been analysed for As in these two districts; 42.3 and 19.1% have concentration above 10 and 50 μg/l respectively （Chakraborti, D 2004）. From these two districts, 27 villages have been identified where As in groundwater is above 50 μg/l. Recently, the Public Health Engineering Department (PHED) in association with UNICEF collected groundwater samples in the districts of Assam situated near Brahmaputra River and, found the presence of As above BIS permissible limits in the places spread over in 15 districts.In Tripura, distribution of As in groundwater varied from 1.38 to 191.91 μg/l in West Tripura (27.19%), 4.49 to 444.48 μg/l in Dhalai (36.12%), and 3.23 to 215.0 μg/l in North Tripura (24.47%). Maximum As in drinking water was found in Jirania and Bishalgarh blocks, West Tripura; Salema and Kamalpur blocks, Dhalai and Dharmanagar, Kailasahar, Kanchanpur and Jampui blocks, North Tripura. Only South Tripura was found to be free from arsenic contamination（Singh 2004）. In Thoubal district of Manipur, about 25% of the collected samples had As in the range 798–986 μg/l. The sediment in the northern region contains a high percentage of clay and organic compounds （Acharyya ,1999）, which may retain and release As in the groundwater aquifers. A study（Baruah, 2003） on As in carbonaceous matter in Arunachal Pradesh, Assam, Nagaland and Meghalaya, indicated that the mean As concentration of samples from the four regions was 95.1 mg/kg. It is believed that the weathering of sulphide associated with carbonaceous matter may have produced As-rich iron oxyhydroxides, which in turn released As (after reduction) to the existing sedimentary environment（Khan 1994，Nickson 1998）. Results indicated increased As enrichment from east to west in Northeast India. The distribution of arsenic in northeastern India is presented in Figure 1.

Arsenic sources

Arsenic is a natural constituent of the earth’s crust and is the 20th most abundant element. The average concentration（NAS 1977，Taylor 19 85） of As in the continental crust is 1–2 mg/kg. Arsenic is released in the environment through natural processes such as weathering and volcanic eruptions, and may be transported over long distances as suspended particulates and aerosols through water or air. Arsenic emission from industrial activity also accounts for widespread contamination of soil and groundwater environment（Jacks，G. 1998，Juillot, F. 1999）， Many authors have reported As emissions to the atmosphere on global, regional and local scales（Nriagu, J. O.1988，Pacyna, J. M. 2001）. Once introduced into the atmosphere, As may circulate in natural ecosystems for a long time depending on the prevailing geochemical environments （Boyle, R. W. 1973，Yan Chu, H., 1994）

Toxicity and health effects of arsenic：

The United States Environment Protection Agency (USEPA) and International Agency for Research on Cancer (IARC) have specified arsenic as known human carcinogen. According to EPA weight of evidence classification for carcinogens, arsenic is categorized as Group A Carcinogen. Its classification indicates that there is sufficient evidence from epidemiological studies to support a case–effects relationship between the substance and cancer. As is virulent poison on acute ingestion, 76 mg As (3+) is considered to be lethal to adults and extremely toxic on long-term exposure to a very low concentration (Azcue and Narjagu, 1994 in Sharma 1999). Extremely toxic arsenic oxide former use as a poison for vermin has been vastly reduced on account of concerns over its accumulation in the food chain. Arsenic enters the human body through ingestion, inhalation, or skin absorption. Significant route of As ingestion is drinking water. The amount of As species in urine is often considered an indication of chronic As exposure. The species are the result of the biotransformation of inorganic As (Table 1)

Table 1: Arsenic speciation in human urine：(Smith,T.J. 1977)％

| Species | Average values | Μg/L |
| --- | --- | --- |
| As(III) | 1.3 | 1.9 |
| As(V) | 1.3 | 3.9 |
| Methylarsonic acid | 3.4 | 1.8 |
| Dimethyl arsenic acid | 11.5 | 15.0 |
| Total As | 21.2±2.04 | 22.5±8.5 |

The discovery of arsenic in drinking water in many areas of the world has caused widespread public health concern. Close to 100 million people in the world, including about 13 million in the United States, are chronically exposed to inorganic As [International Agency for Research on Cancer (IARC) 2004]. Inorganic As is an established potent human carcinogen (IARC 2004). In addition, ingestion of As through drinking water has been implicated in several noncancer diseases, for example, peripheral vascular disease; hypertension; respiratory, neurologic, and liver disorders; and diabetes mellitus [IARC 2004; National Research Council (NRC) 2001; WHO/IPCS (International Programme on Chemical Safety) 2001]. Early effects of exposure to As in drinking water include pigmentation changes and hyperkeratosis (IARC 2004; Smith et al. 2000), which reportedly appear after 5–10 years of exposure (Guha Mazumder et al. 1998). There may be some degree of skin absorption in contact of trivalent oxide, because of its rapid solubility. Most ingested and inhaled arsenic is well absorbed through the gastrointestinal tract and lungs into blood stream. It is distributed in large number of organs including the liver, lung, kidney and skin. About 70 % of the arsenic is excreted mainly through the urine. Most arsenic absorbed into the body is converted by liver to less toxic methylated arsenic then efficiently excreted in the urine (Saha, 1999, in Nagarnaik 2002). In the initial stage of chronic exposure of arsenic for more than five years, skin colour becomes black (melanosis), rough and tough (keratosis), eyes become red (conjunctivitis). Also in some cases there will be pain in inhaling (Bronchitis) and Vomiting and Diarrhea (Gastroenteritis). The manifestations of arsenicosis are clearer in the second stage with black and white spots on the skin (leukomelanosite), palms and soles are affected by hard nodules (Hyperkeratosis), swelling of legs, Peripheral Neuropathy and complications of kidney and liver. Finally it also turns to cancer in skin, lungs, kidneys, liver and other organs.

Guideline value for arsenic in drinking water

The first version of International standards for drinking water included arsenic in the category of toxic substances and established 200 ppb as the allowable concentration in drinking water (WHO, 1958). In updated standards of 1963, WHO lowered the allowable concentration to 50 ppb (WHO, 1963). The WHO continued its review work to lower the guideline value for arsenic in drinking water by establishing a guideline value (provisional) of 10 ppb in 1993 (WHO 1993). This provisional Guideline Value (GV) of 10 ppb has been adopted as the national standards for drinking water by a number of countries. However many developing countries have retained the previous WHO GV of 50 ppb as their national standards.

Table 2: Currently accepted national standards for arsenic in drinking water in some selected countries.

| S.No. | Countries | National Standards for As in drinking water (ppb) | Year since when it has been accepted |
| --- | --- | --- | --- |
| 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 | Australia Jordan Japan EC Mongolia Laos USA Canada Philippines Sri Lanka Vietnam India Bangladesh China Nepal | 7 10 10 10 10 10 10 25 50 50 50 50 50 50 50 | 1996 1991 1993 1998 1998 1999 2001 1999 1978 1983 1989 NA NA NA 2003 |

Testing for arsenic

Field methods

The most important characteristic of the field-testing method is that the testing can be carried out in field, where the sample is taken. In this method relatively very simple testing field-kits are used. Although the test resulting from field kits are not precise, field-testing is considered best option for Nepal, where there are only a few laboratories with competent personnel and equipments. When any metal arsenide reacts with strong acids, arsine gas is formed. Most arsenic test kits rely on the reduction of inorganic arsenic to arsine gas (AsH3) using zinc metal and hydrochloric acid. This gas is allowed to pass through the mercury bromide (HgBr2) indicator paper and the intensity of colour indicates the concentration of arsenic.

Many field kits, including two Nepali kits are available in Nepal listed as follows;

• AAN Kit (Japan)

• E-Merck Kit (Germany)

• NIPSOM Kit (Bangladesh)

• AIIHPH Kit (India)

• ENPHO Kit (Nepal)

• Modified AAN Kit (Nepal)

• Hach EZ (USA)

• Wagtech Arsenator (UK)

Analytical Methods

Numerous methods are described in the literature, for the analysis of total arsenic in water. Many analytical methods essentially employ the same principles, but apply different reagents or concentrations.

The possibilities for total arsenic determination include:

1. Atomic absorption spectrometry (AAS)

a. Hydride Generation System (AAS-HG)

b. Graphite furnace (AAS-GF) for atomization,

2. Inductively coupled plasma

a. With atomic emission spectrometry (ICP-AES)

b. With mass spectrometry (ICP-MS)

3. Atomic fluorescence spectrometry (AFS)

4. Anodic stripping voltammetry (ASV) or

5. Spectrophotometry.

Both atomic absorption spectrometry and atomic fluorescence spectrometry, a relatively new and sensitive technique, are single element specific techniques with known and controllable interferences. The inductively coupled plasma techniques offer the possibility of examining a number of contaminants, as they are multi-element techniques, again with known and controllable interferences. Anodic stripping voltammetry is a useful technique for samples containing only free dissolved arsenic, while the spectrophotometric method, which is also a single element technique, has the advantage of being relatively inexpensive in terms of equipment. The mostly used in Indian laboratories AAS-HG technique is based on the atomic absorption measurement of arsenic generated by thermal decomposition of arsenic (3+) hydride. As (3+) is reduced to arsine gas by reaction with sodium tetrahydroborate in a hydrochloric acid medium (ISO 11969:1996; SM 3114:1999). Arsenate and Arsenite have different sensitivities using this technique so any arsenate must be reduced to trivalent arsenic prior to the determination and done by using a solution of hydrochloric acid, potassium iodide and ascorbic acid. In India the silver diethyldithiocarbamate spectrometric method (SDDC) and spectrophotometry have been also used as alternate to AAS-HG. The key points of each of the above techniques are summarized below in Table 3

Table 3: Summary of analytical methods for Arsenic test:

| Method | Detection Limit (ppb) | Sample Size (ml) | Equipment Cost (USS in ‘000) | Daily Throughput | Remarks | Selected References |
| --- | --- | --- | --- | --- | --- | --- |
| AAS-HG | 0.05 | 50 | 20-100 | 30-60 | Single element | ISO,11969 (1996); SM 3114(1999) |
| AAS-GF | 1-5 | 1-2 | 40-100 | 50-100 | Single element | ISO/CD 15586 (2000); SM 3113 (1999) |
| ICP-AES | 35-50 | 10-20 | 60-100 | 50-100 | Multi element | ISO/CD 11885 (1996); SM 3120 (1999) |
| ICP-MS | 0.02-1 | 10-20 | 150-400 | 20-100 | Multi element | SM 3125 (1999) |
| HGAFS | 0.01 | 40-50 | 20-25 | 30-60 | Single element | CEN/TC/230/WGI/TG, 12 N3 (1999) |
| ASV | 0.1 | 25-50 | 10-20 | 25-50 | Only free Dissolved arsenic | USEPA 7063 |
| SDDC | 1-10 | 100 | 2-10 | 20-30 | Limited to water sample | SM 3500 (1999) ISO 6595 (1982) |

Global situation of arsenic in groundwater

Active groundwater contributes about 0.274 percent of total water budget and is the major source as fresh water for drinking water proposes. Arsenic contamination in groundwater has been reported in 20 different countries of the world. Four major calamities in order of magnitude are in Asia and these are Bangladesh, India (West-Bengal), China (including Inner Mongolia) and Taiwan. In terms of population exposed, arsenic problems in ground water from the alluvial deltaic aquifers of Bangladesh and West Bengal represent the most serious occurrences identified globally. The southwest coastal zone of Taiwan was perhaps the first area to be identified as a problem area for health effects arising from chronic arsenic exposure. Awareness of the arsenic problem began during the 1960s (Smedly et al., 2003) and arsenic–related health problems were documented. Well-known black-foot dieses in Taiwan had been identified science then. The Chaco-Pampeon Plain of central Argentina perhaps is the largest region of high-arsenic groundwaters known, covering around one million km2.

Table 4. Naturally-occurring As problems in world ground waters: (In Smedley et al., 2003)

| S.No. | Country/Region | Population exposed (million) | Area (Km2) | Max Conc. Range (ppb) |
| --- | --- | --- | --- | --- |
| 1 2 3 4 5 6 7 8 9 10 | Bangladesh India/West Bengal China Argentina Nepal Chile(North) Mexico USA(South west) Taiwan Mongolia (Huhhot Basin) | 30 6 5.6 2 0.46-0.75 0.5 0.4 0.35 0.1 0.1 | 150000 23000 NA 1000000 30000 125000 32000 206300 4000 4300 | 2500 3200 NA 5300(7800 in some pore waters) 600(2620 in one case) 1000 620 2600 2400 |

Discussion:

Despite limited studies and information, a significant segment of the rural Indian population residing in the northeastern has been exposed to an elevated level of arsenic. An accurate figure of the exposed

population may be much higher than presently believed, and requires the majority of the tube wells to be examined. Clinical studies on patients from the arsenic affected districts have displayed symptoms of arsenicosis on the skin as well as other health disorders. Symptoms of arsenicosis may appear after years of exposure, depending on the level of exposure and the person's weight and health conditions. The minimum drinking water to sustain life ranges from2 to 5 L/d in moderate climatic condition with average activity levels (Gleick, 1996). The average drinking water intake by Bangladesh population was estimated to be 3 L/d with a maximum of 5.7 L/d (Ohno et al., 2007; Watanabe et al., 2004). The average drinking water intake by northeast people of India inhabiting may be close to these values because they fall under a similar climatic region. If a patient drinks about 2–4 L of arsenic contaminated water per day over a long period, the symptoms of arsenic related diseases may appear. However, most signs and symptoms are nonspecific and are typically accompanied by hyper pigmentation or keratoses or both (Smith et al., 2000). Maharjan et al. (2005) reported arsenicosis was prevalent in all age groups greater than 15 years. Cases of arsenicosis will increase in the future because, Part of the arsenic contamination in a vast area of the Ganges and Brahmaputra basin Northeastern states is possibly mainly geological.

One of the ways to mitigate this arsenic problem is to change the source (uncontaminated groundwater), which brings up other issues of privacy and ownership. Some field tests suggested that water from deeper tube wells (N30 m) contains a low level of arsenic (World Bank, 2005); therefore pumping water from deep tube wells for supply is another option. However, this requires a thorough investigation of the aquifers and a detailed cost analysis. And again, it may need some sort of treatment depending on the arsenic level. Arsenic could be removed by co-precipitation as well as by adsorption on ferric hydroxide surfaces if the groundwater contains an appreciable concentration of dissolved iron. Oxidation of iron (II) chemically or biologically to ferric hydroxide is essential. About 95% of the area of the northeastern region contains dissolved iron in excess of 2 mg/l, and the iron concentration is as high as 15 mg/l in many areas（Singh, 2004）; therefore, a simple iron assisted biological sand filter may be applicable to remove arsenic to an acceptable level. The household filters currently distributed in the arsenic affected districts contain rusted iron nails (ferric hydroxides) as the sink for arsenic adsorption by a surface complexation mechanism. The soluble iron (Fe2+) already present in the groundwater oxidizes in the form of ferric hydroxide, and the elemental iron (iron nails) oxidizes to ferric hydroxide chemically (air) and biologically, especially by air and iron bacteria, respectively.

The arsenic loaded iron particulates are retained on the sand filter by mechanical straining. The advantages of this kind of filter are that the iron bacteria, which thrive on iron and organic matter, develop on the filter. The outer cell of these bacteria provides a large surface area for arsenic loaded

iron oxide adsorption (Katsoyiannis and Zouboulis, 2004). the pitcher filter unit can remove 90– 98% As-bearing water when As bearing groundwater was passed through wood charcoal and sand. This technology is effective at household level in removing As, but the system may be quickly clogged as groundwater of the northeastern region contains excessive iron. Risk of bacterial contamination may also to be checked by sterilizing the medium before filter-construction. Ngai et al. (2006) reported 93–95% removal of iron and turbidity by KAF during the field test. Murcott and Lukacs (2002) conducted a technological evaluation of the biosand filter and the possible mechanism of arsenic, iron, and pathogen removal. A recent study by Jin and Chiu (2007) at the University of Delaware stated that zero-valent iron based filters were effective in removing pathogenic bacteria and viruses (99.999%) from drinking water. The mechanism of virus removal was not clear, but the researchers believe that viruses might have been inactivated chemically by iron oxide or due to the adsorption of viruses on the iron oxide surfaces; E. coli, Hepatitis A, Norovirus and Rotavirus were also removed by zero-valent iron assisted filters (Jin and Chiu, 2007). The filters currently introduced in the northeast region are a good arsenic mitigation alternative. A long-term plan should be formulated by the government for the treatment and sustainable use of northeast groundwater. Every field kits should be checked for their performances. For this purpose establishment of a reference laboratory is urgent. Every new tube well should be constructed only after the test for arsenic.

Conclusion:

This review has attempted to summarize the incidents of arsenic contamination in groundwater in the northeastern states of India. It poses a significant risk to public health in the northeast region of India. Therefore, the first priority to remediate the crisis should be early identification of the affected sources, and the next hurdle is to provide arsenic-safe water to the affected masses. It is necessary to seal the highly contaminated tube wells to protect the non-contaminated aquifers and provide the good biosand filters to the rural northeast regions.

Acknowledgements

The authors would like to thank the reviewers for their constructive comments.

Corresponding to:

Miss.N.Linthoingambi Devi, School of Environmental Studies, Key Laboratory of Bio and Environmental Geology of Ministry of Education,China University of Geosciences, 388, Lumo Road, Wuhan, Hubei, 430074，P.R. China.

Email: n.linthoi.devi@gmail.com   phone no: 008613098823940

Submission date: 1st April 2009

Reference：

1.    Acharyya, S. K., Chatraborty, P., Lahiri, S., Raymahashay, B. C., Guha, S. and Bhowmik, A., (1999) Arsenic poisoning in the Ganges delta. Nature, 401: 545–546.

2.  British Geological Survey/Department of Public Health Engineering. (2001). Arsenic contamination of groundwater in Bangladesh. Technical Report, Key worth, UK.

3.    Baruah, M. K., Kotoky, P., Baruah, J., Borah, G. C. and Bora, P. K. (2003) Arsenic association and distribution in carbonaceous materials in northeastern India. Curr. Res., 85: 204–208.

4.    Boyle, R. W. and Jonasson, I. R., (1973) The geochemistry of arsenic and its use as an indicator element for geochemical prospecting. J. Geochem. Explor., 2: 252–296.

5.    Chakraborti, D. et al., (2004) Groundwater arsenic contamination and its health effects in the Ganga–Meghna–Brahmaputra plain. J. Environ. Monit. 6:74N–83N.

6.    Chowdhury, U. K., (2001) Groundwater arsenic-contamination status at four geo-morphological areas in Bangladesh (special reference to arsenic in biological samples and agricultural crop). Ph D dissertation, Jadavpur University, Kolkata.

7.    CEN/TC/230/WG1/TG 12 N 3 (1999) Water quality – Determination of arsenic in drinking, surface, ground, saline and industrial and domestic waste waters.

8.    Gleick PH (1996) Basic water requirements for human activities: meeting basic needs. Water

Int;21(2):83–92.

9.    Guha Mazumder DN, Haque R, Ghosh N, De BK, Santra A, Chakraborty D, et al. (1998).Arsenic levels in drinking water and the prevalence of skin lesions in West Bengal, India. Int J Epidemiol 27(5):871–877.

10.  IARC (International Agency for Research on Cancer),(2004) Some Drinking-Water Disinfectants and Contaminants, Including Arsenic. IARC Monogr Eval Carcinog Risks Hum 84.

11.   ISO 11885,(1996) Water quality – Determination of 33 elements by inductively coupled plasma atomic emission spectrometry.

12.   ISO 11969, (1996) Water quality – Determination of arsenic – Atom absorption spectrometric method (hydride technique).

13.   ISO 6595(1982) Water quality – Determination of total arsenic – silver diethyldithiocarbamate spectrophotometric method.

14.   ISO/CD 15586, (2000) Water quality – Determination of trace elements by atomic absorption spectrometry with graphite furnace.

15.   Jacks, G. and Bhattacharya, P. (1998) Arsenic contamination in the environment due to the use of CCA-wood preservatives. In Arsenic in Wood Preservatives: Part I, Kemi Report, vol.3/98:.     7–75.

16.   Jin Y, Chiu P. (2007) New technology removes viruses from water; 2007. http://www.terradaily.

com/reports/New_Technology_Removes_Viruses_From_Drinking_Water_999.html

(Accessed April 29, 2007).

17.    Juillot, F., Ildefonse, P. H., Morin, G., Calas, G., de Kersabiec, A. M. and Benedetti, M., (1999) Remobilization of arsenic from buried wastes at an industrial site: mineralogical and     geochemical control. Appl. Geochem., 14:1031–1048.

18.    Katsoyiannis IA, Zouboulis AI.(2004) Application of biological processes for the removal of

arsenic from groundwaters. Water Res;38(7):17–26.

19.    Khan, H. R., (1994) Management of groundwater resources for irrigation in Bangladesh, FAO

20.    M 3500-As B, (1999) Standard Methods for the Examination of Water and Wastewater, Silver Diethyldithiocarbamate method.

21.    Murcott S, Lukacs H. Household water treatment in Nepal; (2002). http://thinkcycle.mle. ie/thinkcycle/main/development_by_design_2002/publication household d_water_treatment_in_nepal/Lukacs_Murcott2.pdf (accessed April 27, 2007).

22.    Maharjan M, Watanabe C, Ahmad A, Ohtsuka R(2005) Arsenic contamination in drinking water and skin manifestations in lowland Nepal: the first community-based survey. Am J Trop Med Hyg; 73:477–9.

23.    Nagarnaik P. B. , Bhole A.G. and Natarajan G.S. (2002) Arsenic removal of ground water – a state of art, Water Resources Journal, December: 51-66.

24.   NRC (National Research Council). (2001) Arsenic in Drinking Water: 2001 Update. Washington, DC: National Academy Press.

25.    NAS, (1977) Medical and biologic effects of environmental pollutants: arsenic. National Academy of Sciences, Washington DC

26.    Ngai T, Dangol B, Murcott S, Shrestha RR. (2006) A simple arsenic solution for the arsenic

problem, Kanchan Arsenic Filter. Environment and Public Health Organization;

27.    Nickson, R. T., McArthur, J. M., Burgess, W. G., Ahmed, K. M., Ravens croft, P. and Rahaman, M., (1998) Arsenic poisoning of Bangladesh groundwater. Nature, 395–338.

28.     Nriagu, J. O. and Pacyna, J. M., (1988) Quantitative assessment of worldwide contamination of air, water and soils with trace metals. Nature, 333: 134–139

29.     Pacyna, J. M. and Pacyna, E. G., (2001) An assessment of global and regional emissions of trace metals to the atmosphere from anthropogenic sources worldwide. Environ. Rev. 9:269–298.

30.     Saha J.C., Dixit A.K., Bandyopadhyay M., Saha K.C. (1999) A review of arsenic poisoning and its effects on human health”, Critical reviews in Environmental Science and Technology,           Vol. 29, No3:281-313.

31.    Singh, A. K., (2004) Arsenic contamination in groundwater of North Eastern India. In Proceedings of 11th National Symposium on Hydrology with Focal Theme on Water Quality, National Institute of Hydrology, Roorkee, pp. 255–262.

32.     Sharma, R.M. (1999) Research study on possible contamination of groundwater with Arsenic in Jhapa, Morang, and Sunsari districts of Eastern Terai of Nepal. Report of the WHO Project, DWSS, Govt of Nepal.

33.    Smith, A. H. et al. (1992) Cancer risks from arsenic in drinking water. Environ. Health Perspect., 97: 259–267.

34.    SM 3113(1999) Standard Methods for the Examination of Water and Wastewater. Metals by electrothermal atomic absorption spectrometry.

35.    SM 3114 :(1999) Standard Methods for the Examination of Water and Wastewater. Arsenic and selenium by hydride generation/atomic absorption spectrometry.

36.     SM 3120 :(1999),Standard Methods for the Examination of Water and Wastewater. Metals by plasma emission spectrometry.

37.    Smedley P.L. and David G K. (2003), Source and behaviour of arsenic in natural waters, chapter 1, Arsenic report, WHO.

38.    Smith AH, Lingas EO, Rahman M. (2000)Contamination of drinking water by arsenic in

Bangladesh: a public health emergency. Bull W H O;78(9):1093–103.

39.    Taylor, S. R. and McLennan, S. M., (1985) The Continental Crust: Its Composition and Evolution, Blackwell Scientific, London,

40.    USEPA 7063 (1996) Arsenic in aqueous samples and extracts by anodic stripping voltammetry (AVS), method 7063. U.S. Environmental Protection Agency.

41.    WHO, (1958). International Standards for Drinking-water

42.    WHO, (1963). International Standards for Drinking-water, Second edition, vol. 3

43.    WHO, (1993). Guidelines for drinking-water quality, second edition, vol. 1.

44.    WHO/International Programme on Chemical Safety. (2001). Arsenic and Arsenic Compounds. Environmental Health Criteria 224. 2nd ed. Geneva: World Health Organization

45.    Yan Chu, H., (1994) Arsenic distribution in soils. In Arsenic in the Environment, Part I: Cycling and Characterization (ed. Nriagu, J.O.), John Wiley, New York, , pp. 17–49.

4/1/2009