Table 1: Ionic Variation of groundwater in Jaipur City during monsoon season:

| CODE | pH | EC | TDS | Ca2+ | Mg2+ | Na+ | K+ | CO32- | HCO3- | Cl- | SO42- | NO3- | F- |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| S1 | 8.20 | 1482 | 738 | 52.1 | 72.96 | 140 | 3.8 | 18 | 256.2 | 207.92 | 78 | 158 | 0.18 |
| S2 | 8.25 | 580 | 290 | 32.06 | 32.83 | 31.5 | 4.3 | 12 | 183 | 44.98 | 16 | 52 | 0.2 |
| S3 | 8.32 | 426 | 213 | 48.1 | 17.02 | 9.2 | 2.1 | 12 | 146.4 | 19.99 | 32 | 39 | 0.26 |
| S4 | 7.18 | 1831 | 918 | 142.28 | 41.34 | 116.7 | 3.4 | 0 | 337.7 | 259.9 | 86 | 226 | 0.21 |
| S5 | 7.40 | 2148 | 1076 | 118.24 | 120.38 | 126.2 | 3.7 | 0 | 549 | 317.37 | 122 | 79 | 0.59 |
| S6 | 8.31 | 374 | 187 | 8.16 | 19.46 | 36 | 2.2 | 36 | 109.8 | 19.99 | 13 | 11 | 0.32 |
| S7 | 7.60 | 3004 | 1498 | 192.38 | 205.5 | 84 | 2.9 | 0 | 335.5 | 562.27 | 182 | 228 | 0.56 |
| S8 | 8.20 | 1166 | 583 | 48.1 | 46.21 | 121.4 | 1.8 | 0 | 549 | 24.99 | 63 | 54 | 0.78 |
| S9 | 7.79 | 2213 | 1106 | 266.53 | 74.28 | 60 | 3.8 | 0 | 140.3 | 392.34 | 98 | 216 | 0.14 |
| SA | 7.75 | 2737 | 1401 | 198.39 | 92.42 | 204 | 24 | 0 | 207.4 | 632.25 | 112 | 200 | 0.2 |
| SB | 8.35 | 1346 | 676 | 30.06 | 25.54 | 220 | 3.2 | 36 | 250.1 | 153 | 100 | 126 | 0.12 |

All values are in mg/L. except pH and EC

Table 2: Correlation of physico-chemical parameters of groundwater:

|  | pH | EC | TDS | Ca2+ | Mg2+ | Na+ | K+ | CO32- | HCO3- | Cl- | SO42- | NO3- |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| EC | -0.7238 |  |  |  |  |  |  |  |  |  |  |  |
| TDS | -0.7218 | 0.9998 |  |  |  |  |  |  |  |  |  |  |
| Ca2+ | -0.6907 | 0.8423 | 0.8422 |  |  |  |  |  |  |  |  |  |
| Mg2+ | -0.5642 | 0.8320 | 0.8256 | 0.6095 |  |  |  |  |  |  |  |  |
| Na+ | -0.1682 | 0.4865 | 0.4941 | 0.1181 | 0.1508 |  |  |  |  |  |  |  |
| K+ | -0.1926 | 0.4598 | 0.4773 | 0.4020 | 0.1659 | 0.4955 |  |  |  |  |  |  |
| CO32- | 0.6942 | -0.6120 | -0.6114 | -0.6970 | -0.5288 | 0.0325 | -0.2576 |  |  |  |  |  |
| HCO3- | -0.4187 | 0.3099 | 0.3047 | 0.0041 | 0.3650 | 0.3450 | -0.1667 | -0.4710 |  |  |  |  |
| Cl- | -0.6508 | 0.9546 | 0.9582 | 0.8523 | 0.7780 | 0.4213 | 0.6302 | -0.5331 | 0.0640 |  |  |  |
| SO42- | -0.6274 | 0.9317 | 0.9271 | 0.6770 | 0.8688 | 0.4974 | 0.2202 | -0.4633 | 0.4102 | 0.8347 |  |  |
| NO3- | -0.6381 | 0.8356 | 0.8340 | 0.8070 | 0.5509 | 0.4045 | 0.3428 | -0.4690 | -0.0072 | 0.8139 | 0.7418 |  |
| F- | -0.1742 | 0.1387 | 0.1328 | -0.0607 | 0.4160 | -0.0677 | -0.2471 | -0.3952 | 0.7964 | -0.0394 | 0.2466 | -0.2637 |

Table 3.Characterization of groundwater of Jaipur on the basis of Piper tri-linear diagram:

| Subdivision of the diamond | Characteristics of corresponding subdivision of diamond shaped field | Samples |
| --- | --- | --- |
|  | Alkaline earths (Ca2+ + Mg2+) exceed alkalies (Na+ + K+) | 10(All samples except SB) |
|  | Alkalies exceeds alkaline earths | 1 (SB) |
|  | Weak acids (CO32- + HCO3-) exceed strong acids) (SO42- + Cl- + F-) | 4 (S2, S3, S6 and S8) |
|  | Strong acids exceed weak acids | 7 (all samples except S2, S3, S6 and S8) |
|  | Carbonate hardness (secondary alkalinity) exceeds 50% (chemical properties are dominated by alkaline earths and weak acids) | 4 (S2, S3, S6 and S8)) |
|  | Non-carbonate hardness (secondary salinity) exceeds 50% (chemical properties are dominated by alkaline earths and strong acids) | 2 (S7 and S9) |
|  | Carbonate alkali (primary salinity) exceeds 50% (chemical properties are dominated by alkalies and weak acids) | 1 (SB) |
|  | Carbonate alkali (primary alkalinity) exceeds 50% (chemical properties are dominated by alkalies and weak acids) | 0 |
|  | No cation–anion pair exceeds 50% | 4 (S1, S4, S5 and SA) |

Table 4 Quality of irrigation water based on Electrical Conductivity:

| Salinity-hazard class | Specific conductance (µS/cm)1 | Characteristics | Samples |
| --- | --- | --- | --- |
| Low | 0-250 | Low-salinity water can be used for irrigation on most soil with minimal likelihood that soil salinity will develop. | Nil |
| Medium | 251-750 | Medium-salinity water can be used for irrigation if a moderate amount of drainage occurs. | 3 (S2, S3 and S6) |
| High | 751-2,250 | High-salinity water is not suitable for use on soil with restricted drainage. Even with adequate drainage, special management for salinity control may be required. | 6 (S1, S4, S5, S8, S9 and SB) |
| Very high | More than 2,250 | Very high-salinity water is not suitable for irrigation under normal conditions. | 2 (S7 and SA) |

1µS/cm, microsiemens per centimeter at 25 degrees Celsius.

Table 5: Quality of groundwater based on % Sodium:

| % Na | Quality of water | Samples |
| --- | --- | --- |
| <20% | Excellent | 3(S5, S7 and SB) |
| 20-40% | Good | 3(S3, S8 and SA) |
| 40-60% | Permissible | 4(S1, S2, S4 and S6) |
| 60-80% | Doubtful | 1(S9) |
| >80% | Unsuitable | Nil |

Table 6: SAR values can then be compared to characteristics of the four sodium-hazard classes as follows:

| SAR | Water-suitability for irrigation |
| --- | --- |
| 0-10 | Suitable for all types of soils except for those crops which are highly sensitive to Sodium. |
| 10-18 | Suitable for coarce textured or organic soil with good permeability. Relatively unsuitable in fine textured soil. |
| 18-26 | Harmful for almost all types of soils. Requires good drainage, high leaching and gypsum addition. |
| >26 | Unsuitable for irrigation |

Table 7: Quality of groundwater based on residual Sodium Carbonate:

| RSC | Remark the quality | Samples |
| --- | --- | --- |
| < 1.25 | Good | All samples except S6 and S9 |
| 1.25-2.5 | Doubtful | 1 ( S9) |
| >2.5 | Unsuitable | 1(S6) |

Table 8: The Value of RSC, SAR and Na %:

| CODE | RSC | SAR | Na% |
| --- | --- | --- | --- |
| S1 | Nil | 2.94 | 41.84 |
| S2 | Nil | 0.93 | 25.61 |
| S3 | Nil | 0.29 | 10.67 |
| S4 | Nil | 3.27 | 41.89 |
| S5 | Nil | 1.95 | 26.11 |
| S6 | 0.99 | 1.56 | 44.69 |
| S7 | Nil | 1 | 12.33 |
| S8 | 2.8 | 3 | 46.21 |
| S9 | Nil | 0.84 | 12.24 |
| SA | Nil | 3 | 35.15 |
| SB | 1.7 | 7.13 | 72.83 |