MATCHED QUICK SWITCHING VARIABLE SAMPLING                           SYSTEM WITH QUICK SWITCHING ATTRIBUTE                     SAMPLING SYSTEM

G.V.Sriramachandran1*, M.Palanivel2

1Department of Mathematics, Dr.Mahalingam College of Engineering and Technology, Pollachi-642 003, INDIA

(gvsriramachandran@yahoo.com)

Abtract. This paper presents a methodology for finding a Quick Switching Single Sampling variables inspection system matching a given Quick Switching attribute sampling inspection system.  Here matching implies the same Acceptance Quality Level (AQL)  and Limiting Quality Level (LQL)  of the Operating Characteristic (OC) curves for both the systems.

Keywords: Operating Characteristic Curve, Acceptance Sampling, Acceptance Quality Level and Limiting Quality Level

1. Introduction

Hamaker (1979) has given a method of constructing single sampling variables inspection plans such that the OC curve of a given single sampling attributes inspection plan and the OC of the variables plan have the same indifference quality level () and the same relative slope (h0) of the OC curve at p0.  Bender (1975) has given a table for single sampling variables inspection plans matched at the points  and  with attributes inspection plans given in TABLE II-A of MIL-STD-105D (1963). Bender (1975) achieves this matching by means of an iterative computer program involving non central t-distribution.

Romboski (1969) has studied a new system, comprising of normal and tightened plans, called Quick switching system (n;c2,c1)  [(n,c2) and (n,c1) are normal and tightened single sampling plans respectively with c2>c1 ] proposed by Dodge (1967).  Taylor (1996) investigated how to evaluate and select Quick Switching Systems. Soundarajan.V and Palanivel.M (1997) and Soundarajan.V and Palanivel.M (2000) has investigated on Quick Switching Variables Simple Sampling (QSVSS) Systems.

2. Operating Procedure

Step 1 : From a lot, take a random sample of size n and count the number of defectives, d

i) If   d accept the lot and repeat the step 1 for the next lot.

ii) If   reject the lot and go to step 2.

Step 2 : From the next lot, take a random sample of size n and count the number of defectives, d

i) If    accept the lot and  go to step 1repeat the step 1 for the next lot.

ii) If   reject the lot and repeat the step 2.

Based on this procedure, a quick switching single sampling variables inspection system can be operated as follows:

Step 1: Draw a sample of size  from the lot, inspect and record the measurement of the quality characteristic for each unit of the sample.  Compute the sample mean

If   (where U is the upper specification limit) accept the lot and repeat step 1 otherwise, reject the lot and follow step 2.

Step 2: Draw a sample of size  from the next lot, inspect and record the measurement of the quality characteristic for each unit of the sample.  Compute the sample mean,

If   accept the lot and go to step 1 otherwise, reject the lot and repeat step 2.

3. Preliminaries

According to Romboski (1969) the OC function of Quick Switching Single Sampling Attributes System (n;c2,c1) is given by

|  | (1) |
| --- | --- |

By assuming the Poisson model, one obtain

and

|  | (2) |
| --- | --- |

For a quick  switching single sampling variables inspection system QSVSS       [ (  and  ( are the normal and tightened single sampling plans respectively, with ] with known standard deviation (), the fraction non-conforming in a given lot will be

| P=F(-v) with | (3) |
| --- | --- |

and the OC function of the system has been given by

|  | (4) |
| --- | --- |

where

with

And

|  | (5) |
| --- | --- |

4. Matched QSS Variable System with Attribute System

The procedure for obtaining a Quick switching Variable Sampling Inspection System  matching a given attributes system QSS (n;c2,c1)  of Soundarajan.V and Arumainayagam S.D. (1990) is as follows:

For the QSS (n;c2,c1)  with =0.014, =0.05, =0.05 and 0.10, from  Table 1 the following values are determined.

The nearest value of 3.571 in the table is 3.5815, which has associated with it value of.  The sample size is then determined by

n=

The attributes system is designated as QSS (86,3,1)

From equation (1)

For the above system

|  | (6) |
| --- | --- |

Therefore

Similarly

|  | (7) |
| --- | --- |

Therefore

Thus the OC curve of the QSS (86,3,1) passes through . To obtain Quick switching sampling variable system we consider the OC function

where

If		then

[ From (6) & (7)]

| and 1.82 | (8) |
| --- | --- |

If		then

[From (8) & (9)]

| and | (9) |
| --- | --- |

If

Through (10)  and  (11 )  one can get

From the given Quick switching sampling attribute inspection system ( 86;3,1)  one can obtain the QSVSS as

1.

2.

3.

4.

Thus the quick switching variable sampling system (13: 1.7132, 2.068) is such that the OC curve passes through    and.

The equivalence of the OC curves is illustrated in Table 3.  Though in practice the sample size   would have to be rounded to 13, the OC curve for the Quick switching variable sampling system has been computed with the fractional value n in order to better demonstrate the closeness of the agreement of the OC curves.  One can imagine the saving of the variable system with attributes system when the sample size 13 is compared with 86.

5. Selection of variable Systems Matching Quick Switching Attribute System Indexed by AQL and LQL

Table 2 provides matched variables system to that of attributes systems indexed by AQL and LQL.  For example, for given ,  the “OR” value is 4.1666, the nearest value of 4.1666 in the Table 3.9 is 4.2069, which has associated with the attribute system n=91,   and  one can obtain the corresponding matched Quick switching  sampling variable system from Table 2 as ,  ,  and  . Table 1 provides  together with the value of .

Table 1 : Values of   for QSS

|  |  | for |  |
| --- | --- | --- | --- |
| 1 | 0 | 8.2128 | 0.3078 |
| 2 | 1 | 5.3013 | 0.7695 |
| 2 | 0 | 4.3834 | 0.6437 |
| 3 | 2 | 4.1703 | 1.3178 |
| 3 | 1 | 3.5815 | 1.2104 |
| 3 | 0 | 3.1344 | 1.0046 |
| 6 | 5 | 2.9126 | 3.2363 |
| 5 | 3 | 2.8568 | 2.4721 |
| 7 | 6 | 2.7163 | 3.9318 |
| 6 | 4 | 2.6543 | 3.1486 |
| 4 | 0 | 2.5404 | 1.3754 |
| 6 | 3 | 2.4340 | 3.0089 |
| 5 | 1 | 2.3707 | 2.0915 |
| 9 | 7 | 2.2849 | 5.2963 |
| 6 | 2 | 2.2509 | 2.8056 |
| 5 | 0 | 2.1989 | 1.7504 |
| 9 | 6 | 2.1444 | 5.1774 |
| 6 | 1 | 2.1001 | 2.5239 |
| 8 | 4 | 2.0837 | 4.2658 |
| 9 | 5 | 2.0220 | 5.0129 |
| 8 | 3 | 1.9662 | 4.0358 |
| 7 | 1 | 1.9160 | 2.9508 |
| 8 | 2 | 1.8669 | 3.7427 |
| 7 | 0 | 1.8259 | 2.5051 |
| 8 | 1 | 1.7833 | 3.3725 |
| 9 | 2 | 1.7491 | 4.1974 |
| 9 | 1 | 1.6281 | 3.7899 |
| 9 | 0 | 1.6281 | 3.2613 |
| 11 | 2 | 1.5871 | 5.0852 |
| 11 | 1 | 1.5436 | 4.6135 |
| 12 | 0 | 1.4611 | 4.3941 |

Table 2: Quick Switching Variable Sampling System Matched with Quick Switching Attribute Sampling System

|  | Attribute QSS | Variable QSS |
| --- | --- | --- |
|  | n |  |  |  |  |  |
| 8.3333 | 128 | 1 | 0 | 9 | 2.2330 | 2.5769 |
| 5.2857 | 110 | 2 | 1 | 11 | 1.9597 | 2.1714 |
| 4.4615 | 99 | 2 | 0 | 10 | 1.9064 | 2.4358 |
| 4.2069 | 91 | 3 | 2 | 16 | 1.7623 | 1.9030 |
| 3.5714 | 86 | 3 | 1 | 13 | 1.7164 | 2.0700 |
| 3.1333 | 67 | 3 | 0 | 10 | 1.5446 | 2.2538 |
| 2.9250 | 81 | 6 | 5 | 22 | 1.3985 | 1.4828 |
| 2.8438 | 77 | 5 | 3 | 18 | 1.4526 | 1.6736 |
| 2.7200 | 79 | 7 | 6 | 23 | 1.3060 | 1.3855 |
| 2.6522 | 69 | 6 | 4 | 20 | 1.3028 | 1.4945 |
| 2.5238 | 66 | 4 | 0 | 11 | 1.4100 | 2.2126 |
| 2.4390 | 73 | 6 | 3 | 19 | 1.3241 | 1.6401 |
| 2.3793 | 72 | 5 | 1 | 15 | 1.3794 | 1.9467 |
| 2.2857 | 76 | 9 | 7 | 24 | 1.1380 | 1.2789 |
| 2.2500 | 78 | 6 | 2 | 18 | 1.3542 | 1.8165 |
| 2.2000 | 70 | 5 | 0 | 13 | 1.3293 | 2.1944 |
| 2.1447 | 68 | 9 | 6 | 23 | 1.0638 | 1.2883 |
| 2.0952 | 60 | 6 | 1 | 15 | 1.1758 | 1.8582 |
| 2.0789 | 56 | 8 | 4 | 19 | 1.0100 | 1.3703 |
| 2.0263 | 66 | 9 | 5 | 22 | 1.3592 | 1.0450 |
| 1.9692 | 62 | 8 | 3 | 21 | 1.0651 | 1.5342 |
| 1.9286 | 70 | 7 | 1 | 17 | 1.1847 | 1.9097 |
| 1.8654 | 72 | 8 | 2 | 19 | 1.1419 | 1.7512 |
| 1.8095 | 119 | 7 | 0 | 18 | 1.4385 | 2.3461 |
| 1.7742 | 109 | 8 | 1 | 12 | 1.2344 | 2.2838 |
| 1.7600 | 168 | 9 | 2 | 28 | 1.5433 | 2.1039 |
| 1.7037 | 140 | 9 | 1 | 23 | 1.1431 | 2.1716 |
| 1.6316 | 172 | 9 | 0 | 25 | 1.5130 | 2.4070 |
| 1.6000 | 170 | 11 | 2 | 27 | 1.4242 | 2.1047 |
| 1.4762 | 209 | 12 | 0 | 28 | 1.4421 | 2.4526 |

Table 3 : Values of [p,L(p)] for Quick Switching Attribute Sampling System and the equivalent variable system of the proposed method

| p | L(p) of attributes QSS | L(p) of Variables QSS |
| --- | --- | --- |
| 0.01 | 0.9846 | 0.9855 |
| 0.02 | 0.8331 | 0.8107 |
| 0.03 | 0.5044 | 0.4518 |
| 0.04 | 0.2393 | 0.2224 |
| 0.05 | 0.1041 | 0.0956 |
| 0.06 | 0.0444 | 0.0434 |
| 0.07 | 0.0191 | 0.0203 |
| 0.08 | 0.0087 | 0.0099 |
| 0.09 | 0.0042 | 0.0048 |
| 0.10 | 0.0021 | 0.0024 |

Fig. 1

6. Conclusion

The methodology used in this paper could be adopted for other developed sampling system to match with other sampling system. In the shop floor, we could apply both the given attribute quick switching systems as well as variable quick switch systems. From the Table 2 and Table 3, one can conclude that the variable quick switching sampling system is better one.

Acknowledgement

The authors are grateful to the Management of Dr.Mahalingam College of Engineering & Technology for the encouragement and support in preparation of this research paper.

References:

1.  Bender, A.J. (1975): Single Sampling by variables to control the Fraction Defective- Part 2. Journal of                Quality Technology, Vol 7, No.5, pp. 71-75.

2.   DODGE, H.F. (1967): A New Dual System of Acceptance Sampling. Technical report No.16, The Statistics       Center, Rutgers – The State University, New Brunswick, NJ

3.   HAMAKER, H.C. (1979): Acceptance Sampling for Percent Defective by Variable and Attributes.  Journal       of Quality Technology, Vol.11, No.3, pp. 139-148.

4.   MIL-STD-105D, (1963): Military Standard Sampling Procedures and Tables for Inspection by Attributes,          US Government Printing Press, Washington D.C

5.  ROMBOSKI, L.D. (1969): An Investigation of Quick Switching Acceptance Sampling System. Doctoral            Dissertation Rutgers- The State University, New Brunswick, New Jersey.

6.  SOUNDARAJAN, V. and ARUMAINAYAGAM, S.D. (1990): Construction and Selection of  Modified            Quick  Switching  System. Journal  of Applied  Statistics, Vol.17, No.1, pp. 83- 114

7.  SOUNDARAJAN, V. and PALANIVEL, M. (1997): Quick Switching Variables Single Sampling (QSVSS)       System indexed by AQL and LQL: Acceptance Criterion Tightening. Journal of Applied Statistics Science,

Vol.6, No.1, pp. 45-57.

8.  SOUNDARAJAN, V. and PALANIVEL, M. (2000):  Quick  Switching Variables Single Sampling (QSVSS)

System indexed by AQL and AOQL. Journal of Applied Statistics, Vol.27, No.7, pp. 771-778

9.  TAYLOR, W.A. (1996):  Quick   Switching   Systems.  Journal  of  Quality  Technology,  Vol.28,  No.4,  pp.

460-472.

# Text boxes

Attributes   ______

Variables  - - - - - -

L(p)

p

0.1

0.09

0.08

0.07

0.06

0.05

0.04

0.03

0.02

0.01

1.2

1

0.8

0.6

0.4

0.2

0

OC curves - Attributes  QSS vs Variables QSS