RESULTS AND DISCUSSION

Investigations and experiments

By comparing the results of investigations essentially for two years(2006and 2007), organic pollutants have been found in the entire study area. A total of six relatively high concentration pollutants were found: methylene chloride, chloroform, dichloromethane, benzene, two chloro-propane and toluene.

In November 2007, the landfills PH value was 7.9, its inorganic content are in table 5.

Table 5 Inorganic ions concentration

Element                            Concentration (mg/l)                     Element                  Concentration(mg/l)

As                                     0.057                                                     Ni                            0.996

B                                    1.772                                                     P                                 20.8

Ba                                   1.321                                                     Pb                               0.0715

Ca                                   60.981                                                    S                                60.6

Cd                                  0.002                                                      Sb                              0.0905

Co                                   0.0605                                                   Se                               0.0025

Cr                                   0.263                                                     Si                               24.38

Cu                                   0.033                                                     Sr                              0.7245

Fe                                   6.3045                                                  V                               0.441

K                                    2019.668                                              Zn                             0.3555

Li                                    0.576                                                    F-                              300.54

Mg                                 78.671                                                   Cl-                            4445.958

Mn                                  0.265                                                     NO2-                         N

Mo                                    N                                                         NO3-                         N

Na                                     2023.313                                             SO42-                        172.904

*N means component note found or has a very low concentration.

The test found a high concentration of chloride ion in Jiaxing  landfills leachate (4446mg / l). And  experimental data showed different chloride ion concentrations in different layers. Absorption desorption phenomenon exists in pink sand layer while it is very weak in sand and loam layers(Figure 12 and table 6-7).

Table 6 Filtrate sample number and volume for leaching experiment.

Soil Samples              Filtrate Absorption No        Volume(ml)      Filtrate Desorption No     Volume

CLJ1                         300                           CLJJ1                    300

CLJ2                        300                            CLJJ2                   300

CLJ3                        300                            CLJJ3                    300

Sand                                              CLJ4                        300                            CLJJ4                    300

CLJ5                        300                            CLJJ5                    300

FLJ1                         238                            FLJJ1                     185

FLJ2                         200                            FLJJ2                     200

FLJ3                         208                            FLJJ3                     240

FLJ4                         212                            FLJJ4                     200

FLJ5                         212                            FLJJ5                     200

FLJ6                         216                            FLJJ6                     228

Pink                                               FLJ7                        232                             FLJJ7                     248

Sand                                               FLJ8                        229                            FLJJ8                     248

FLJ9                         200                           FLJJ9                     278

FLJ10                       205                           FLJJ9                     287

SLJ1                         57                             SLJJ1                       65

SLJ2                         41

SLJ3                         62

SLJ4                         78

Loam                                              SLJ5                         58

SLJ6                         42

SLJ7                         40

SLJ8                         43

SLJ9                         46

SLJ10                       25

Figure 11 Absorption and desorption curves of chloride ions

Table 7 Cl-concentration changes in absorption and desorption experiments of powder sand

Sample            Filtrate                      Filtrate                         Cl-content of       Sample                 Cl-content

No.                volume（ml）        concentration（mg/l）    filtrate（mg）   Concentration           (mg)

FLJ1                 238                             35.05                                   8.34                  4445.96                 1058.14

FLJ2X              200                             3941.043                             788.21              4445.96                  889.19

FLJ3X              208                             2796.18                               581.60              4445.96                  924.76

FLJ4X              212                             4431.42                               939.46              4445.96                  942.54

FLJ5X              176                             4497.72                               791.6                4445.96                  782.49

FLJ6X              216                             4457.06                               962.72              4445.96                  960.33

FJL7X              232                             4526.81                               1050.22            4445.96                 1031.46

FJL8X              229                             4416.16                               1011.30            4445.96                 1018.12

FLJ9X              200                             4436.87                               887.37              4445.96                   889.19

FLJ10               205                             4463.90                               915.10              4445.96                   911.42

FLJJ1X             185                              4373.87                              809.17               14.00                         2.59

FLJJ2X             200                              2317.44                              463.49               14.00                         2.8

FLJJ3X             240                              204.08                                48.98                 14.00                         3.36

FLJJ4X             200                                58.82                                 11.76                 14.00                       2.80

FLJJ5X             225                                50.14                                 11.28                  14.00                      3.15

FLJJ6X             228                                49.02                                 11.18                   14.00                     3.19

FLJJ7X             248                                45.03                                 11.17                  14.00                      3.47

FLJJ8X             248                                30.30                                   7.15                  14.00                      3.47

FLJJ9X             278                                28.93                                   8.04                  14.00                      3.89

FLJJ10X           287                                28.20                                   8.09                  14.00                      4.02

According to mass conservation law, the experimental adsorption of chloride ions is calculated as:

(1)

S-unit mass of soil samples the amount of chloride ion adsorption (mg / kg); i-filtrate ID; C0-AS concentration (mg / l); Vi-section No. i filtrate volume (l); Ci-section No. i filtrate concentration ( mg / l); V0-pore volume (l); M-soil quality (kg).

By the same way, we got a weak absorption-desortption in loam layer for sulfate and fluoride ions(table 8 and figure 13-14).

Table 8 Sulfate powder sand desorption-absorption test Record

Sample            Filtrate                      Filtrate                       SO42-content of       Sample          SO42-content

No.                volume (ml）        concentration（mg/l）    filtrate（mg）   Concentration           (mg)

FLJ1                 238                             29.56                                   7.02                172.90                 41.15

FLJ2X              200                             63.1995                              12.64               172.90                  34.58

FLJ3X              208                             148.91                                30.97               172.90                  35.96

FLJ4X              212                             150.86                                31.98               172.90                  36.66

FLJ5X              176                             147.79                               26.01                172.90                  30.43

FLJ6X              216                             150.83                                32.58               172.90                  37.35

FJL7X              232                             144.15                                 33.44              172.90                   40.11

FJL8X              229                             145.02                                 33.21               172.90                  39.60

FLJ9X              200                             144.16                                28.83                172.90                  34.58

FLJ10               205                             141.34                                28.98                172.90                  35.45

FLJJ1X             185                              173.70                                32.13                 28.30                   2.59

FLJJ2X             200                              114.87                                22.97                 28.30                   2.80

FLJJ3X             240                               46.31                                 11.11                 28.30                   3.36

FLJJ4X             200                                42.12                                  8.42                 28.30                    2.80

FLJJ5X             225                                44.97                                 10.12                28.30                    3.15

FLJJ6X             228                                47.66                                 10.87                28.30                    3.19

FLJJ7X             248                                46.57                                 11.55                28.30                    3.47

FLJJ8X             248                                38.15                                   9.46                28.30                    3.47

FLJJ9X             278                                43.05                                  11.97               28.30                    3.89

FLJJ10X           287                                28.20                                  12.31               28.30                    4.02

Figure 12 sulfate adsorption and desorption curves

Figure 13 Absorption and desorption curves of fluoride ion.

No absorption for nitrate ion, and its most desorption was in pink sand(Figure 15). Also the absorption of iron ion was very weak in pink sand while its desorption is very weak in sand and loam(Figure 16).

Pink sand                                                                                 loam

Sand

Figure 14 desorption curve of Nitrate ion

Figure 15 Absorption and desorption curves of iron ions

Simulation

Water level  is always high near the landfill while it is often very low far from the landfill.(Figure 17-18-19). That affected seriously the solute transport from high level to low level.

Figure 16 changes in water table in wells

Figure 17 contour map in July 2007                              Figure 18 contour map in July 2009

From the simulation results, in January 2009 the chlorine ion (10mg / l) contour lines moved northward at about 220m. And  in January 2011 they moved for about 235m. So from January 2009 to January 2011, during these two years, the 10mg / l contour moved to the north for about 15m(see table9 and Figure20-21-22).

Figure 19 chloride ion concentration changes

Table 9 chloride ion (5mg / l) expansion in the second layer

Time(period)                                                   The expansion of distance(m)

2000.1.1                                                                                    90

2002.1.1                                                                                    142

2004.1.1                                                                                    170

2006.1.1                                                                                    196

2008.1.1                                                                                    217

2010.1.1                                                                                    238

(1 January, 2009)                                           (1 January, 2010)

(1 January, 2011)

Figure 20 Chloride ion concentration in the second layer

Figure 21 Change in chloride ion (mg / l)at some sampling points

From the simulation results 0.01mg/l  of BTEX(benzene, toluene, ethylbenzene and xylene) contour line ,moved about 50m northward in 10 Years and about 84m northward in 20 years(figure 23-24-25). The main parameters of this simulation are in table 10 and the simulation times and migration distances are in table 11.

Table 10 the main parameters of the model

Parameter Name                                                     Parameter values

F2+                                                                        20.0mg/l

Methane                                                                   28mg/l

0.08day-1

0.009day-1

0.0004day-1

0.00019day-1

0.0001day-1

0.01[ML-3]

0.01[ML-3]

10[ML-3]

0.01[ML-3]

Figure 22 Landfill zone zoom after simulation

Table 11Simulation times and migration distances of BTEX(0.01mg / l )

time                                           Distance

2010/7                                   50m

2015/7                                 70m

2020/7                                 84m

July 2010                                               July 2015

July 2020

Figure 23 changes in BTEX concentration (mg / l) (enlarged simulation)

Figure 24 changes in BTEX (mg / l)

Dissolved oxygen and nitrate ion almost disappeared while sulfate and ferrous ions increased at the end of the simulation(Figure 26-27)

Dissolved oxygen                                                                  Sulfate

Ferrous ion

Figure25 concentration(mg / l) changes simulation for July 2010

Dissolved oxygen                                                              Sulfate ion

Ferrous ion                                                        Nitrate ion

Figure 26 Changes in groundwater concentration (mg/l) on Landfill site

The exploitation of shallow groundwater is mainly from local residents. In recent years, because of groundwater pollution they can not continue to increase consumption.

This landfill was not a sanitary landfill because it did not have any protection system at the bottom and the top. There was no isolation from the entry of oxygen and rainfall infiltration; so that increased leachate production. The hydrogeological structure was not indicated for landfill therefore surface and groundwater are polluted.

CONCLUSION

Jiaxing landfill has been capped and transformed into a park, but its groundwater and surface water pollution will continue for many years. Anti-seepage curtain must be built to prevent the leakage of landfill leacheate. The application of ecological methods to remove harmful substances such as the cultivation of suitable plants is also necessary.

ACKNOWLEDGEMENT

This research was supported by China Scholarship Council and China University of Geosciences, School of Environmental Studies Wuhan China. The authors wish to thank The Hydrogeology and Water Resources Department of the School of Environmental Studies of China University of Geosciences in Wuhan China and the China Scholarship Council for their support.

REFERENCES

[1]Addiscott T M and Wagenet R J. 1985. Concepts of solute leaching in soil.a review of modeling approaches. Journal of soil Science,，36:411一424. DOI: 10.1111/j.1365-2389.1985.tb00347.x

[2] Lapidus L , Amundson N R. 1952. Mathematics of adsorption in Beds[J ]. The Journal of Physical Chemistry., 56 : 984 - 988. DOI: 10.1021/j150500a014

[3] Nielsen D R , Biggar J W. 1961. Miscible displacement in soils : Ⅰ. Experimental information

[J].Soil Sci. Soc. Am. Pro, , 25: 1 - 5. http://soil.scijournals.org/cgi/content/abstract/25/1/1

[4] Nielsen D R , Biggar J W. 1962. Miscible displacement in soils: Ⅲ. Theoretical consideration[J ]. Soil Sci. Soc. Am. Pro.,26: 216 - 221. http://soil.scijournals.org/cgi/content/abstract/26/3/216

[5] P.Viotti, M. Petrangeni Papili, N.Straqualursi abd C. Gamba.2005.Contaminant transport in an unsaturated soil: laboratory tests and numerical simulation model as procedure for parameters evaluation. Ecological Modeling., Vol 182 issue 2 p 131-148. DOI:10.1016/j.ecolmodel.2004.07.014

[6]Lindstrom ,F. T. ,Haque ,R. ,Freed ,V. H. and Boersma ,L. 1967. Theory on the movement of some herbicides in soils. Environ[J]. Sci. Technol., 1 :561～565.ISBN-13:978-8493-4316-2(alk. paper)

[7]Cleary ,R. W. and Adrain ,D. D.1973. Analytical solution of the convective-dispersive equation for cation adsorption in soils. Soil Sci. Soc.Am. Proc. , ,37 :197～199. http://soil.scijournals.org/cgi/content/abstract/37/2/197

[8] J . C. Parker ,and M. T. van Genuchten. 1984. Determining transport parameters from laboratory and field tracer experiments. Virginia Agricultural Experiment Station Bulletin.,84～93

[9] Dasgupta..D； Sengupta.S； Wong, K V； Nemerow. N.1984. Two-dimensional time-dependent simulation of contaminant transport from a landfill[J]. Applied Mathematical Modelling, vol.8, no.3, pp.203-210,. Doi:10.1016/0307-904X(84)90091-X

[10] Morrison, Stan J； Tripathi, Vijay S； Spangler, Robert R.1995. Coupled reaction/transport modeling of a chemical barrier for controlling uranium(VI) contamination in groundwater[J]. Journal of Contaminant Hydrology, vol. 17, no. 4, pp.347-363. Doi:10.1016/0169-7722(94)00040-O

[11] Toride N , Leij F J . 1996. Convective2Dispersive St ream Tube Model for field - scale solute transport : Ⅰmoment analysis [J] .Soil Sci. Soc. Am. J . , 60 (2) : 342 - 352. http://74.125.155.132/scholar?q=cache:OAwCbLOtzVAJ:scholar.google.com/&hl=en&as_sdt=2000

12] Flury M.1998. Analytical solution for solute t ransport with depth dependent transformation or sorption coefficient s [J] . Water Resour. Res., 34 (11) : 2931 - 2937.

[13] Pachepsky Y A , Craeford J W, Rawls WJ. 1999. Fractal models in soil science[J] . Geoderma , , 88 : 137 - 164. ISBN:0-444-50530-x

[14] Stewart, Iris T； Loague, Keith.1999. A type transfer function approach for regional-scale pesticide leaching assessments[J]. Journal of Environmental Quality.,28,.2,378-387. http://jeq.scijournals.org/cgi/content/abstract/28/2/378

[15] Hrissi K. Karapanagioti, Chris M. Gossard, Keith A. Strevett, Randall L. Kolar and David A. Sabatini. 2001. Model coupling intraparticle diffusion/sorption, nonlinear sorption, and biodegradation processes[J]. Contaminant Hydrology.,3:1-21. Doi: 10.1016/S0169-7722(00)00179-0

[16] Vanderborght J , Vereecken H. 2007. Review of dispersivities for transport modeling in soils[J] Vadose Zone Journal., 6 :29 - 52. DOI: 10.2136/vzj2006.0096

[17] Mark L,Brusseau. 1995. The effect of nonlinear sorption on transformation of contaminants during transport in porous media[J]. Journal of Contaminant Hydrology.,17(4):277-291. DOI:10.1016/0169-7722(94)00041-F

[18] Zhihui Zhang,Mark L.Brusseau. 2004. Nonideal transport of reactive contaminants in heterogeneous porous media:7.distributed-domain model incorporating immiscible-liquid dissolution and rate-limited sorption/desorption[J].Journal contaminant hydrology., 74(1-4): 83-103.  DOI: 10.1016/j.jconhyd.2004.02.006

[19] G.R.Johnson,K.Gupta,D.K.Putz,D.K.Putz. 2003. The effect of local-scale physical heterogeneity and nonlinear,rate-limited sorption/desorption on contaminant transport in porous media[J]. Journal contaminant hydrology., 64 (1-2):35-58. DOI: 10.1016/S0169-7722(02)00103-1

[20] Leslie A Desimone,Brian L howes,Paul M Barlow. 1997. Mass-balance analysis of reactive transport and cation exchange in a plume of waster-contaminated groundwater[J].Journal of Hydrology., 203:228-249. DOI: 10.1016/S0022-1694(97)00101-7

[21] Jeonsang Hahn. 1996. Analysis of remedial alternatives of the Nanji Landfill, Korea. Environmental Geology., 28 (1) :12-21. Doi: 10.1007/s002540050073

[22] SEVGI TOKG OZ GüNES, AYSEN TURKMAN. 2007. Effect of a Hasardous Waste Landfill Area on Groundwater Quality. Air, Water and Soil Quality Modelling for Risk and Impact Assessment., 281 –292. DOI: 10.1007/978-1-4020-5877-6_26

[23] DESPINA FATTA, ACHILLEAS PAPADOPOULOS and MARIA LOIZIDOU. 1999. A STUDY ON THE LANDFILL LEACHATE AND ITS IMPACT ON THE GROUNDWATER QUALITY OF THE GREATER AREA[J]. Environmental Geochemistry and Health., 21: 175–190..DOI: 10.1023/A:1006613530137