AN INFLUENCE OF CROSSOVER OPERATOR WITH GENERATION AND POPULATION VARIATION IN GENETIC ALGORITHM FOR NETWORK DESIGN PROBLEM.

| Anand Kumar Department of Master of Computer Applications AMC Engineering College, Bangalore kumaranandkumar@gmail.com | Dr. N. N. Jani Faculty of Computer Studies Kadi Sarva Vishwavidyalya, Gandhinagar drnnjanicsd@gmail.com |
| --- | --- |

# ABSTRACT

This paper presents an influence of genetic operators (crossover) in genetic algorithm for network design problem. It also describes the performance variation with the number of generation and number of chromosomes for various different sizes of networks. A network design problem for this paper falls under the network topology category which is a degree constrained minimum spanning tree with various types of constraint demanded by the current requirement which makes it NP-hard problem. Genetic operators play an important key role in genetic algorithm approach. Since many researchers have tried to solve this problem for small to mid size, we have explored the use of genetic algorithm with various operators with modification but without changing the nature of genetic algorithm. Various crossover and mutation operators have been developed here as per the requirement of the problem and applied with the various size of network. In this paper we have tried to show that how genetic operators affects the performance of genetic algorithm and also shown that GA is an alternative solution for this NP-hard problem.

## KEY WORDS

Genetic Algorithm, Network design, Crossover, Mutation, Minimum spanning tree.

- INTRODUCTION

In Genetic Algorithm after encoding and selection the third decision to make in implementing is to use genetic operators. Genetic operators play an important key role to achieve the optimal result. It could be said that the main distinguish feature of genetic algorithm is genetic operator. This paper is the extension of work [10] and describes the importance and influence of genetic operators for network design problem. The network design problem is a NP-hard problem [2] [6] and genetic algorithm approach to design the network is one of the ultimate solutions because traditional heuristics has the limited success.  Many researchers have tried to

solve the problem [1] [3] [4]. However there is very limited research on using GA for network design with the influence of genetic operators. This paper presents the different variation in crossover and mutation operator with its impact on network size. It also describes the relationship between number of generation    and number of chromosomes generated in genetic algorithm approach. Still no researchers have tried to explore this field of genetic algorithm approach.

Network Design

In this paper network design is considered as network topology which is a degree constraint spanning tree consists of various nodes considered as vertex.  A tree is a connected graph containing no cycles.

A spanning tree of a connected, undirected graph is just a sub graph that contains all the vertices and is a tree. A graph may have many spanning trees. A minimum spanning tree (MST) is a spanning tree with weight less than or equal to the weight of every other spanning tree A MSTP can be defined as:

For an undirected connected graph

a subgraph  of   is a spanning tree of  if  is a tree.  Where  is the set of vertices and   is the set of possible edges between pair of vertices, and for each edge . There is a weight specifying the distance to connect  and . The spanning tree connects all the vertices and the total weight of the tree should be:

…………(1)

The MST algorithm may occasionally generate a minimal spanning tree where all the links connect to one or two nodes. This solution, although optimal, may be highly vulnerable to failure due to over reliance on a few nodes. Furthermore, the technology to connect many links to a node may not be available or may be too expensive. Hence, it may be necessary to limit the number of links connecting to a node. Alternatively, from reliability perspective it is desirable to have more than one link connect to a node so that alternative routes can be selected in the case of a node or link failure [5]. DCMST was specifically developed as a special case of MST with additional constraints to improve the reliability of the network and rerouting of traffic in the case of node failures. This is the extended version of minimum spanning tree problem where an extra constraint is added with each vertex. When this extra constraint is added this problem becomes NP-hard [6]. This constraint is usually motivated by the need to impose a limit on the number of ports in each node. In a shortest spanning tree resulting from the preceding construction, a vertex   can end up with any degree; that is

Where  is the total no of vertex and is the degree denoted byof a node. The degree is the number of incident edges, and the degree of a graph is the maximum degree of its nodes. The degree constrained MST problem is to determine a spanning tree of the minimum total edge cost and degree no more than a given value.

.

Genetic Algorithm

Genetic algorithms (GA) is a powerful, robust search and optimization tool, which work on the natural concept of evolution, based on natural genetics and natural selection.. Using these nature-inspired search methods it is possible to overcome some limitations of traditional optimization methods, and to increase the number of solvable problems. The application of GAs too many optimization problems in organizations often results in good performance and high quality solutions. Its working principle is completely different, compared to classical search and optimization methods. Because of its broad applicability, ease of use, and global perspective, GAs has been increasingly applied to various search and optimization problems in the recent past.  Genetic algorithms are typically implemented as a computer simulation in which a population of abstract representations (called chromosomes) of candidate solutions (called individuals) to an optimization problem evolves toward better solution. The evolution starts from a population of completely random individuals and happens in generations. This process is repeated generation by generation until the required result is not found. Most importantly of all, GAs is critically dependent on the fitness function. If we can’t define the fitness function, then we can't apply a GA.

Work flow of GA

- Initialisation of parent population.

- Evaluation

  - Self loop check

  - Isolated node or edge check

  - Cycle check

  - Path constraint

  - Degree constraint

  - Store the best result

- Selection of child population

- Apply Crossover/ Recombination

- Evaluation

- Replace the result if it is better than previously stored.

- Apply Mutation

- Evaluation

- Replace the result if it is better than previously stored.

- Go to step 3 until termination criteria satisfies

- GENETIC ALGORITHM APPROACH TO SOLVE THE PROBLEM

The Network design problem is considered as a unidirectional graph and represented with the help of adjacency matrix. Parent population in the form of chromosome is generated randomly according to the size of network.  Number of gene in a chromosome is equal to number of node in a network. The total number of chromosome may vary and it is based on user input. Here a chromosome is generated for a 10 node network. The association between nodes is considered between positions to position.

| node | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| chromosome | 2 | 10 | 4 | 9 | 6 | 7 | 5 | 9 | 8 | 3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

The logic behind association is that, the node [1] is connected with node 2; node [2] is connected with 10 and so on.

Fig-1.

From fig-1 it is clear that this is not a spanning tree because of the isolated circle.  Similarly with some other randomly generated chromosome, some other problems have been observed.

By observing these problems it has been concluded that there are five main reasons for illegal chromosome:

  - Self loop

  - Isolated node or edge

  - Cycle

  - Path constraint

  - Degree constraint

Evaluation

By observing these problems, fitness functions have been developed to evaluate these chromosomes. On the basis of these fitness functions, fitness points are given to the chromosomes and on the basis of these fitness points chromosomes are selected as a child population for next generation. Since the paper is based mainly based on genetic operators   so details of these fitness function is not given here but it is available in Anand Kumar and Dr. N.N.Jani [10].

SELECTION

After the randomly generation of parent population and its evaluation, selection is the phase of genetic algorithm which decides the child population for the next generation from the current population.  In genetic algorithm fit solution are likely to survive and bad solution are likely to die off. The purpose of selection is to emphasize the fitter individuals in the population in hopes that their offspring will in turn have even higher fitness. In this research Roulette wheel Selection   function is used for the selection of child population.

Roulette wheel Selection   :  This function selects the chromosome on the basis of roulette wheel algorithm.

S = (fitness/Avg)

Avg = Sum of fitness / no. of chromosomes.

r →(0-S).

function [new_chromosomes] =

Roulette_ wheel_selection(chromosomes)

a=size(chromosomes);

disp(chromosomes);

row = a(1);

col = a(2)-1;

r=row*round(rand());

s(row,1)=0;

temp=0;

for i=1:row

temp=temp+chromosomes(i,a(2));

end

avg=temp/row;

disp('avg');

disp(avg);

disp('**temp**');

for i=1:row

temp=(chromosomes(i,a(2))/avg);

disp(temp);

end

temp=0;

for i=1:row

temp=temp+(chromosomes(i,a(2))/avg);

s(i)=temp;

end

temp=s(i);

disp('s');

disp(s);

k=1;

for i=1:row

r=rand*temp;

disp('r');

disp(r);

for j=1:row

if(r<s(j))

for t=1:col

new_chromosomes(k,t)=chromosoms(j,t);

end

k=k+1;

break;

end

end

end

disp(new_chromosomes);

end

- GENETIC OPERATORS

This is the main part of this research paper. After the population generation, evaluation and selection of the child population this is phase of genetic algorithm which describes that how to rebuild the population with the existing resource. Genetic operators plays  important key role in genetic algorithm approach. Genetic operators: must be designed based on the problem. There are mainly two types of genetic operators but variation are available and this is the subject of research. The main two types of operators are crossover and mutation:

CROSSOVER

It could be said that the main distinguishing feature of genetic algorithm is the use of crossover. This operator randomly chooses a locus and exchanges the subsequences before and after that locus between two chromosomes to create two offspring. Single point crossover is the simplest form. The idea here is, of course to recombine building blocks on different strings. Single-point crossover has some shortcomings, though. For one thing it cannot combine all possible schemas [7].  To  reduce positional bias two- point crossover is applied in which two positions are chosen at random and the segments between them are exchanged. Two-point crossover is less likely to disrupt schemas with large defining lengths and can combine more schemas than single point crossover. In addition the segments that are exchanged do not necessarily contain the endpoints of the string. In this research work three different crossover functions have been developed.

  - Single_point _crossover:

This crossover function crossovers each pair of chromosome on a different single point. First pair of chromosome will be crossover on first column from left, similarly next second pair of chromosome is crossover on second point and so on.

function [chromosomes] = single_point_crossover(chromosomes)

a=size(chromosomes);

row = a(1);

col = a(2);

t=1;i=1;

while( i<row)

for j=1:t

temp = chromosomes(i,j);

chromosomes(i,j) = chromosomes((i+1),j);

chromosomes((i+1),j)=temp;

end

i=i+2;

t=t+1;

if(t>col)

t=1;

end

end

return;

end

  - Double_fixed-point_crossover:

This function crossovers the chromosome on fixed two different points for each pair of the chromosome.

function [chromosomes] =

double_fixed-point_crossover12(chromosomes)

disp(chromosomes);

a=size(chromosomes);

row = a(1);

col = a(2);

t=1;i=1;

p=round(rand()*col);

q=round(rand()*col);

disp('begin point');

disp(p);

if(p==0)

p=1;

end

if(q==0)

q=1;

end

disp('end point');

disp(q);

if(p>q)

p1=q;

p2=p;

else

p1=p;

p2=q;

end

while( i<row)

for j=p1:p2

temp = chromosomes(i,j);

chromosomes(i,j) = chromosomes((i+1),j);

chromosomes((i+1),j)=temp;

end

i=i+2;

t=t+1;

if(t>col)

t=1;

end

end

disp(chromosomes);

return;

end

  - Double_vary-point_crossover :

This function crossovers the chromosome on different   two different points for each pair of the chromosome. This is the variation of  Double_fixed-point_crossover.

function [chromosomes] =

double_vary-point_crossover13(chromosomes)

disp(chromosomes);

a=size(chromosomes);

row = a(1);

col = a(2);

i=1;

while( i<row)

p=round(rand()*col);

if(p==0)

p=1;

end

q=round(rand()*col);

if(q==0)

q=1;

end

if(p>q)

p1=q;

p2=p;

else

p1=p;

p2=q;

end

disp('begin point');

disp(p1);

disp('end point');

disp(p2);

for j=p1:p2

temp = chromosomes(i,j);

chromosomes(i,j) = chromosomes((i+1),j);

chromosomes((i+1),j)=temp;

end

disp(chromosomes);

i=i+2;

end

end

MUTATION

This operator randomly flips some of the bits in a chromosome. Mutation can occur at each bit position with some probability, usually, very small. This mutation operator mutates only those chromosomes which does not have the full fitness. The logic is quite simple that find the chromosome and change its value with its position. If first chromosome is selected then its first place will be replaced by maximum no (say N). If the second chromosome is selected then second place will be selected by (N-1) and so on.

function [mutated_chromosome] = mutation1(new_chromosome)

a=size(new_chromosome);

row = a(1);

k=1;

for i=1:row

if(new_chromosome(i,a(2)) ~= (a(2)+3))

new_chromosome(i,i) = (a(2)-i);

end

end

for i=1:row

for j=1:a(2)-1

mutated_chromosome(i,j) = new_chromosome(i,j);

end

end

- EXPERIMENTAL RESULT

Ten different network of size 10,60……100 have been used. Total number of chromosomes and total number of generations for each network is 100. The experiment is done in MATLAB R2008a version 7.6.0.324. All the crossover is experimented with various size of network and population –generation combination. Following tables and  figures display the result:

TABLE -1

MINIMUM COST OF NETWORK FOR VARIOUS CROSSOVER OPERATORS-NETWORK SIZE -10

| Population | generation | Single Point crossover | Double_ fixed point crossover | Double vary-point crossover |
| --- | --- | --- | --- | --- |
| 10 | 100 | 307 | 297 | 315 |
| 20 | 100 | 257 | 302 | 277 |
| 30 | 100 | 286 | 260 | 252 |
| 40 | 100 | 286 | 308 | 276 |
| 50 | 100 | 269 | 274 | 233 |
| 60 | 100 | 251 | 221 | 263 |
| 70 | 100 | 247 | 286 | 251 |
| 80 | 100 | 271 | 240 | 278 |
| 90 | 100 | 262 | 254 | 245 |
| 100 | 100 | 231 | 268 | 207 |
| 200 | 100 | 237 | 245 | 254 |
| 300 | 100 | 242 | 258 | 252 |
| 400 | 100 | 248 | 229 | 226 |
| 500 | 100 | 249 | 225 | 195 |
| 1000 | 100 | 210 | 197 | 237 |

Fig-2.

TABLE -2

MINIMUM COST OF NETWORK FOR VARIOUS CROSSOVER OPERATORS- NETWORK SIZE -10

| Population | generation | Single Point crossover | Double_ fixed point crossover | Double vary-point crossover |
| --- | --- | --- | --- | --- |
| 100 | 10 | 317 | 298 | 291 |
| 100 | 20 | 248 | 265 | 263 |
| 100 | 30 | 249 | 280 | 261 |
| 100 | 40 | 256 | 251 | 284 |
| 100 | 50 | 255 | 245 | 271 |
| 100 | 60 | 222 | 260 | 267 |
| 100 | 70 | 220 | 223 | 258 |
| 100 | 80 | 265 | 229 | 225 |
| 100 | 90 | 242 | 274 | 228 |
| 100 | 100 | 241 | 226 | 255 |
| 100 | 200 | 237 | 246 | 262 |
| 100 | 300 | 234 | 266 | 209 |
| 100 | 400 | 250 | 253 | 241 |
| 100 | 500 | 248 | 235 | 270 |
| 100 | 600 | 232 | 255 | 233 |
| 100 | 700 | 208 | 248 | 224 |
| 100 | 800 | 240 | 251 | 238 |
| 100 | 900 | 265 | 213 | 240 |
| 100 | 1000 | 254 | 272 | 256 |

Fig-3.

TABLE -3

MINIMUM COST OF NETWORK FOR VARIOUS CROSSOVER OPERATORS- NETWORK SIZE -60

| Population | generation | Single Point crossover | Double_ fixed point crossover | Double vary-point crossover |
| --- | --- | --- | --- | --- |
| 20 | 100 | 0 | 2233 | 0 |
| 40 | 100 | 2457 | 2425 | 0 |
| 60 | 100 | 0 | 2285 | 2211 |
| 80 | 100 | 2246 | 2253 | 2166 |
| 100 | 100 | 2169 | 2166 | 2273 |
| 200 | 100 | 2161 | 2091 | 2142 |
| 300 | 100 | 2014 | 2084 | 2010 |
| 400 | 100 | 2053 | 2130 | 1933 |
| 500 | 100 | 2047 | 2066 | 1954 |
| 600 | 100 | 2031 | 2177 | 2065 |
| 700 | 100 | 2041 | 2047 | 2040 |
| 800 | 100 | 2013 | 1905 | 1983 |
| 900 | 100 | 2004 | 1983 | 2105 |
| 1000 | 100 | 1962 | 2032 | 2041 |

Fig-4.

TABLE -4

MINIMUM COST OF NETWORK FOR VARIOUS CROSSOVER OPERATORS- NETWORK SIZE -60

| Population | generation | Single Point crossover | Double_ fixed point crossover | Double vary-point crossover |
| --- | --- | --- | --- | --- |
| 100 | 10 | 0 | 0 | 2161 |
| 100 | 20 | 2133 | 2364 | 2386 |
| 100 | 30 | 2179 | 2212 | 2190 |
| 100 | 40 | 2189 | 2178 | 2170 |
| 100 | 50 | 2203 | 2201 | 2284 |
| 100 | 60 | 2061 | 2074 | 2187 |
| 100 | 70 | 2276 | 2216 | 2209 |
| 100 | 80 | 2248 | 2256 | 2151 |
| 100 | 90 | 2084 | 2013 | 2059 |
| 100 | 100 | 2254 | 2145 | 2092 |
| 100 | 200 | 2226 | 2218 | 2184 |
| 100 | 300 | 2081 | 2111 | 2234 |
| 100 | 400 | 2212 | 2152 | 2381 |
| 100 | 500 | 2076 | 2083 | 2245 |
| 100 | 600 | 2228 | 2151 | 2121 |
| 100 | 700 | 2140 | 2106 | 2139 |
| 100 | 800 | 2123 | 2180 | 2107 |
| 100 | 900 | 2134 | 2154 | 2144 |
| 100 | 1000 | 0 | 2238 | 2064 |

Fig-5.

TABLE -5

MINIMUM COST OF NETWORK FOR VARIOUS CROSSOVER OPERATORS- NETWORK SIZE -100

| Population | generation | Single Point crossover | Double_ fixed point crossover | Double vary-point crossover |
| --- | --- | --- | --- | --- |
| 100 | 10 | 0 | 0 | 0 |
| 100 | 20 | 0 | 0 | 0 |
| 100 | 30 | 0 | 0 | 0 |
| 100 | 40 | 0 | 3789 | 3256 |
| 100 | 50 | 0 | 0 | 0 |
| 100 | 60 | 0 | 0 | 0 |
| 100 | 70 | 0 | 0 | 0 |
| 100 | 80 | 0 | 0 | 0 |
| 100 | 90 | 3883 | 0 | 0 |
| 100 | 100 | 0 | 0 | 0 |
| 100 | 200 | 0 | 0 | 0 |
| 100 | 300 | 0 | 0 | 0 |
| 100 | 400 | 0 | 0 | 3456 |
| 100 | 500 | 0 | 0 | 0 |
| 100 | 600 | 0 | 0 | 0 |
| 100 | 700 | 0 | 0 | 0 |
| 100 | 800 | 4356 | 0 | 4123 |
| 100 | 900 | 0 | 0 | 0 |
| 100 | 1000 | 0 | 3245 | 0 |

Fig-6.

TABLE -6

MINIMUM COST OF NETWORK FOR VARIOUS CROSSOVER OPERATORS- NETWORK SIZE -100

| Population | generation | Single Point crossover | Double_ fixed point crossover | Double vary-point crossover |
| --- | --- | --- | --- | --- |
| 50 | 100 | 0 | 0 | 0 |
| 100 | 100 | 0 | 0 | 3768 |
| 200 | 100 | 0 | 0 | 3478 |
| 300 | 100 | 3877 | 3855 | 3659 |
| 400 | 100 | 3666 | 3543 | 3624 |
| 500 | 100 | 3767 | 3874 | 3693 |
| 600 | 100 | 4013 | 3669 | 3547 |
| 700 | 100 | 3886 | 3335 | 3699 |
| 800 | 100 | 3692 | 3998 | 3678 |
| 900 | 100 | 3673 | 3321 | 3378 |
| 1000 | 100 | 3819 | 3330 | 3221 |

Fig-7.

- CONCLUSIONS

From the above experimental result of Table-1 to  Table-6 and the figure1 to figure7, following conclusions have been made.

- For the smaller size network (Network Size 10), there is possibility of better result with the maximum generation and maximum population and double fixed point crossover.

- For the medium size network (Network Size 60), there is possibility of better result with the maximum generation and all the crossover function has almost same impact.

- For the larger size network (Network Size 100), there is possibility of better result with only  maximum population and double  point crossover (fixed and varying)

Acknowledgements

Our thanks to the reviewers for their cogent and insightful comments.

References

- M. Gruber and G. Raidl. A new 0.1 ILP approach for the bounded diameter minimum spanning tree problem. In L. Gouveia and C. Mour.ao, editors, Proc. of the Int. Network Optimization Conference, volume 1, pages 178.185, Lisbon, Portugal, 2005.

- Ellis Horwitz, Sartaj Sahni and Sanguthevar Rajasekaran, Computer algorithms, University Press,2007

- Rajeev Kumar and Nilanjan Banerjee, Multicriteria Network Design UsingEvolutionary Algorithm, GECCO 2003, LNCS 2724, pp. 2179–2190, 2003.Springer-Verlag Berlin Heidelberg 2003.

- Lixiar Hanr and Yuping wang, A Novel genetic algorithm for degree constrained minimum spanning tree problem, International Journal of Computer science and network security, VOL 6 No. 7A, July 2006

- F. Harary and J. P. Hayes, “Node fault tolerance in graphs,” Networks, vol. 27, no. 1, pp. 19–23, 1996.

- S.K. Basu, 2005. Design Methods and Analysis of algorithms (PHI) ISBN :  81-203-2637-7

- Melanie M. (1998). An Introduction to genetic Algorithm    (PHI ) ISBN 81-203-1385-5

- Michael D. Vose. 1999. The simple genetic algorithm : (PHI) ISBN 61-203-2459-5

- Narsingh Deo, 2000. Graph Theory with Applications to Engineering and Computer science: (PHI)

- Anand Kumar, Dr. N.N.Jani,  Proceeding of the International Conference on Mathematics and Computer Science ICMCS FEB 2010, ISBN: 978-81-908234-2-5Chennai.

*******************