Dr. O.I. Popoola

Lecturer, Deparment of Physics, University of Ibadan, 211001, Nigeria.

Email: iopopoola@yahoo.com

Dr. J.A. Adegoke

Lecturer, Deparment of Physics, University of Ibadan, 211001, Nigeria.

Email: adegokeja@yahoo.com

Mr. O.O. Alabi

Lecturer, Department of Physics, 2College of Science, Engineering and Technology, Osun State University, Osogbo, 230001, Nigeria.

Email: geosciencealabi@yahoo.com

Mr. F.O. Akinluyi

Lecturer, Department of Physics, Adeyemi College of Education, 351001, Nigeria

Email: akinluyi18370@alumni.itc.nl

Engineer, K.A. Fayemiwo

Lecturer, Department of Industrial Engineering, 2College of Science, Engineering and Technology, Osun State University, Osogbo, 230001, Nigeria.

Email: kfayemiwo@yahoo.ca

Controlling Contaminated Fluid From Polluting

Groundwater using Porous Media.

1O.I. Popoola ,1J.A. Adegoke, 2*O.O. Alabi, 3*F.O. Akinluyi, and 2K.A. Fayemiwo

1Deparment of Physics, University of Ibadan, 211001, Nigeria.

2College of Science, Engineering and Technology, Osun State University, Osogbo, 230001, Nigeria.

3Physics Department, Adeyemi College of Education, 351001, Nigeria.

Akinluyi18370@alumni.itc.nl; geosciencealabi@yahoo.com

Abstract: The study of movement of underground water helps to predict the flow of contaminated fluid from a solid waste landfill into a portable water supply. Sand  samples from river bed were used as stratified porous media and a laboratory experiment was set up to look at the deflection pattern in term of volume of liquid flowing across a unit cross-sectional area per unit time at different angles. Water was made to flow through the inlet and outlet pipes filled with sands of different porosities and the volume of water discharge was determined by volumetric method. A graph of cosine of angle of deflection against porosity ratio gives a relation cos  = 1.98ln  + 1.13. With this established equation, a stratified porous media of known porosity ratio can be used to control the direction of contaminated fluid in sub-surface layer.

Key words: porosity, inclination angle, volume flux, deflection, outlet angle

1.    Introduction

There are three major wastewater disposed techniques. They are treatment and discharge into surface waters, treatment and reuse and land disposal via septic tanks and spray irrigation (Henry, 2003). Major consideration will be given to land disposal of sewage in this study. The major factor influencing the suitability of the soil for filter field use is the water-saturated hydraulic conductivity.

Sewage effluent may move so rapidly in high hydraulic conductivity sand and disease organisms are not destroyed before shallow- water supplies become contaminated. Soils with low hydraulic conductivity are not suited for septic drain fields, because the sewage effluent may saturate soil and contaminate the surface soil (Henry, 2003). Thus, there is a need to seek for better or suitable soil filter for the field.

Heterogeneous medium is used as protective filter and drainage control medium, for example when a small amount of clay is mixed with sand in man- made constructions (Sower and Sower, 1970 and Cedergreen, 1976). However, it has been observed that under the same hydraulic gradient, layered (stratified) heterogeneous medium serves better than mixed heterogeneous medium (Popoola et al, 2008). In another experiment, it was observed that layered heterogeneous medium arranged in descending order of porosity from bottom serves better and gives the relationship between maximum volume flux (or specific discharge) qmax and porosity ratio r as qmax  = 37.89 -18.39 (Popoola et al, 2008)

The purpose of this work is to device a means to deflect the sewage effluent from the direction of  water supplies by using layered (or stratified) heterogeneous medium by establishing the relationship between angle  of deflection (θ) and porosity ratio which  can be used to control the direction of flow of contaminated fluid or sewage effluent in sub-surface groundwater.

2.    Theoretical Background

When streamlines from a medium of a given hydraulic conductivity K1 cross the boundary of a medium with different hydraulic conductivity K2, they are refracted in a manner similar to optical refraction of light rays. The refraction follows the law

(1)

( Casagrande, 1937 and Cedergreen, 1976)

where

θ1 = angle between the normal line and the incident line in medium of hydraulic conductivity K, and

θ2 = angle between the normal line and the refraction line in medium of hydraulic conductivity K2

The flow lines deflect to conform to equation

(Cedergreen, 1976)		(2)

Where

( = angle between the flow line in medium 1

and the boundary ( or interface)

(  = angle between the deflected flow line in

medium 2 and the boundary

k1  =  permeability of medium 1

k2  =  permeability of medium 2

.

Figure. 1: Schematic diagram to show the relationship between refracted angle and deflection angle.

The equation 1 above is used to construct flow net, which can be used to solve drainage and seepage problem by civil engineers (Cedergreen 1976). However this can only be used to reduce the seepage but not to deflect the fluid. Also, it is has been found that permeability varies with porosity and gradient (Popoola et al, 2007). Thus a simple parameter like porosity that can be easily determined in the laboratory will be used in the new equation to be established. The same concept is viewed in another way from the fundamental optical principle (Snell’s law) to explain fluid flow in a medium of two strata of different porosity vis-à-vis hydraulic conductivity.

.    	By using Snell’s law in optics, another equation which relates   angles ( and ( with porosity is obtained as

(3)

Where  and

( = angle between the flow line and the boundary in medium 1

( = angle between the deflected flow line and the boundary in medium 2

( = angle between the normal line and the flow line in the medium

(1= porosity of medium 1 (fined-grained medium)

(2= porosity of medium 2 (coarse-grained medium)

q1= volume flux in medium 1 and

q2= volume flux in the medium 2

In other to make the equation relevant to the experimental set up for the purpose of application, angle  is assumed to be 900 (laminar flow) and related with angle  (Figure. 1).

Then equation (3) becomes

(4)

Where porosity ratio

This shows that deflection angle θ is related with porosity ratio as written above.

This equation (4) can now be used as the basis for this work.

3.    Material and Method

Sand samples were collected from two rivers, processed and sieved into five different sizes so as to have different porosities. Porosity of these samples were obtained by volumetric approach and the results are presented in Table 1.

Figure.2: Schematic Diagram of set-up to determine volume flux at different outlet angles.

A modelled experiment was performed in the laboratory using riverbed sand of varying porosities. A set-up (Figure 2) consisting of a big transparent cylindrical pipe 108.5cm long with radius 2.23cm was used as inlet pipe while five small equal cylindrical pipe of radii 0.3cm were used as outlet pipes, which were joined to the circular plastic plate on the top of the inlet pipe at angle ( of 00, 200, 500, 700 and 900.  Water was allowed to flow through this set-up without any porous media. This serves as control experiment and thereafter the inlet and outlet pipes were filled with the sand of the same porosity. Then, outlet pipes were filled with soil of the same porosity while the inlet pipe was filled with another soil of different porosity.  The volume of water discharged through each outlet pipe for 60seconds was collected with beaker and measured with measuring cylinder. This experiment was repeated for different tilt angles ( = 00, 5.00, 10.00, 15.00 and 200 for five different samples. .This was done in order to examine the effect of angle of inclination on angle of deflection of flow in the porous media. The volumetric flow rate and volume flux were later computed from the values of volume discharged. The outlet with maximum volume flux with respect to each porosity ratio was noted, which is an indication of angle of deflection. The results obtained were presented in table 2 – 12

Fig. 3: Experimental set-up to determine volume flux at different outlet angles.

4.    Results and Analysis

Tables 1: Porosities of the samples

| S/No | Sample | Porosity |
| --- | --- | --- |
| 1 | A | 0.250 |
| 2 | B | 0.333 |
| 3 | C | 0.364 |
| 4 | D | 0.400 |
| 5 | E | 0.420 |

Table 2:  Volume Flux at different Outlet angles for Porosity Ratio 0.5952 i.e.

| Angle of inclination (/ Degree | Outlet Angle (/degree |
| --- | --- |
|  | 0 q x 10-3 (ms-1) | 20 q x10-3 (ms-1) | 50 q x 10-3 (ms-1) | 70 q x 10-3 (ms-1) | 90 q x 10-3 (ms-1) |
| 0 | 0 | 0 | 0 | 0 | 0 |
| 5 | 0.43 | 0.92 | 1.08 | 1.06 | 1.30 |
| 10 | 1.02 | 1.93 | 2.59 | 2.78 | 3.42 |
| 15 | 1.10 | 2.11 | 3.85 | 4.52 | 5.11 |
| 20 | 1.46 | 2.48 | 4.01 | 5.47 | 6.27( |

Table 3:  Volume Flux at different Outlet angles for Porosity Ratio 0.6250 i.e.

| Angle of inclination (/ Degree | Outlet Angle (/degree |
| --- | --- |
|  | 0 q x 10-3 (ms-1) | 20 q x10-3 (ms-1) | 50 q x 10-3 (ms-1) | 70 q x 10-3 (ms-1) | 90 q x 10-3 (ms-1) |
| 0 | 0 | 0 | 0 | 0 | 0 |
| 5 | 0.24 | 0.87 | 1.26 | 1.06 | 0.35 |
| 10 | 0.35 | 1.61 | 1.30 | 3.14 | 0.49 |
| 15 | 0.71 | 2.16 | 3.14 | 4.64 | 0.71 |
| 20 | 0.75 | 2.52 | 4.83 | 5.95( | 1.43 |

Table 4:   Volume Flux at different Outlet angles for Porosity Ratio 0.6868 i.e.

| Angle of inclination (/ Degree | Outlet Angle (/degree |
| --- | --- |
|  | 0 q x 10-3 (ms-1) | 20 q x10-3 (ms-1) | 50 q x 10-3 (ms-1) | 70 q x 10-3 (ms-1) | 90 q x 10-3 (ms-1) |
| 0 | 0 | 0 | 0 | 0 | 0 |
| 5 | 0 | 0.59 | 0.73 | 0.98 | 0.25 |
| 10 | 0.13 | 1.02 | 0.96 | 2.71 | 0.35 |
| 15 | 0.15 | 1.26 | 1.18 | 4.48 | 0.75 |
| 20 | 1.70 | 1.65 | 6.22( | 4.60 | 1.30 |

Table 5:    Volume Flux at different Outlet angles for Porosity Ratio 0.7508 i.e.

| Angle of inclination (/ Degree | Outlet Angle (/degree |
| --- | --- |
|  | 0 q x 10-3 (ms-1) | 20 q x10-3 (ms-1) | 50 q x 10-3 (ms-1) | 70 q x 10-3 (ms-1) | 90 q x 10-3 (ms-1) |
| 0 | 0 | 0 | 0 | 0 | 0 |
| 5 | 0.13 | 0.71 | 0.74 | 0.63 | 0.12 |
| 10 | 0.24 | 0.75 | 0.82 | 0.75 | 0.20 |
| 15 | 0.61 | 0.75 | 2.24 | 1.46 | 0.43 |
| 20 | 0.62 | 0.82 | 4.91( | 3.14 | 0.75 |

Table 6: Volume Flux at different Outlet angles for Porosity Ratio 0.7929 i.e.

| Angle of inclination (/ Degree | Outlet Angle (/degree |
| --- | --- |
|  | 0 q x 10-3 (ms-1) | 20 q x10-3 (ms-1) | 50 q x 10-3 (ms-1) | 70 q x 10-3 (ms-1) | 90 q x 10-3 (ms-1) |
| 0 | 0 | 0 | 0 | 0 | 0 |
| 5 | 0 | 0.16 | 4.36 | 1.85 | 0.90 |
| 10 | 0.12 | 1.85 | 5.11 | 3.93 | 2.43 |
| 15 | 1.26 | 2.71 | 6.11 | 5.13 | 3.40 |
| 20 | 2.64 | 3.40 | 11.98( | 10.96 | 5.70 |

Table 7:   Volume Flux at different Outlet angles for Porosity Ratio 0.8325 i.e.

| Angle of inclination (/ Degree | Outlet Angle (/degree |
| --- | --- |
|  | 0 q x 10-3 (ms-1) | 20 q x10-3 (ms-1) | 50 q x 10-3 (ms-1) | 70 q x 10-3 (ms-1) | 90 q x 10-3 (ms-1) |
| 0 | 0 | 0 | 0 | 0 | 0 |
| 5 | 0 | 0 | 4.01 | 1.61 | 0.43 |
| 10 | 0 | 0 | 4.95 | 3.73 | 1.85 |
| 15 | 0.90 | 1.02 | 5.07 | 4.91 | 3.65 |
| 20 | 1.26 | 2.59 | 11.43( | 10.96 | 4.56 |

Table 8:  Volume Flux at different Outlet angles for Porosity Ratio 0.8667

| Angle of inclination (/ Degree | Outlet Angle (/degree |
| --- | --- |
|  | 0 q x 10-3 (ms-1) | 20 q x10-3 (ms-1) | 50 q x 10-3 (ms-1) | 70 q x 10-3 (ms-1) | 90 q x 10-3 (ms-1) |
| 0 | 0 | 0 | 0 | 0 | 0 |
| 5 | 0 | 6.13 | 1.89 | 0.90 | 0.61 |
| 10 | 0.16 | 9.10 | 4.56 | 2.71 | 2.04 |
| 15 | 1.34 | 12.45 | 7.35 | 6.09 | 5.35 |
| 20 | 3.07 | 15.52( | 12.65 | 7.33 | 6.09 |

Table 9:  Volume Flux at different Outlet angles for Porosity Ratio 0.9100

| Angle of inclination (/ Degree | Outlet Angle (/degree |
| --- | --- |
|  | 0 q x 10-3 (ms-1) | 20 q x10-3 (ms-1) | 50 q x 10-3 (ms-1) | 70 q x 10-3 (ms-1) | 90 q x 10-3 (ms-1) |
| 0 | 0 | 0 | 0 | 0 | 0 |
| 5 | 0.20 | 2.71 | 1.85 | 1.43 | 0 |
| 10 | 2.43 | 5.07 | 3.14 | 1.46 | 0.12 |
| 15 | 6.11 | 8.40 | 4.29 | 2.64 | 1.61 |
| 20 | 7.19 | 8.67( | 4.36 | 3.92 | 1.02 |

Table 10:  Volume Flux at different Outlet angles for Porosity Ratio 0.9148

| Angle of inclination (/ Degree | Outlet Angle (/degree |
| --- | --- |
|  | 0 q x 10-3 (ms-1) | 20 q x10-3 (ms-1) | 50 q x 10-3 (ms-1) | 70 q x 10-3 (ms-1) | 90 q x 10-3 (ms-1) |
| 0 | 0 | 0 | 0 | 0 | 0 |
| 5 | 2.48 | 0.90 | 0.90 | 0.75 | 0 |
| 10 | 5.13 | 1.89 | 2.43 | 1.89 | 0 |
| 15 | 8.31 | 2.71 | 2.64 | 2.43 | 0.12 |
| 20 | 8.41( | 7.35 | 5.11 | 4.29 | 0.12 |

Table 11:  Volume Flux at different Outlet angles for Porosity Ratio 0.9523

| Angle of inclination (/ Degree | Outlet Angle (/degree |
| --- | --- |
|  | 0 q x 10-3 (ms-1) | 20 q x10-3 (ms-1) | 50 q x 10-3 (ms-1) | 70 q x 10-3 (ms-1) | 90 q x 10-3 (ms-1) |
| 0 | 0 | 0 | 0 | 0 | 0 |
| 5 | 7.88 | 2.43 | 1.26 | 0 | 0 |
| 10 | 11.02 | 5.35 | 4.29 | 0.20 | 0 |
| 15 | 16.82 | 8.41 | 7.19 | 2.48 | 0.12 |
| 20 | 17.80( | 8.57 | 8.31 | 6.01 | 0.16 |

* Maximum volume flux with respect to each porosity ratio.

Table 12:  The outlet angle with the maximum volume flux, which indicates the direction of fluid flow with respective porosity ratio.

| Porosity ratio | Angle of Deflection, Cosθ (/Degree |
| --- | --- |
| 0.9523 | 0 1 |
| 0.9148 | 0 1 |
| 0.9100 | 20 0.9397 |
| 0.8667 | 20 0.9397 |
| 0.8325 | 50 0.6428 |
| 0.7929 | 50 0.6428 |
| 0.7508 | 50 0.6428 |
| 0.6868 | 70 0.3420 |
| 0.6250 | 70 0.3420 |
| 0.5952 | 90 0 |

Figure 4: Cos against porosity ratio

The cosine of angle of deflection for respective porosity ratios were obtained and presented in table 12. The cos θ was plotted against the porosity ratio and the equation obtained is .This equation established the relationship between θ and. From this equation, the maximum angle of deflection in stratified porous medium made up of fine and medium sand is 89.4o. This is true because the minimum value of porosity ratio is 0.5682 (0.25 / 0.44) for medium and fine sands (Freeze and Cherry, 1979).

It is now obvious that if porosity ratio of a stratified (or layered) porous medium is known, the angle of deflection of fluid flow through that media can be determined from the above equation.

5.    Conclusion and Recommendation

From these results, it is reasonable to conclude that a stratified porous media of a known porosity ratio can be used to control the direction of contaminated or unwanted fluid . This can be done by excavating the region between the source of water supply and contaminant and backfill with stratified porous media (or layered soils) of known porosities. However, the contributions or suggestions of building or civil engineering department would be necessary for full application or implementation of these fundamental results.

Acknowledgement

We hereby acknowledged the effort of Mr. Ariyo of Mechanical and Maintenance Department of Physics, University of Ibadan, West-Africa, for the assistance rendered in constructing the experimental set-up used for this experiment.

Correspondence to:

Akinluyi Francis O.

Department of Phsics

Adeyemi College of Education

Ondo, 351001, Nigeria

Cellular phone: 00234-8033596566

Emails: akinluyi18370@alumni.itc.nl; fakinluyi@yahoo.com

REFERENCES

[1]	Casagrande A. Seepage through Dams. Journal of the New England water Works Association 1937: 	209.

[2]	Cedergreen H.R. Seepage, Drainage and Flow Nets. 2nd Edition Willy Interscience Publication, New 	York. 1976: 101-103.

[3]	Freeze R.A. and Jerry J.A. Groundwater. Prentice –Hall, Inc. Englewood Cliffs, N.J. 1979: 604

[4]	Henry D.F. (2003) Fundamental of Soil Science (Water waste disposal). 8th Edition John Wiley and 	Sons, New York. 2003: 94-95.

[5]	Popoola I.O., Adegoke J. A. and Alabi O.O. A Laboratory Study of the Effect of Porosity on the 	Deviation from Darcy’s Law in Saturated Porous Media. Journal of Applied Sciences 2007; 2 (8): 892-	899.

[6]	Popoola I.O., Adegoke J.A. and Alabi O.O. Studying the Permeability of Saturated Homogenous and 	Heterogeneous Porous Media. Journal of Research in Physical Sciences 2008; 4(4): 149-157.

[7]	Sowers G.B. and Sowers G.F. Introductory Soil Mechanics and Foundation. 3rd Edition Macmillan 	publishing Company Inc, New York. 1970: 85-87.

# Text boxes

Normal

(

(

(

1

60cm

60cm

108.5 cm

Soil sample B of (B

Inlet pipe

Soil sample A of (A

h

Note:

As h is varied  ( increases

(   =   angle of inclination. ( = 00, 50, 100, 150 and 200

(1  = 	 00   to the normal

(2  = 	200 	“

(3  = 	500 	“

(4  = 	700	 “

(5  =	 900 	“

(

5

4

3

2

(1

(2

(5

Outlet pipe

4.46cm

diameter of inlet pipe

ow pipe

0.6cm

diameter of outlet pipe

(4

(3