Optimization Of Asparaginase Production By

Pseudomonas Aeruginosa Using Experimental Methods

R. Manikandan*‡, CN Pratheeba† and Pankaj Sah ‡

* Department of Biotechnology, Mepco Schlenk Engineering College, Sivakasi, TN (India)

† Department of Chemical Engineering, Kalasalingam University, TN (India)

‡ Department of Applied Sciences, Higher College of Technology, Muscat                         (Sultanate of Oman)

GSM: +96896643648

Email: pankaj@hct.edu.om

drpankaj_sah2002@yahoo.com

Abstract

Aims: Evaluation of fermentation process parameter interactions for the production of l-asparaginase by Pseudomonas aeruginosa.

Methods and Results: Box-Behnken design of experimentation was adopted to optimize nutritional sources, physiological (incubation period) and microbial (inoculum level).The experimental results and software predicted enzyme production values were comparable.

Conclusion: Incubation period, inoculum level and nutritional source (soybean) were major influential parameters at their individual level. Interaction data of the selected fermentation parameters could be classified as least and most significant at individual and interactive levels.

Significance and Impact of the Study: All selected factors showed impact on

l-asparaginase enzyme production by this isolated microbial strain either at the individual or interactive level. Incubation temperature, inoculums concentration, and nutritional source (soybean) had impact at individual level. Significant improvement in enzyme production by this microbial isolate was noted under optimized environment.

1. Introduction:

L-Asparaginase has received increased awareness in current years for its anticarcinogenic potential. Cancer cells distinguish themselves from normal cells in diminished expression of l-asparagine (Swain et al. 1993; Manna et al. 1995). Hence, they are not capable of producing l-asparagine, and mainly depend on the l-asparagine from the circulating plasma pools (Swain et al. 1993).l-Asparaginase (l-asparagine amidohydrolase EC 3.5.1.1) catalyses the conversion of l-asparagine to l-aspartate and ammonium, and this catalytic reaction is essentially permanent under physiological conditions. If l-asparaginase is given to cancer patients then there will be nonstop reduction of l-asparagine. This extradinary behaviour of cancerous cells was broken by scithefic community (Story et al. 1993; Swain et al. 1993). Asparaginase is used for treating acute lymphoblastic leukemia, lymphosarcoma. This therapy brought a major breakthrough in modern oncology. With the development of its new functions, a great demand for l-asparaginase is expected in the coming years. The biochemical and enzyme kinetic properties vary with the microbial source. However, Erwinia asparaginase had a shorter half life than E. coli (Asselin et al. 1993); suggesting the need to discover new l-asparaginases that are serologically different, but have similar beneficial effects. This requires selection of soil samples from various sources for isolation of possible microbes, which have the ability to produce the most wanted enzyme.

Experimental designs nowadays have been regarded as one of the most favorable techniques in covering a large area of practical statistics and obtain unambiguous results with the least expense. Response surface method (RSM) designs help to quantify the relationships between one or more measured responses and the vital input factors. The most popular response surface methodologies are Central Composite, Box-Behnken designs.

Box-Behnken design is an efficient and creative three-level composite design for fitting second-order response surfaces. It is an independent quadratic design. The methodology is based on the construction of balance designs which are rotatable and enable each factor level to be tested several times. Each factor or independent variable can be placed at one of three equally spaced values (coded as –1, 0, and +1). In this design the treatment combinations are at the midpoints of edges of the cubical design region and at the center. Box-Behnken designs provide excellent predictability within the spherical design space and require fewer experiments compared to the full factorial designs or central composite designs. The number of required experiments for Box-Behnken design can be calculated according to N = k2 + k + cp, where k is the factor number and cp is the replicate number of the central point.

In the present investigation, we study about optimization of asparaginase production by Pseudomona aeruginosa using design of experiments by Box-Benhken Design.

2. Materials and methods:

2.1 Maintenance and cultivation of Microorganism

The strain Pseudomonas aeruginosa was obtained from NCIM, Pune, India. The strain was subcultured in nutrient broth. The broth was incubated in the shaker with 175 rpm and at 37C overnight. Sterile plates containing nutrient agar of specified composition were streak plated with the overnight cultures.In 100 ml nutrient broth, the cultures are grown overnight.The culture on the broth was used as the source for the entire experiment.Cultivation was achieved by solid-state fermentation (SSF) as previously reported by Ramesh and Lonsane (1987).2.24 g  of  soyabean  is  moistened  with  5 ml  of  phosphate buffer  containing culture.The plates are incubated for 48 hrs  &  are checked for enzyme activity.

2.2 Estimation of L-asparaginase activity

Reaction mixture consisting of  0.5 ml  of  0.08 mol/l  of  1 l-asparagine, 1ml of  0.05mol/l  borate buffer (pH 7.5) and 0.5 ml of enzyme solution was incubated for  10 min at 37 0C. The reaction was stopped by the addition of  0.2 ml of  15% trichloroacetic acid solution. The liberated ammonia was coupled with 1 ml Nessler’s reagent & OD is measured at 500 nm, and was quantitatively determined using standard curve.

2.3 Optimization of the process parameters

Process optimization was carried out by conducting 17 experiments to identify the best combinations of the parameters which involved in the production biomass to obtain high yield of crude extract. The parameters, soybean (10, 12.5,15 gms), inoculums (300, 450, 600 µl) and incubation (48, 72, 60 h) were selected. 17 different cultures were obtained by varying the three parameters. The concentration of the enzyme was measured using standard plot. The data obtained from 17 experiments, were used to find out the optimum point of the process parameters by using Box-Behnken Design in Response surface methodology. All the data were treated with the aid of Design Expert from Stat-Ease.

3.RESULTS AND DISCUSSION

3.1 Analysis of variance

Based on design of experiment, 17 combination were developed (Table 1) and processed to obtain asparaginase as mentioned in this paper. The data obtained from the experiments were used to the analysis of variance (Table 2 and 3). The Model F-value of 6.366E+007 implies the model is significant.  There is only a 0.01% chance that a "Model F-Value" this large could occur due to noise. Values of "Prob > F" less than 0.0500 indicate model terms are significant.   In this case A, B, C, AB, AC, BC, A2, B2, C2, A2B, A2C, AB2are significant model.

Table 1 Combination of process variables

| Run | A:Soybean (g) | B:Incubation (h) | C:Inoculum (µl) | Asparaginase (mg/ml) |
| --- | --- | --- | --- | --- |
| 1 | 10 | 72 | 450 | 6.448 |
| 2 | 10 | 48 | 450 | 5.485 |
| 3 | 15 | 60 | 600 | 6.770 |
| 4 | 10 | 60 | 600 | 6.847 |
| 5 | 12.5 | 60 | 450 | 5.566 |
| 6 | 12.5 | 60 | 450 | 5.566 |
| 7 | 12.5 | 60 | 450 | 5.566 |
| 8 | 12.5 | 48 | 600 | 6.393 |
| 9 | 15 | 72 | 450 | 5.030 |
| 10 | 15 | 60 | 300 | 6.550 |
| 11 | 12.5 | 72 | 300 | 5.736 |
| 12 | 12.5 | 48 | 300 | 6.640 |
| 13 | 10 | 60 | 300 | 4.479 |
| 14 | 12.5 | 60 | 450 | 5.566 |
| 15 | 12.5 | 60 | 450 | 5.566 |
| 16 | 12.5 | 72 | 600 | 5.121 |
| 17 | 15 | 48 | 450 | 5.100 |

Table 2 ANOVA for Response Surface Cubic Model

| Source | Sum of Squares | df | Mean Square | F Value | p-value Prob >F |  |
| --- | --- | --- | --- | --- | --- | --- |
| Model | 7.741125 | 12 | 0.645094 | 6.366E+007 | <0.0001 | significant |
| A-Soybean(g) | 0.994009 | 1 | 0.994009 | 6.366E+007 | <0.0001 |  |
| B-Incubation(h) | 1.183744 | 1 | 1.183744 | 6.366E+007 | <0.0001 |  |
| C-Inoculum(µl) | 0.185761 | 1 | 0.185761 | 6.366E+007 | <0.0001 |  |
| AB | 0.266772 | 1 | 0.266772 | 6.366E+007 | <0.0001 |  |
| AC | 1.153476 | 1 | 1.153476 | 6.366E+007 | <0.0001 |  |
| BC | 0.033856 | 1 | 0.033856 | 6.366E+007 | <0.0001 |  |
| A2 | 0.020265 | 1 | 0.020265 | 6.366E+007 | <0.0001 |  |
| B2 | 0.060253 | 1 | 0.060253 | 6.366E+007 | <0.0001 |  |
| C2 | 1.165505 | 1 | 1.165505 | 6.366E+007 | <0.0001 |  |
| ABC | 0 | 0 |  |  |  |  |
| A2B | 1.177345 | 1 | 1.177345 | 6.366E+007 | <0.0001 |  |
| A2C | 1.487813 | 1 | 1.487813 | 6.366E+007 | <0.0001 |  |
| AB2 | 1.802151 | 1 | 1.802151 | 6.366E+007 | <0.0001 |  |
| AC2 | 0 | 0 |  |  |  |  |
| B2C | 0 | 0 |  |  |  |  |
| BC2 | 0 | 0 |  |  |  |  |
| A3 | 0 | 0 |  |  |  |  |
| B3 | 0 | 0 |  |  |  |  |
| C3 | 0 | 0 |  |  |  |  |
| Pure Error | 0 | 4 | 0 |  |  |  |
| Cor Total | 7.741125 | 16 |  |  |  |  |

The Model F-value of 6.366E+007 implies the model is significant.  There is only a 0.01% chance that a "Model F-Value" this large could occur due to noise. Values of "Prob > F" less than 0.0500 indicate model terms are significant.   In this case A, B, C, AB, AC, BC, A2, B2, C2, A2B, A2C, AB2are significant model.

Table 3   Regression Analysis

| Std. Dev. | 0 | R-Squared | 1 |
| --- | --- | --- | --- |
| Mean | 5.78 | Adj R-Squared | 1 |
| C.V. % | 0 | Pred R-Squared | N/A |
| PRESS | N/A | Adeq Precision | 0 |

Values greater than 0.1000 indicate the model terms are not significant.  
If there are many insignificant model terms (not counting those required to support hierarchy), model reduction may improve your model.

Table 4   Coefficient value of the factor

| Factor | Coefficient Estimate | df | Standard Error | 95% CI Low | 95% CI High | VIF |
| --- | --- | --- | --- | --- | --- | --- |
| Intercept | 5.566 | 1 |  |  |  |  |
| A-Soybean(g) | 0.4985 | 1 |  |  |  | 2 |
| B-Incubation(h) | -0.544 | 1 |  |  |  | 2 |
| C- inoculum(µl) | -0.2155 | 1 |  |  |  | 2 |
| AB | -0.25825 | 1 |  |  |  | 1 |
| AC | -0.537 | 1 |  |  |  | 1 |
| BC | -0.092 | 1 |  |  |  | 1 |
| A2 | 0.069375 | 1 |  |  |  | 1.005882 |
| B2 | -0.11963 | 1 |  |  |  | 1.005882 |
| C2 | 0.526125 | 1 |  |  |  | 1.005882 |
| ABC ALIASED Intercept |
| A2B | 0.76725 | 1 |  |  |  | 2 |
| A2C | 0.8625 | 1 |  |  |  | 2 |
| AB2 | -0.94925 | 1 |  |  |  | 2 |
| AC2ALIASED A, AB2 |  |  |  |
| B2C ALIASED C, A2C |  |  |  |
| BC2ALIASED B, A2B |  |  |  |
| A3 ALIASED A |  |  |  |
| B3ALIASED B |  |  |  |
| C3ALIASED C |  |  |  |

Final equation in terms of terms of coded factors:

Asparaginase (mg/ml) = 5.56 + ( 0.4985 * A) - ( 0.544 * B) - ( 0.2155 * C) - (0.25825 * A * B ) - (0.537 * A * C) - (0.092 * B * C) + (0.069375 * A2) - (0.11963 * B2) + (0.526125 * C2) + (0.76725 * A2* B ) + (0.8625 * A2* C) - (0.94925 * A * B2)

Analysis of process variables by response surface plots

The optimum values of the selected variables were obtained by solving their regression equation and analyzing response surface contour plots. Response Surface plots as a function of two factor at a time maintaining all other factors at a fixed level (zero for instance) are more helpful in understanding both the main and interaction effects of the two factors. The plots can be easily obtained by calculating the data from the model. The values were taken by one factor, where the second varies with constant of a given Y -values. The yield values of the different concentrations of the variable can also be predicted from respective response surface plots.Figure 1 to 6 shows the relative effect of the two variables with protein concentration level. The coordinates of the central point within the highest contour levels in each of these figures corresponded to the optimum concentrations of the respective components.

Figure 1 and 2 show their contour and response surface plot obtained as a function of incubation period vs medium with asparaginase concentration, while all other variables are maintained at zero level (coded units). Figure 3 and 4 show their contour and response surface plot obtained as a function of volume of inoculum vs medium with soybean concentration, while all other variables are maintained at zero level (coded units).Figure 5 and 6 show their contour and response surface plot obtained as a function of Incubation period vs medium with asparaginase concentration, while all other variables are maintained at zero level (coded units).

Optimum values

The protein production was predominantly influenced by the amount of soybean, incubation period and inoculum. The contour plots show the region of the desirability for the production of protein content. The point prediction from the analysis of variable for response surface cubic model for the production of protein concentration (5.566 mg/ml) is 12.5 ml of medium, 450 µl of inoculum, and 60 h of incubation.

Table 5   Predicted value from Box - Behnken design

| Factor | Name | Level | Low Level | High Level | Std. Dev. | Coding |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| A | Soybean(g) | 12.5 | 10 | 15 | 0 | Actual |  |
| B | Incubation(h) | 60 | 48 | 72 | 0 | Actual |  |
| C | Inoculum(µl) | 450 | 300 | 600 | 0 | Actual |  |
| Response | Prediction | SE Mean | 95% CI low | 95% CI high | SE Pred | 95% PI low | 95% PI high |
| Asparaginase(mg/ml) | 5.566 | 0 | 5.566 | 5.566 | 0 | 5.566 | 5.566 |

PI - Prediction interval

CI - Confidence interval

SE Mean – Standard error of the mean.

SE Pred – Standard error of prediction

3.Conclusion

In this work the process parameters the amount of soyabean, incubation time and inoculum were selected and optimized to produce asparaginase. Design Expert from Stat-Ease was used to develop design of experiment. Box Behnken design in Response surface method was used to optimize the process condition.  Thus it has been concluded that the point prediction from the analysis of variable for response surface cubic model for the production of protein concentration (5.566 mg/ml) is 12.5 ml of medium, 450 µl of inoculum, and 60 h of incubation.

4.References:

Cedar,  H. et al., 1968 , “Production of L-Asparaginase II by Escherichia coli” , Journal of Bacteriology ,p. 2043 -2048.

Peterson, R.E. et al., 1969 , “L-Asparaginase Production by Erwinia aroideae” , Applied  Microbiology ,p. 64-67.

Sarhan, M. et al., 2004 , “Production, Isolation, and Purification of L-Asparaginase from Pseudomonas Aeruginosa 50071 Using Solid-state Fermentation” , Journal  of Biochemistry & Molecular Biology, Vol. 37, No. 4, pp. 387-393.

Prakasham, R.S.  et al., 2006 , “L-asparaginase production by isolated Staphylococcus sp. – 6A: design of experiment considering interaction effect for process parameter optimization” , Journal  of Applied  microbiology,ISSN 1364-5072.

Heinemann, B. et al., 1969 ,”Production of Tumor-Inhibitory L-Asparaginase by Submerged Growth of Serratia marcescens” , Applied Microbiology  p. 550 – 554.

Swain, A. et al., 1993 , ”Crystal structure of Escherichia coli L-asparaginase, an enzyme used in cancer therapy” , Proc Natl Acad Sci USA 90, 1474–1478.

Arima, K. et al., 1964 , “Microbial enzyme production in Global Impact of Applied Microbiology” , M.P. Starr (eds.), pp. 279-299, John Willey, New York, USA.

Balcao, V. M. et al.,  2001, “Structural and functional stabilization of L-asparaginase via subunit: Immobilization on to highly activated supports” , Biotechnol. Prog. 17, 537-542.

Castaman, G. et al., 1993 , “Erwinia and E. coli derived L-asparaginase have similar effect on hemostasis. Hematologica” , 78, 57-60.

Datar, R.,  1986 , “Economic of primary separation steps in relation to fermentation and genetics engineering” ,Process Biochem. 21, 19-26.

Derst, C. et al., 1994 ,  “States and functions of tyrosine residues in Escherichia coli asparaginase” ,Eur.J.Biochem.224,533-540.

Distasio, J. A. et al., 1976 , “Purification and characterization of L-asparaginase with antilymphoma activity from Vibroi succinogenes” , J. Biolog. Chem. 251, 6929-6933.

El-Gamal, B. et al., 2001 ,Purification and characterization of chloramphenicol acetyltransferase from Morganella morganii. J. Biochem. Mol. Biol. 34, 415-420.

Gallogher, M. P.et al., 1989 , “Asparaginase drug for treatment of acute lymphoblastic leukemia” , Essays Biochem. 24, 1-40.

Hill, J. et al., 1967 , “Lasparaginase therapy for leukemia and other malignant neoplasm”  JAMA 202, 882.

Keating, M. J. et al., 1993 , “ Lasparaginase and PEG sparaginase past, present and future. Leuk. Lympmoma” , 10, 153-157.

Manna, S. et al., 1995 , “:Purification, characterization and antitumor activity  of L-asparaginase isolated from Pseudomonas stutzeri MB- 405” , Curr Microbiol 30, 291–298.

Asselin, B.L. et al., 1993 , “Comparative  pharmacokinetic studies of three asparaginase preparations” , J Clin Oncol 11, 1780–1786.

Story,  M..D. et al., 1993 , “L-asparaginase kills lymphoma cells by apoptosis” , Cancer Chemoter Pharmacol 32, 129–133.

Prakasham, R.S.et al.,  2005 ,“ Alkaline protease production by an isolated Bacillus circulans under solid state fermentation using agro-industrial waste: process parameter optimization” , Biotechnol Prog 21, 1380–1388.

Prakasham, R.S.et al.,  2005 , “Optimization of alkaline protease production by Bacillus sp. using Taguchi methodology ” ,Appl Biochem Biotechnol 120, 133–144.

Prakasham, R.S.et al.,  2006 ,”Enhancement of acid amylase production by an isolated Aspergillus awamori” , J Appl Microbiol (doi:10.1111/j.1365-2672.2006.03058.x published online).

6/20/2009